## Slide 1: 3GPP TSG-RAN WG4 Meeting #90bis Xi’An, China, 8th – 12th April 2019
Huawei, HiSilicon
Way forward on L1-RSRP test
R4-1903785

## Slide 2: Test case list for accuracy test
Test case number | Test purpose | Remark
1 | L1-RSRP measurement accuracy based on SSB in FR1 | Periodic report is used for verdict.
2 | L1-RSRP measurement accuracy based on SSB in FR2 | UE is assumed to use FFS rough or fine Rx beam. Periodic report is used for verdict.
3 | L1-RSRP measurement accuracy based on CSI-RS in FR1 | Periodic CSI-RS resource set with repetition off. Periodic report is used for verdict.
4 | L1-RSRP measurement accuracy based on CSI-RS in FR2 | Periodic CSI-RS resource set with repetition off; TCI is configured and referring to SSB. UE is assumed to use FFS rough or fine Rx beam. Periodic report is used for verdict.
Note: Test cases should be defined separately for EN-DC and SA. |  | 

## Slide 3: Test case list for delay test
Test case number | Test purpose | Remark
1 | L1-RSRP measurement delay based on SSB in FR1 | One SSB is transmitted through the whole test time; Another SSB is transmitted only in T2. Periodic report after T2 is used for verdict.
2 | L1-RSRP measurement delay based on SSB in FR2 | One SSB is transmitted through the whole test time; Another SSB is transmitted only in T2. UE is assumed to use FFS rough or fine Rx beam. Periodic report after T2 is used for verdict.
3 | L1-RSRP measurement delay based on CSI-RS in FR1 | Aperiodic CSI-RS resource set with repetition off and TCI referring to SSB is transmitted in T2. Aperiodic report after T2 is used for verdict.
4 | L1-RSRP measurement accuracy based on CSI-RS in FR2 | Aperiodic CSI-RS resource set with repetition off and TCI referring to SSB is transmitted in T2. UE is assumed to use FFS rough or fine Rx beam. Aperiodic report after T2 is used for verdict.
Note: Test cases should be defined separately for EN-DC and SA. Note: Test cases should be defined separately for DRX and no-DRX. Note: Test cases should be defined without measurement gap configured. |  | 

## Slide 4: Test setup
If fine Rx beam is assumed for L1-RSRP measurement on SSB or CSI-RS resource set with repetition OFF, RAN4 will not define test for L1-RSRP measurement CSI-RS resource set with repetition ON.
In L1-RSRP measurement test with CSI-RS, TCI pointing to SSB is configured for each CSI-RS resource.
RAN4 to consider the following options for Rx beam assumption in L1-RSRP tests.
  Option 1: UE is assumed to use rough Rx beam
  Option 2: UE is assumed to use fine Rx beam, provided that in the test UE is given enough time to do L3 cell identification before L1-RSRP measurement.
For L1-RSRP delay test, use the same test method as for L3 measurement delay test.