## Slide 1: 3GPP TSG-RAN WG4 Meeting #90Bis Xi‘an, China, 04 – 08 April, 2019
Huawei, …
Way forward on General part of NR BS demodulation performance
R4-1904715

## Slide 2: Background
The following WFs were approved:
  R4-1808022 Way forward on general part for NR BS demodulation requirements, RAN4#87
  R4-1809370 Way forward on general parameters for BS demodulation performance requirements, RAN4#AH1807
  R4-1811726 Way forward on general part of NR BS demodulation performance, RAN4#88
  R4-1813755 Way forward on NR BS demodulation general part, RAN4#88Bis
  R4-1816346 Way forward on NR BS demodulation general part, RAN4#89
  R4-1902438 Way forward on General part of NR BS demodulation performance, RAN4#90

## Slide 3: Manufacture declarations
Use table format to capture the feature declarations
  Reuse Table 4.6-1 in TS 38.141-1 and TS 38.141-2 for the manufacture’s declarations for demodulation conformance test
  Declaration Identifier numbering starts from 100
  Declaration Identifier plus table number are used for one specific manufacture’s declaration in section 8.1.2 of TS 38.141-1 and TS 38.141-2, and in the “Initial conditions” of the requirements for each channel in TS 38.141-2.
    Example: see D.7 in Table 4.6-1

## Slide 4: Test Applicability - 1
Add the following in section “Definition and applicability” for each physical channel performance requirements :
  Which specific test(s) are applicable to BS is based on the test applicability rules defined in subclause 8.1.2
Applicability rule for BS with larger number of Rx antenna
  Capture the agreements made before in specification

## Slide 5: Test Applicability - 2
Encourage company to check the following test applicability for CA in next meeting
Test applicability for CA
  Option 1: Capture the previous agreements in the specification
    For a BS supporting UL carrier aggregation, only the CC combination with the largest aggregated bandwidth per SCS is used for test.
    If there is more than one combination, the CC combination with the largest number of CCs is used for the test.
      Not mixed SCS CA combination to be tested for within a frequency range
      Verify the performance per CC basis
  Option 2: Define CA demodulation requirements for CP-OFDM PUSCH only
    For a BS supporting UL carrier aggregation, only the CC combination with largest aggregated bandwidth is used for the test.
    If there is more than one combination, the CC combination with the largest number of CCs is used for the test.
    For each CC, if more than one SCS is supported, the largest SCS is used for the test.
    Verify the performance at per CC basis.

## Slide 6: OTA test constraints
For FR2, adopt an absolute AWGN level that is 15dB above the RF sensitivity.
  FFS: which sensitivity to be used considering different BS type, different power class, different band, etc.,
  Check if the EIS value can be used
The SNR upper bound for FR2 test is 20dB.
  How to handle the tests with SNR > 20dB
    Option 1: Remove all final requirements with SNR > 20dB
    Option 2: Keep the requirements with SNR>20dB but with a declaration of testability
      Add note in the TS 38.141-2 [3] applicability rules, stating that FR2 minimum performance requirements, which require a SNR value of >[20]dB in TS 38.104 [2], do not need to be tested OTA

## Slide 7: MU and TT
FR1
  Remove the square bracket for MU and TT in CR R4-1902842 for FR1 conducted test
  Add the MU and TT for FR1 OTA test in CR R4-1904744
FR2
  The MU for FR2 demodulation tests equal to the MU for corresponding FR1 demodulation tests as per the discussion in R4-1903489 and agreement in R4-1903490