## Slide 1: WF on high speed related requirements for NR BS demodulation in Rel.15
3GPP TSG-RAN WG4 Meeting #90bis
Xi'an, China, 8th – 12th April 2019
Agenda item: 6.12.2.1 General [NR_newRAT-Perf]
Document for: Approval
R4-1904720
NTT DOCOMO, INC., China Telecom

## Slide 2: Background
In RAN #81, it was approved to discuss HST in TEI15 after December 2018 [1].
The UE and BS demodulation performance requirements under HST scenarios are treated in TEI15 after December 2018.
In RAN #82, performance requirements for high speed train was captured as one of the remaining open issues in SR [2].
In RAN4 #90, WF was approved [3].
In RAN4 #90bis, NR BS performance requirements for high speed were discussed based on contributions [4-9].

## Slide 3: Overview
Release to define NR BS HST requirements
  Option 1: Release 15
  Option 2: Release 16 with starting point of 350km/h on the same Band 1 as LTE
  One of the above options will be decided based on the outcome of the evaluation.
The performance requirements for HST are optional, and the applicability depends on the declaration.
Assumptions for the following HST evaluations are for NR Rel-15 HST for RAN4#91 meeting. Bases on the evaluation results, companies can share their views on the HST requirements definition.

## Slide 4: For evaluation on PUSCH for HST
UE speed
  300km/h
Carrier frequency (Band)
  15kHz SCS
    Band n1 (2.1GHz)
  30kHz SCS
    Band n77 (3.6GHz)
Maximum Doppler shift
  15kHz SCS
    1150Hz
  30kHz SCS
    Option 1: 2000Hz
    Option 2: 1150Hz
Channel model
  AWGN (Single tap HST)
BS-Railway track distance (Dmin) and Initial distance of the train from BS (Ds/2):
  Same as LTE HST scenario 3 for tunnel

## Slide 5: For evaluation on PUSCH for HST
Antenna configuration
  1x2
DMRS configuration
  Baseline: DMRS 1+1, the position of FL DMRS l0 = 3 for both 15kHz and 30kHz SCS
  DMRS 1+1+1 for 30kHz SCS is welcome to provide evaluation results
Time domain resource allocation type
  Type A
Transform precoding
  Option 1: Both enable and disable
  Option 2: disable
MCS index
  MCS 2
SCS and BW
  Transform precoding disable:
    15kHz: 10MHz;
    30kHz: 40MHz;
  Transform precoding enable:
    15kHz: 5MHz;
    30kHz: 10MHz.
Testing metric
  SNR @70% of maximum throughput

## Slide 6: For evaluation on PUSCH for HST
Parameter | value | 
 | FR1 | FR1
Transform precoding | Disabled | Enabled
Number of Tx | 1 | 1
Number of Rx | 2 | 2
Number of layers | 1 | 1
Transmission scheme | Identity matrix (TPMI index 0) | Identity matrix (TPMI index 0)
DMRS type | type 1 | type 1
Number of DMRS symbols | Baseline: DMRS 1+1, the position of FL DMRS l0= 3 for both 15kHz and 30kHz SCS DMRS 1+1+1 for 30kHz SCS is welcome to provide evaluation results | Baseline: DMRS 1+1, the position of FL DMRS l0=3 for both 15kHz and 30kHz SCS DMRS 1+1+1 for 30kHz SCS is welcome to provide evaluation results
symbols length | 14 | 14
start symbol index | 0 | 0
Time domain resource allocation type | type A | type A
Frequency domain resource | Full applicable test bandwidth | 15kHz: 25 PRB; 30kHz: 24 PRB (middle of test BW)
MCS index | 2 | 2
Carrier frequency (GHz) | 15kHz SCS: 2.1GHz 30kHz SCS: 2.1GHz or 3.6GHz | 15kHz SCS: 2.1GHz 30kHz SCS: 2.1GHz or 3.6GHz
Propagation condition | Scenario 3 with AWGN | Scenario 3 with AWGN
SCS and BW | 15kHz: 10MHz 30kHz: 40MHz | 15kHz: 5MHz; 30kHz: 10MHz
PTRS | Not configured | Not configured
Timing offset | 0 | 0
Frequency offset | 0 | 0
Code block group, Frequency hopping, Limited buffer rate matching | Disabled | Disabled
Number of HARQ transmissions | 4 | 4
Testing metric | SNR @70% of maximum throughput | SNR @70% of maximum throughput
Simulation assumption

## Slide 7: For evaluation on PUSCH for HST
Simulation assumption
Parameter | Value
 | Scenario 3
 | 300 m
 | 2 m
 | 300 km/h
 | For 15kHz SCS: - 1150Hz For 30kHz SCS: - Option 1: 2000Hz - Option 2: 1150Hz

## Slide 8: For evaluation on PRACH restricted set
PRACH performance requirements for HST
  Baseline: Restricted set type B
  Restricted set type A is welcome to provide evaluation results
Burst format
  Burst format 0
Channel model and frequency offset
  Reuse parameters of requirements for burst format 0 from LTE
    AWGN
      Baseline: AWGN with 1875 Hz frequency offset for restricted set type B
        FFS: AWGN with 2000 Hz frequency offset for restricted set type B
      AWGN with 1340 Hz frequency offset for restricted set type A is welcome to provide evaluation results
    TDLC300-100
      Base line: TDLC300-100 with 400Hz frequency offset for restricted set type B
      TDLC300-100 with 400Hz frequency offset for restricted set type A is welcome to provide evaluation results

## Slide 9: Way forward
Companies are encourage to evaluate PUSCH and PRACH performance under HST for RAN4#91.
If no technical issues are identified and no concern is raised on the evaluation assumptions, Draft CRs implementing framework of PUSCH for HST and PRACH for restricted set type A or/and B, for TS 38.104, TS 38.141-1 and TS 38.141-2, might be provided in RAN4 #91.

## Slide 10: Reference
[1] RP-182149, “Way forward on RAN4 work for Core and Perf. part for NR”, RAN4 Chairman, RAN #81
[2] RP-182805, “Status Report of WI on New Radio Access Technology”, NTT DOCOMO, INC., RAN #82
[3] R4-1902442, “WF on high speed related requirements for NR BS demodulation in Rel.15”, NTT DOCOMO, INC., RAN4#90
[4] R4-1903570, “Motivation and discussion priority for NR high speed in Rel.15”, NTT DOCOMO, INC., RAN4#90bis
[5] R4-1903571, “NR PUSCH for high speed in Rel.15”, NTT DOCOMO, INC., RAN4#90bis
[6] R4-1903364, “Remaining issues on performance requirements for NR PUSCH in Rel-15”, Samsung, RAN4#90bis
[7] R4-1904034, “HST for NR BS demod in Rel-15”, Ericsson, RAN4#90bis
[8] R4-1904229, “Discuss on HST demodulation requirements for NR Rel-15 BS”, Huawei, HiSilicon, RAN4#90bis
[9] R4-1903572, “NR PRACH for high speed in Rel.15”, NTT DOCOMO, INC., RAN4#90bis