## Slide 1: Way forward on SDR requirements
NTT DOCOMO, …
3GPP TSG-RAN WG4 Meeting #90bis
Xi’an, China, 8 April – 12 April 2018 Agenda Item: 6.12.1.2
R4-1904755

## Slide 2: Upper bound/Practical MCS for FR1
      Previous agreement
UE capability index |  |  |  |  | 
1 | 1 | 8 | 1 | 26 | [26]
2 | 1 | 8 | 0.8 | 21 | 
3 | 1 | 8 | 0.75 | 20 | 
4 | 1 | 8 | 0.4 | 11 | 
5 | 1 | 6 | 1 | 27 | [27]
6 | 1 | 6 | 0.8 | 23 | 
7 | 1 | 6 | 0.75 | 22 | 
8 | 1 | 6 | 0.4 | 14 | 
9 | 1 | 4 | 1 | 16 | [16]
10 | 1 | 4 | 0.8 | 16 | 
11 | 1 | 4 | 0.75 | 16 | 
12 | 1 | 4 | 0.4 | 10 | 
13 | 1 | 2 | 1 | 9 | [9]
14 | 1 | 2 | 0.8 | 9 | 
15 | 1 | 2 | 0.75 | 9 | 
16 | 1 | 2 | 0.4 | 4 | 
17 | 2 | 8 | 1 | 26 | [26]
18 | 2 | 8 | 0.8 | 21 | 
19 | 2 | 8 | 0.75 | 20 | 
20 | 2 | 8 | 0.4 | 11 | 
21 | 2 | 6 | 1 | 27 | [27]
22 | 2 | 6 | 0.8 | 23 | 
23 | 2 | 6 | 0.75 | 22 | 
24 | 2 | 6 | 0.4 | 14 | 
25 | 2 | 4 | 1 | 16 | [16]
26 | 2 | 4 | 0.8 | 16 | 
27 | 2 | 4 | 0.75 | 16 | 
28 | 2 | 4 | 0.4 | 10 | 
UE capability index |  |  |  |  | 
29 | 2 | 2 | 1 | 9 | [9]
30 | 2 | 2 | 0.8 | 9 | 
31 | 2 | 2 | 0.75 | 9 | 
32 | 2 | 2 | 0.4 | 4 | 
33 | 4 | 8 | 1 | 27 | [26]
34 | 4 | 8 | 0.8 | 23 | 
35 | 4 | 8 | 0.75 | 22 | 
36 | 4 | 8 | 0.4 | 12 | 
37 | 4 | 6 | 1 | 28 | [27]
38 | 4 | 6 | 0.8 | 24 | 
39 | 4 | 6 | 0.75 | 23 | 
40 | 4 | 6 | 0.4 | 14 | 
41 | 4 | 4 | 1 | 16 | [16]
42 | 4 | 4 | 0.8 | 16 | 
43 | 4 | 4 | 0.75 | 16 | 
44 | 4 | 4 | 0.4 | 11 | 
45 | 4 | 2 | 1 | 9 | [9]
46 | 4 | 2 | 0.8 | 9 | 
47 | 4 | 2 | 0.75 | 9 | 
48 | 4 | 2 | 0.4 | 5 | 

## Slide 3: Upper bound/Practical MCS for FR1
      Issue 1: Upper bound MCS
        Option 1: Keep previous agreement
        Option 2: Change some upper bound MCSs
      Issue 2: Practical MCS
        Proposal: Remove [] from previous agreement
UE capability index |  |  |  | 
12 | 1 | 4 | 0.4 | 14
16 | 1 | 2 | 0.4 | 9
28 | 2 | 4 | 0.4 | 14
32 | 2 | 2 | 0.4 | 9
44 | 4 | 4 | 0.4 | 14
48 | 4 | 2 | 0.4 | 9

## Slide 4: Methodology for MCS determination for FR2
Previous agreement
  Option 1: Keep the exiting procedure (Baseline)
    Use general procedure to select CA bandwidth for testing
    Derive for each CC based on UE capability by the previous slide (j is CC index)
    Identify testable SNR value for particular test configuration based on test equipment characteristics
    Use “SNR to MCS+Rank” table to find for each CC (Detail of “SNR to MCS+Rank” table is FFS)
    Conduct SDR test with for each CC
  Option 2: New procedure proposed in R4-1900048
  Further evaluation and comparison among these two options in next RAN4 meeting, if no difference for test channel bandwidth combinations among Op1 and Op2 ; then using option1

## Slide 5: Methodology for MCS determination for FR2
Proposal:
  Use procedure proposed in R4-1900048 (Option 2)
    Step 1: For all supported CA configurations and set of per component carrier (CC) UE capabilities among all supported UE capabilities:
      Use the table defining the MCS to determine the MCS (=MCS1) achieving the largest data rate [TS 38.306 [14, Section 4.1.2]] based on UE capabilities.
      Use the table defining the mapping between MCS and SNR required to achieve that MCS to determine the largest MCS (=MCS2) requiring SNR below test equipment maximum achievable SNR for each CC in that CA configuration.
      Compute the aggregate throughput for CA configuration using the MCS = min(MCS1,MCS2) for each CC in CA bandwidth combination.
    Step 2: Choose the CA bandwidth combination among all supported CA configurations that achieves maximum aggregate throughput in step 1 among all UE capabilities.
      Set of per CC UE capabilities includes channel bandwidth, subcarrier spacing, number of PDSCH MIMO layers, modulation format and scaling factor [TS 38.306 [14, Section 4.1.2]].
      When there are multiple sets of CA bandwidth combinations and UE capabilities (channel bandwidth, subcarrier spacing, number of MIMO layer, modulation format, scaling factor) with same aggregate throughput, select TBD smallest CA bandwidth
    Step 3: For each CC in chosen CA bandwidth combination, use determined MCS for each CC in step 1 for that CA configuration based on test parameters and indicated UE capabilities.
  To define methodology for testable baseband SNR range in TR 38.810

## Slide 6: Upper bound MCS (MCS1) / practical MCS (MCS2) for FR2
Previous agreement:
UE capability index |  |  |  | 
1 | 1 | 6 | 1 | 27
2 | 1 | 6 | 0.8 | 23
3 | 1 | 6 | 0.75 | 22
4 | 1 | 6 | 0.4 | 14
5 | 1 | 4 | 1 | 16
6 | 1 | 4 | 0.8 | 16
7 | 1 | 4 | 0.75 | 16
8 | 1 | 4 | 0.4 | 10
9 | 1 | 2 | 1 | 9
10 | 1 | 2 | 0.8 | 9
11 | 1 | 2 | 0.75 | 9
12 | 1 | 2 | 0.4 | 4
13 | 2 | 6 | 1 | 27
14 | 2 | 6 | 0.8 | 23
15 | 2 | 6 | 0.75 | 22
16 | 2 | 6 | 0.4 | 14
17 | 2 | 4 | 1 | 16
18 | 2 | 4 | 0.8 | 16
19 | 2 | 4 | 0.75 | 16
20 | 2 | 4 | 0.4 | 10
21 | 2 | 2 | 1 | 9
22 | 2 | 2 | 0.8 | 9
23 | 2 | 2 | 0.75 | 9
24 | 2 | 2 | 0.4 | 4

## Slide 7: Upper bound MCS (MCS1) / practical MCS (MCS2) for FR2
Proposal:
  Mapping from SNR to MCS2
  Note: The SNR value is based on the impairment results in R4-1902880
<= Testable baseband SNR (dB) | MCS
[9.0] | MCS13
[9.9] | MCS14
[11.0] | MCS15
[11.6] | MCS16
[13.1] | MCS17
[13.6] | MCS18
[14.6] | MCS19
[15.5] | MCS20
[16.4] | MCS21
[17.6] | MCS22
[18.6] | MCS23
[19.7] | MCS24
[21.2] | MCS25
[22.3] | MCS26
[23.5] | MCS27
For Rank2
For Rank1
<= Testable baseband SNR (dB) | MCS
[6.1] | MCS13
[7.1] | MCS14
[8.1] | MCS15
[8.7] | MCS16
[10.0] | MCS17
[10.6] | MCS18
[11.6] | MCS19
[12.5] | MCS20
[13.4] | MCS21
[14.7] | MCS22
[15.5] | MCS23
[16.8] | MCS24
[18.1] | MCS25
[19.1] | MCS26
[20.3] | MCS27

## Slide 8: SDR methodology for EN-DC within FR1
Previous agreement:
  Proposed methodology in R4-1900364
    Step 1: Select one EN-DC bandwidth combination among all supported EN-DC configurations and set of per component carrier (CC) UE capabilities among all supported UE capabilities that provides the largest data rate [TS 38.306 [14, Section 4.1.2]].
      Set of per NR CC UE capabilities includes channel bandwidth, subcarrier spacing, number of PDSCH MIMO layers, modulation format and scaling factor [TS 38.306 [14, Section 4.1.2]].
      Set of per EUTRA CC UE capabilities includes channel bandwidth, number of PDSCH MIMO layers and modulation format [TS 38.306 [14, Section 4.1.2]].
    Step 2: For each NR CC in EN-DC bandwidth combination, use MCSs from FR1 or FR2 SA SDR requirements depending on EN-DC scenario. For each EUTRA CC in EN-DC bandwidth combination, reuse LTE SDR FRCs [TS 36.101, Sections 8.7].
  Further evaluated above methodology in next RAN4 meeting
  Other options not excluded
Proposal:
  Use proposed methodology from the previous meeting in (R4-1900364) as baseline

## Slide 9: SDR methodology for EN-DC including FR2
Previous agreement:
  Same as for SDR methodology for EN-DC within FR1
Current options:
  Option 1 (Intel):
    Step 1: Calculate data rate (DataRateFR2) for FR2 CCs for all supported EN-DC configurations and set of per component carrier (CC) UE capabilities among all supported UE capabilities:
      Step 1-1: Select MCSupperbound which allows to achieve the largest data rate [TS 38.306 [14, Section 4.1.2]] based on UE capabilities.
      Step 1-2: Identify testable SNR value for particular test configuration based on test equipment characteristics
      Step 1-3: Use “SNR to MCS+Rank” table to find MCSpractical for each FR2 CC in EN-DC bandwidth combination
      Step 1-4: Calculate data rate using the MCS = min(MCSupperbound, MCSpractical) for each FR2 CC in EN-DC bandwidth combination
    Step 2: Calculate data rate (DataRateEUTRA) for EUTRA CCs for all supported EN-DC configurations and set of per component carrier (CC) UE capabilities among all supported UE capabilities using equation from [TS 38.306 [14, Section 4.1.2]]
      Set of per EUTRA CC UE capabilities includes channel bandwidth, number of PDSCH MIMO layers and modulation format [TS 38.306 [14, Section 4.1.2]].

## Slide 10: SDR methodology for EN-DC including FR2
Current options(Cont.):
  Option 1 (Intel):
    Step 3: Select one EN-DC bandwidth combination among all supported EN-DC configurations and set of per component carrier (CC) UE capabilities among all supported UE capabilities that provides the largest total data rate (DataRateEUTRA+ DataRateFR2)
    Step 4: For each NR FR2 CC in EN-DC bandwidth combination, use MCSs from Step 1-4 for selected EN-DC bandwidth combination.
Proposal:
  Taking Option 1 as baseline

## Slide 11: SDR methodology for EN-DC including FR1 and FR2
Previous agreement:
  Same as for SDR methodology for EN-DC within FR1
Current options:
  Option 1 (Intel):
    Step 1: Calculate data rate (DataRateFR2) for FR2 CCs for all supported EN-DC configurations and set of per component carrier (CC) UE capabilities among all supported UE capabilities:
      Step 1-1: Select MCSupperbound which allows to achieve the largest data rate [TS 38.306 [14, Section 4.1.2]] based on UE capabilities.
      Step 1-2: Identify testable SNR value for particular test configuration based on test equipment characteristics
      Step 1-3: Use “SNR to MCS+Rank” table to find MCSpractical for each FR2 CC in EN-DC bandwidth combination
      Step 1-4: Calculate data rate using the MCS = min(MCSupperbound, MCSpractical) for each FR2 CC in EN-DC bandwidth combination
    Step 2: Calculate data rate (DataRateFR1 + DataRateEUTRA) for FR1 NR and EUTRA CCs for all supported EN-DC configurations and set of per component carrier (CC) UE capabilities among all supported UE capabilities using equation from [TS 38.306 [14, Section 4.1.2]]
      Set of per NR CC UE capabilities includes channel bandwidth, subcarrier spacing, number of PDSCH MIMO layers, modulation format and scaling factor [TS 38.306 [14, Section 4.1.2]].
      Set of per EUTRA CC UE capabilities includes channel bandwidth, number of PDSCH MIMO layers and modulation format [TS 38.306 [14, Section 4.1.2]].

## Slide 12: SDR methodology for EN-DC including FR1 and FR2
Current options(Cont.):
  Option 1 (Intel):
    SStep 3: Select one EN-DC bandwidth combination among all supported EN-DC configurations and set of per component carrier (CC) UE capabilities among all supported UE capabilities that provides the largest total data rate (DataRateFR1 + DataRateEUTRA+ DataRateFR2).
    Step 4: For each NR FR2 CC in EN-DC bandwidth combination, use MCSs from Step 1-4 for selected EN-DC bandwidth combination.
Proposal
  Taking Option 1 as baseline

## Slide 13: Others
Issue: HARQ process for scenarios with 60 kHz SCS with TDD DL-UL patter DDSU
  Proposal: Configure maximum number of HARQ process equal to 10