## Slide 1
3GPP TSG-RAN WG4 Meeting #90BIS
Xian, China, 8th – 12th April, 2019
Agenda item: 8.4.1
Document for : Approval
WF on coexistence scenarios for NR V2X
R4-1905098
Qualcomm, LG Electronics

## Slide 2: Scope for RAN4 work
In device coexistence
  (LTE SL and NR SL operation at ITS spectrum) without (LTE or NR Uu in another band) on the same device
    TDM operation in 5.9 GHz ITS spectrum.
      Based on approved WID, no self interference issues are identified for the IDC
        Switching times for TDM operation needs to be studied
    FDM operation
      Clarification on the sentence as below
      FDM-based solutions with static power allocation as per the study outcome
        This will not consider the case where LTE and NR sidelinks are in the same frequency band.
      The inter-band FDM operation includes a band for LTE SL (at 5.9GHz) and a band for NR sidelink operation. RAN4 defers the coexistence discussion to May meeting. Some feedback from 5GAA and operator expected. Final decision on band is discussed in RAN4.
  * There is no self interference problem in ITS spectrum

## Slide 3: Scope for RAN4 work
In-device Inter-band con-current operation
  (LTE SL and NR SL operation at ITS spectrum) with (LTE or NR Uu in another band) on the same device
    Both TDM/FDM operation will be studied based on operator request
    RAN4 defers the coexistence discussion to May meeting. Final decision on band combinations are discussed in RAN4.

## Slide 4: Scope for RAN4 work
UE-to-UE coexistence
  1) 5.9 GHz ITS spectrum
    Aggressor-to-Victim UE coexistence
      NR SL-to-DSRC, NR SL-to-LTE SL
      DSRC-to-NR SL, LTE SL-to-NR SL
    In LTE SL WI, RAN4 already analyze the DSRC impact
    For the new unlicensed ITS spectrum, RAN4 will discuss when it is available
  2) Licensed spectrum
    Aggressor-to-Victim UE coexistence
      NR SL-to-NR/LTE Uu
      LTE/NR Uu-to-NR SL
    RAN4 need to UE-to-UE coexistence parameters and assumptions for these scenarios.
    However, RAN4 defer the coexistence discussion at May meeting. Some feedback from 5GAA and operator expected. Final decision on bands are discussed in RAN4.

## Slide 5: Objective
Define adjacent channel coexistence evaluations scenarios and parameters at 5.9GHz ITS spectrum to support to NR sidelink V2X operation.
5.9GHz SL adjacent channel operation
  Adjacent channel coexistence evaluation with DSRC/802.11p or LTE V2X in ITS spectrum
  Consider following interference scenarios
    REF : DSRC UE-to-DSRC UE
      Case1: NR V2X UE-to-DSRC UE:
      Case2: DSRC UE-to-NR V2X UE:
    REF: LTE V2X UE-to-LTE V2X UE
      Assume all devices will support both LTE V2X and NR V2X
        Assume from a device perspective Tx between LTE V2X and NR V2X is TDM while rx of LTE V2X and NR V2X is simultaneous (as reflected in figures in slide 7)
      Case3: NR V2X UE-to-LTE V2X UE :
      Case4: LTE V2X UE-to-NR V2X UE:

## Slide 6: Coexistence Scenarios at 5.9GHz
1) Case 1 (Aggressor-Victim)
  NR V2X UE-to-DSRC UE
2) Case 2 (Aggressor-Victim)
  DSRC UE-to-NR V2X UE
3) Case 3 (Aggressor-Victim)
  NR V2X UE-to-LTE V2X UE
4) Case 4 (Aggressor-Victim)
  LTE V2X UE-to-NR V2X UE
  Consider NR/LTE V2X SL operation at 5.9GHz
    No LBT mechanism for LTE V2X UE & NR V2X UE
    Max. output power for DSRC, NR and LTE V2X UE: 23dBm or 33dBm
DSRC
NR V2X
f
LTE V2X
NR V2X
f
NR V2X
DSRC
f
NR V2X
LTE V2X
f

## Slide 7: Evaluation methodology
Static simulations
  Monte-carlo based static simulations.
Evaluation metric
  PRR degradation due to adjacent channel interferer(s) for both DSRC and NR/LTE V2X system at 5.9GHz
  FFS Link level simulation mapping model for NR V2X UE.

## Slide 8: References
[1] RP-190766, “New WID on 5G V2X with NR sidelink”, LG Electronics, Huawei
[2] R4-1903031, "Initial coexistence simulation assumptions of NR V2X," LG Electronics France