## Slide 1: WF on General aspects for 7 – 24 GHz SI
Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting#90bis
Xi’an, China, 8th April– 12th April, 2019
R4-1905198

## Slide 2: Introduction
During RAN4#90bis contributions on 7-24 GHz SI were submitted in [1-27].
General, UE-, and BS-related aspects were discussed. Based on discussion, multiple open items were identified.
This WF captures items which are general for the 7-24 GHz SI and are applicable to UE and BS.
Actions and proposals are provided for approval in the following areas:
  FR1/FR2 differentiators study
  Selection of frequency sub-ranges
  Deployment scenarios

## Slide 3: FR1/FR2 differentiators study
One of the 7-24GHz SID objectives is to:
  “Study how to define a boundary frequency and/or boundary conditions, including extending FR1 upwards and/or FR2 downwards in frequency, or alternatively introduce new frequency range(s)… ”
During RAN4#90bis discussion it was identified that for the purpose of SI progress, it is essential to conclude what is meant by “FR1/FR2 frequency ranges extension” as this term was used in multiple contributions and understanding of it’s consequences was varying among companies.
For that purpose, multiple NR technology items which differ among FR1 and FR2 were identified as valid inputs to be considered during further investigation on potential “FR1/FR2 extension” consequences:
  Conducted vs. OTA interface,
  Set of SCS and CHBW supported,
  Broadcast channels coverage (beam-sweeping vs. static),
  Set of supported modulation and coding schemes,
  Duplex mode,
  Single/multi-band support,
  Consideration of deployment scenarios,
  Consideration of UE types and usage conditions,
  For BS only:
    BS types,
    Presence or lack of certain BS requirements,
    Concept for BS receiver requirements,
    Requirement values common in some cases across an FR.
  This list may not be exhaustive; companies are encouraged to indicate next meeting whether there are more aspects to add
Action: Based on the above list, companies are encouraged to provide further analyses of “FR1/FR2 extension” understanding and its potential impact analysis on RAN4 specifications for UE and/or BS.

## Slide 4: Selection of example ranges
Multiple contributions were submitted to RAN4#90bis on the selection of 7-24GHz example ranges for the purpose of the RF technology and RF requirements analyses. The following figure presents summary of selected inputs from companies:
Proposal: Consider the following 7-24GHz example ranges frequencies for the purpose of the RF technology feasibility analyses
  1. example range 1: 7.125 – [10-13] GHz, example frequency: 10GHz
  2. example range 2: [10-13] – [16-18] GHz, example frequency: 15GHz
  3. example range 3: [16-18] – 24.25 GHz, example frequency: 20GHz
Action: Companies are encouraged to provide inputs on the RF technology evaluations for both UE and BS, considering the above example ranges, as well as proposals for the frequency sub-rangesbreak-points.
NOTE 1: the above example ranges will beare selected only for purpose of RF technology analyses during SI and shall not be confused with potential new Frequency Ranges and band plan which could be defined by RAN4 for NR in future.
NOTE 2: the above example ranges are not fixed and could be modified based on RF technology findings during the SI phase.
NOTE 3: in case outcomes of the RF/requirement analyses will be found as sufficiently similar across adjacent example ranges, RAN4 will consider merging them towards SI conclusion on FR1/FR2 extension and/or new FR introduction.

## Slide 5: 7-24GHz deployment scenarios
During RAN4#90bis meeting, selected aspects of the deployment scenarios were raised, e.g. consideration of 256QAM in DL, CA operation, users mobility, ISD, BS power, sectorization, beamforming, etc.
The deployment scenario may end up very dependent on the spectrum environment in which eventual bands end up; this cannot be known but assumptions on neighbour systems should be documented
According to the agreed work-plan, the discussion on the deployment scenarios was expected to be initiated during next RAN4#91 meeting.
Action: Companies are encouraged to provide further inputs on the potential 7-24 GHz deployment scenarios.

## Slide 6: References
[1] R4-1903487 7-24 GHz Filter Aspects, Ericsson
[2] R4-1903988 Overview on system parameters for 7-24GHz, ZTE Corporation
[3] R4-1903328 TR 38.820: updated TR skeleton for 7-24GHz SI, Huawei
[4] R4-1903058 Views on FR1 boundary frequency in the 7-24 GHz frequency range, Apple Inc.
[5] R4-1903455 TP to TR 38.820: Addition of example frequencies in subclause 6.2, Ericsson
[6] R4-1903994 On performance of existing RF connector and probe technology, LG Electronics Finland
[7] R4-1903513 7.125 - 24.25GHz Frequency Range from a UE Perspective, Skyworks Solutions Inc.
[8] R4-1904481 Discussion On 7-24GHz UE RF requirement, Huawei, HiSilicon
[9] R4-1903329 EMC emission requirements for 7-24GHz range, Huawei
[10] R4-1903342 EMC immunity requirements for 7-24GHz range, Huawei
[11] R4-1903343 BS RF general aspects for 7-24GHz SI, Huawei
[12] R4-1903564 on EMC requirements for 7-24GHz, ZTE Corporation
[13] R4-1903464 7-24 GHz PA considerations and dependencies, Ericsson
[14] R4-1903465 TP to TR: 7-24 GHz power amplifier trends, Ericsson
[15] R4-1903466 TP to TR: 7-24 GHz Phase Noise trends, Ericsson
[16] R4-1903484 On BS types for the 7-24GHz range, Ericsson
[17] R4-1903485 TP to TR 38.820: Impact to BS transmitter requirements, Ericsson
[18] R4-1903486 TP to TR 38.820: Impact to BS receiver requirements, Ericsson
[19] R4-1903565 on out-of-band blocking test for 7-24GHz, ZTE Corporation
[20] R4-1903990 Overview on TX requirement for 7-24GHz, ZTE Corporation
[21] R4-1903991 Overview on RX requirement for 7-24GHz, ZTE Corporation
[22] R4-1904070 7-24 GHz Receiver Aspects, Ericsson
[23] R4-1904127 7-24GHz - discuss implications of FR1 and FR2 architectures, Huawei
[24] R4-1904128 7-24GHz - discuss ACIR requirements and potential frequency ranges of interest, Huawei
[25] R4-1904129 7-24GHz - discuss TX IMD and co-location requirements, Huawei
[26] R4-1904130 [7-24GHz] discussion on specification structure (BS), Huawei
[27] R4-1904319 BS RF technology aspects for 7-24 GHz, Nokia, Nokia Shanghai Bell
[28] R4-1902509 Work plan for the 7-24 GHz study item, Huawei

## Slide 7: 7-24GHz SI work-plan for RAN4#91
3GPP meeting | Dates | Location | Proposed workplan
3GPP RAN4 #91 | 13 - 17 May 2019 | Reno, Nevada | System parameters: continue discussion RF technology aspects: continue discussion Deployment scenarios: trigger discussion on possible scenarios, considering technology capabilities BS specifications and requirements: continue discussion UE specifications and requirements: continue discussion BS RF architecture: continue discussion on requirements classification UE RF architecture: continue discussion on requirements classification EMC: conclusion on requirements impact
Extract from [28]: