## Slide 1: WF on coexistence of NB-IoT with NR
Huawei, HiSilicon, Ericsson, CHTTL, SGS Wireless, Nokia, ZTE, Dish, T-Mobile USA
3GPP TSG-RAN WG4 Meeting#90bis
Xi’an, China, 8th April– 12th April, 2019
R4-1905203

## Slide 2: Agreements
  WF on system scenarios
    To clarify the current definition of NB-IoT operation modes when NB-IoT is deployed within NR channel bandwidth, including when spectrum is refarmed from E-UTRA to NR
        whether NB-IoT in-band or guard band operation without a hosting E-UTRA carrier would have backward compatibility impact on Rel’13/14/15 NB-IoT UE, which may expect the presence of a hosting E-UTRA carrier, especially for NB-IoT in-band operation
  Agreement on NB-IoT standalone operating
    There is no issue for NB-IoT standalone coexistence with NR and no further study is needed.
    simulation results will be added in TR annex
    Nokia/Huawei will provide TP in next meeting
  WF on power boosting
    Further investigate if currently specified power boosting could be supported, including when NB-IoT is located at NR edge positions for any channel bandwidth.
    At least 3dB (currently specified RE power dynamic range) power boosting should be feasible.
  Agreement on channel raster
    for NR bands with 100 kHz channel raster and 15 kHz SCS, subcarrier and PRB alignment can be achieved for NB-IoT operating in NR in-band.
    for NR bands with 15 kHz channel raster and 15 kHz SCS, subcarrier and PRB alignment can be achieved for NB-IoT operating in NR in-band.
    Ericsson/ZTE will provide TP in next meeting
  Agreement on mixed numerology
    no requirement is defined for mixed numerology between NR and NB-IoT similar as NR mixed numerology itself.
    ZTE will provide TP in next meeting
  Agreement on bands
    NB-IoT shall be supported on all NR bands refarmed from E-UTRA bands supporting NB-IoT.

## Slide 3: FFS
NB-IoT operating in NR guard band
TAGs misalignment
TDD configuration for sync between NR and NB-IoT
Specification and conformance impact

## Slide 4: References
[1] R4-1903112 System level simulation results for coexistence study between R15 NR and R13/R14/R15 NB-IoT standalone operation Nokia, Nokia Shanghai Bell
[2] R4-1903113 System level simulation results for coexistence study between R15 NR and R13/R14/R15 NB-IoT standalone operation (with NR channel model) Nokia, Nokia Shanghai Bell
[3] R4-1903114 Consideration on NB-IoT operation within NR channel bandwidth Nokia, Nokia Shanghai Bell
[4] R4-1903842 Discussion on NR and NB-IoT coexistence ZTE Corporation
[5] R4-1903849 NB-IoT standalone operating Huawei, HiSilicon
[6] R4-1903850 NB-IoT operating in NR guard band Huawei, HiSilicon
[7] R4-1903851 System scenarios of NB-IoT coexistence with NR Huawei, HiSilicon
[8] R4-1903852 Channel raster, subcarrier and PRB alignment Huawei, HiSilicon
[9] R4-1903853 Power boosting for coexistence of NB-IoT with NR Huawei, HiSilicon
[10] R4-1904017 NB-IoT - NR coexistence : SCS based channel raster Ericsson
[11] R4-1904018 NB-IoT - NR coexistence : BS RF topics Ericsson
[12] R4-1904019 TP to the new TR related to NB-IoT - NR coexistence – channel raster Ericsson