## Slide 1: WF on RefSens exceptions due to UL harmonic for SA CA and EN-DC
vivo, […],
3GPP TSG-RAN WG4#91 Meeting R4-1905509
Reno, US, 13th-17th May, 2019

## Slide 2: Background
Inconsistencies found when introducing Reference sensitivity exceptions due to UL harmonic interference into NR based on LTE
Background information summarized in [R4-1905506] and a list of tentative proposals were provided to correct current configurations and facilitate future work.
It was further discovered that aggressor reference sensitivity should also be satisfied simultaneous to victim carrier for CA Refersen test.

## Slide 3: Way Forward (1)
Proposal 1: For direct overlap, the UL allocation should be set to make the UL harmonics just fully cover the victim measurement bandwidth. If full overlap cannot achieved for large measurement bandwidth, the maximum degree of UL allocation possible should be utilized.

## Slide 4: Way Forward (2)
Proposal 2: Unless stated otherwise, UL resource blocks shall be centred within the transmission bandwidth configuration for the channel bandwidth.
  (Note: This configuration is defined for combinations with direct overlap. For combinations with no direct overlap, the uplink configuration and allocation would be defined case by case.)

## Slide 5: Way Forward (3)
Proposal 3(Updated): To ensure simultaneous DL reference sensitivity for the aggressor and victim, the UL RB allocation in aggressor carrier should be further restricted in case the UL RB number deduced by previous proposals exceed what had been restricted for single carrier reference sensitivity test.
  E.g. For 38.101-1 keeping current note :
    NOTE 2: The UL configuration applies regardless of the channel bandwidth of the low band unless the UL resource blocks exceed that specified in Table 7.3.2-3 for the uplink bandwidth in which case the allocation according to Table 7.3.2-3 applies.

## Slide 6: Way Forward (4)
Proposal 4(Updated): For 2nd order harmonics, clarified that lower MSD (MSD B) region were only defined for the case which channel bandwidth is no larger than 20MHz.

## Slide 7: Reference
[1] R4-1905506, Discussion on MSD requirements for UL harmonics, RAN4#91