## Slide 1: 3GPP TSG-RAN WG4 Meeting #91 Reno, USA, 13th – 17th May 2019
Huawei, HiSilicon
Way forward on R16 enhancement for NB-IoT RRM
R4-1905610

## Slide 2: Group WUS
RAN4 shall wait for further RAN1 progress on release 16 group WUS design to decide whether release 15 WUS requirements can be reused

## Slide 3: Preconfigured UL resource
The TA is viewed as valid when the NRSRP change is below the configured threshold with |delta_NRSRP| <= threshold_NRSRP
Do not introduce the new attribute of TA or DL/UL timing difference for TA validation
The requirements for TA acquisition at least through RACH or EDT procedures follow the ones defined for random access

## Slide 4: Msg3 based channel quality reporting
Legacy requirements defined for R14 msg3 based quality reporting apply for msg3 based quality reporting on non-anchor carriers including,
  Hypothetical NPDCCH and
  Report mapping and
  Reporting accuracy

## Slide 5: NRS presence on non-anchor carriers
RAN4 confirms the feasibility of defining the RSRQ offset between anchor carrier and paging carrier in a carrier specific manner.
RAN4 confirms the feasibility of R15 WUS based serving cell measurement relaxation on non-anchor paging carriers for the UE who supports WUS and measure serving cell only on non-anchor paging carrier