## Slide 1: 3GPP TSG-RAN WG4 Meeting #91 Reno, United States of America, 13 – 17 May, 2019
Ericsson
Agreements for Rel-16 NB-IoT RRM enhancement
R4-1906798

## Slide 2: Preconfigured UL resource
When TA validation based on serving cell RSRP change method is configured, eNodeB shall determine and configure a single RSRP threshold to the UE.
Relaxed serving cell monitoring shall not be allowed when the UE is configured with TA validation method using serving cell RSRP change for PUR.

## Slide 3: Multicarrier operation
Introduce signalling for enabling the serving cell to inform the UE about power difference (DP) with a resolution of 0.5 dB and range between -9 dB to +9 dB. The power difference: DP = (PNRS_anchor - PNRS_non-anchor) in dB.
  Where:
    PNRS_anchor = NRS transmit power on anchor carrier expressed in dBm and
    PNRS_non_anchor = NRS transmit power on non-anchor carrier expressed in dBm.