## Slide 1: Way forward on Rel-15 NB-IOT NPRACH demodulation requirements
Ericsson, Huawei, Nokia
3GPP TSG-RAN WG4 Meeting #91
Reno, NV, USA, 13 – 17 May, 2019
R4-1907388

## Slide 2: FDD NPRACH demodulation requirements
RAN4 agreed to revise the NPRACH FDD format 2 demodulation requirements based on the updated simulation summary (R4-1906589).
CRs to TS36.104 (R4-1907749) and TS36.141 (R4-1906593) are based on the updated simulation summary.

## Slide 3: TDD NPRACH demodulation for alignment
It is observed the huge performance gap between the requirements in TS36.104 V15.6.0 and results by Nokia (R4-1906598).
Interested companies are encouraged to provide the simulation results in RAN4#92 to identify the reason of performance gap.
  Receiver assumption:
    Practical channel estimation
    Ideal channel estimation (Optional)
  See next page for simulation parameters

## Slide 4: Simulation parameters for alignment
Parameters | Values
Preamble formats | TDD NPRACH format 0
Cell ID | 0
NPRACH signature | 0
Uplink-downlink configuration | 1
Special subframe configuration | 7
Number of Tx antennas | 1
Number of Rx antennas | 2
Propagation condition | AWGN
Repetition number | 1
Frequency offset | 0 Hz
Frequency hopping | Enabled Disabled (Optional)
Detection performance | SNR to achieve 1) missed detection probability of 1%, 2) false alarm rate of 0.1%, and 3) timing error probability with limits of 3.646us at the same time

## Slide 5: Way forward on TDD NPRACH demodulation requirements
Once companies results are aligned in RAN4#92, interested companies are encouraged to provide the simulation results in RAN4#92bis with the parameters specified in TS36.104 V15.6.0 Clause 8.5.3.

## Slide 6: References
Tdoc | Title | Sources
R4-1905669 | Discussion on Rel-15 FeNB-IoT NPRACH performance requirements | Huawei, HiSilicon
R4-1906588 | Demodulation performance for NPRACH FDD preamble format 2 | Nokia, Nokia Shanghai Bell
R4-1906589 | Updated Summary of simulation results for Rel-15 FeNB-IoT NPRACH demodulation requirements | Nokia, Nokia Shanghai Bell
R4-1906590 | CR 36.104 Corrections to demodulation performance for NPRACH FDD preamble format 2 | Nokia, Nokia Shanghai Bell
R4-1906591 | CR 36.104 Corrections to demodulation performance for NPRACH FDD preamble format 2 | Nokia, Nokia Shanghai Bell
R4-1906593 | CR 36.141: Corrections to demodulation performance for NPRACH FDD preamble format 2 | Nokia, Nokia Shanghai Bell
R4-1906595 | CR 36.141: Corrections to demodulation performance for NPRACH FDD preamble format 2 | Nokia, Nokia Shanghai Bell
R4-1906598 | Demodulation performance for NPRACH TDD preamble formats | Nokia, Nokia Shanghai Bell
R4-1906600 | CR 36.104 Corrections to demodulation performance for NPRACH TDD preamble formats | Nokia, Nokia Shanghai Bell
R4-1906601 | CR 36.104 Corrections to demodulation performance for NPRACH TDD preamble formats | Nokia, Nokia Shanghai Bell
R4-1906643 | CR 36.141 Corrections to demodulation performance for NPRACH TDD preamble formats | Nokia, Nokia Shanghai Bell
R4-1906644 | CR 36.141 Corrections to demodulation performance for NPRACH TDD preamble formats | Nokia, Nokia Shanghai Bell
R4-1907749 | CR 36.104 Corrections to demodulation performance for NPRACH FDD preamble format 2 | Nokia, Nokia Shanghai Bell