## Slide 1: Simulation assumption of feasibility study for FR2 DL 256QAM
China Telecom
3GPP TSG-RAN WG4 Meeting #91 R4-1907711
Reno, Nevada, USA, 13-17 May 2019

## Slide 2: Background
Contributions submitted to RAN4#91 on FR2 DL 256QAM:
  R4-1906014 System level simulation for 256QAM DL in FR2, Nokia, Nokia Shanghai Bell
  R4-1906883 Impact of Tx and Rx impairments, Nokia, Nokia Shanghai Bell
  R4-1906685 Summary of 256QAM for FR2 analysis, Ericsson
  R4-1905395 Simulation assumption for 256QAM feasibility study, CATT
  R4-1905776 Views on NR FR2 256QAM requirements, Intel Corporation
  R4-1906108 Work plan on the WI: add support of NR DL 256QAM for FR2, China Telecom
  R4-1906109 TR skeleton for TR 38.8xx: Study on support of NR downlink 256 Quadrature Amplitude Modulation (QAM) for frequency range 2 (FR2), China Telecom

## Slide 3: Way forward
Companies are encouraged to provide link level simulations results showing the throughput difference between 64QAM and 256QAM using the assumptions in next slide (slide 4)
  Down-selection and/or prioritization of the simulation assumption will be considered in the next meeting.
Study aims to identify conditions where DL 256QAM provides performance benefits
Discussions on system level simulations are encouraged in next RAN4 meeting

## Slide 4: Link level simulation assumptions
Parameter | Value
Carrier frequency | 29 GHz (n257) and 39 GHz (n260)
CBW | 50 MHz, 100MHz, 200MHz
SCS | 60kHz, 120 kHz;
Allocated RBs | Full allocation
Propagation | TDL-A 30ns delay spread, 35Hz Doppler frequency TDL-D 30ns delay spread, 35Hz Doppler frequency Static
MCS | 64QAM: MCS 23, 24, 26, 28 in TS 38.214 Table 5.1.3.1-1, and other MCSs are not precluded 256QAM: MCS 21, 23, 25, 27 in TS 38.214 Table 5.1.3.1-2, and other MCSs are not precluded Baseline: fixed MCSs; optional: link adaptation
Precoding | Precoding configuration defined in 38.101-4 Section 7.2 for fading channels and Section 7.5 for static channel; follow PMI
Symbol type | CP-OFDM
HARQ | 8, None
Antenna configuration | Fading channel: 2x2 for Rank1 and Rank2, Low correlation Static channel: 1x2 for Rank1, 2x2 for Rank2
Channel estimation | Practical
Receiver type | MMSE
PDSCH configuration | Type A mapping, Start symbol 1, Duration 13 (for D slots)
DMRS configuration | Type 1, Single symbol, 1 additional DMRS
PTRS configuration | KPTRS : 2 (every 2 RBs), LPTRS : 1 (every 1 symbol)
Phase noise compensation | Practical based on PTRS
Phase noise model | TR 38.803 model (in section 6.1.10 and section 6.1.11) modelled Phase noise for TX and RX Option a): PN model config1: example1 (BS) + example1(UE) Option b): PN model config2: example2 (BS) + example2(UE) Option c): PN model config2: example2 (BS) + example2(BS) Option d): PN model config2: example2 (BS) + PN model config1: example1(UE) Option e): Other phase noise models, e.g. ones extracted from commercially available components or published results, are not excluded
txEVM + rxEVM excluding phase noise for 256QAM | txEVM: [1.0%-5.0%], rxEVM: [1.0%-5.0%] Option 1: txEVM < rxEVM; Option 2: no restriction
Other parameters | follow assumptions in 38.101-4 Section 7.2 for fading channels (e.g., case 2-6) and Section 7.5 for static channels