## Slide 1: B41/n41 spectrum sharing
CMCC
TSG-RAN Working Group 4 (Radio) meeting #91 R4-1907714
Reno, NV, USA, 13 – 17 May 2019

## Slide 2: Agreement
Define a new band and UL 7.5kHz shift is mandatory supported in this new band
  The UE supporting new band shall also support band n41
  The UE supporting band combinations with new band shall also support the same band combinations with band n41
  Apply all n41 requirements including band combinations (i.e. CA, DC, SUL) to new band
  UE mandatory support of 100kHz channel raster
  Send LS to RAN2 on the signaling impact
Check the CRs (R4-1906283, R4-1906284, R4-1906285 ).

## Slide 3: Agreement
Issue 1: Whether 7.5KHz is always applied to the new band
  Alt1: The new band will always adopt UL 7.5KHz shift, and n41 would be used for cases without UL 7.5kHz shift
    For Band n87
    FREF, shift = FREF + Δshift, Δshift = 7.5 kHz.
  Alt2: Apply frequencyShift7p5khz to TDD band from Rel-15. Detailed signaling design is up to RAN2. Send LS to RAN2 on the signaling impact.
    For Band n87
    FREF, shift = FREF + Δshift, Δshift = 0 kHz or 7.5 kHz.
    where Δshift is signalled by the network in higher layer parameter frequencyShift7p5khz

## Slide 4: Agreement
Issue 2: Supported SCS (SSB and data) on the new band
  Alt 1: New band only support 15KHz
    Against: KDDI, Samsung, Huawei, Qualcomm, Nokia
  Alt 2: New band support 15KHz, 30KHz, 60KHz

## Slide 5: Agreement
Issue 3: whether additional 100KHz channel raster is mandatory support for the new band
  UE mandatory support without capability

## Slide 6: Annex: Options discussed during offline
Option 4b: reuse band n41 and prevent Rel-15 UE to access band n41 cell with 7.5kHz UL shift configuration
  Introduce new Rel-15 tdd-frequencyShift7p5khz IE in the SIB
    Shift can only be used in 15 kHz n41 channels
    Future UEs not supporting shift know to not connect to cell
    Legacy 15 kHz SA n41 UEs do not appear to exist.
  DSS support:
    15 kHz SCS DSS uses UL 7.5kHz shift, 100kHz channel raster
    30 kHz and 60 kHz SCS DSS requires internal guard bands, so do not need 7.5 kHz shift or 100 kHz raster.
  DSS UL 7.5kHz shift support is mandatory optional in Rel-16 with capability signalling
    New UE capability introduced to indicate support for 7.5 kHz shift, 100 kHz raster
    UEs that do not support 7.5 kHz shift do not scan for alternate Synch Raster positions, so no scanning impact.
    Network can use this for HO and CA decisions for UE and shifted cells
It is claimed that no UE supports n41 with 15KHz so far. No NBC issue is observed.
RAN2 LS (R4-1907061) and RAN4 CRs need to be discussed

## Slide 7: Annex: Options discussed during offline
Option5: Define a new band and UL 7.5kHz shift is mandatory supported in this new band
  The UE supporting new band shall also support band n41
  The UE supporting band combinations with new band shall also support the same band combinations with band n41
  Apply all n41 requirements including band combinations (i.e. CA, DC, SUL) to new band
  Mandatory support of 100kHz channel raster is FFS
  The new band will always adopt UL 7.5KHz shift, and n41 would be used for cases without UL 7.5kHz shift
  The UE supporting new band and band combinations do not need to pass the test cases for n41 and the band combinations with n41
RAN4 CR need to be discussed (R4-1906283, R4-1906284, R4-1906285 ).