## Slide 1: WF on simulation assumptions for IAB co-existence study
Qualcomm Incorporated
3GPP TSG-RAN WG4 Meeting RAN4#91 R4-190xxxx
Reno, United States, 13th – 17th May 2019
Agenda: 8.5.2
Document for: Approval

## Slide 2: Background
In RAN#82, a WID on Integrated Access and Backhaul for NR (IAB) was approved in RP-182882
Among the objectives of the work item, RAN4 is tasked to define RF requirements for both backhaul (BH) and access links of an IAB-node including requirements for co-existence (e.g. ACLR, ACS)
In RAN4 #91 meeting there was intensive discussion on the simulation assumptions to be adopted for the IAB co-existence study

## Slide 3: Layout 1
Layout for nodes | IAB network: Two layer Macro layer: Hex. Grid (3 sector) (all macro BSs are IAB-donors) 19 sites Micro layer: 1 micro BSs per macro BS 1. Random drop (All micro BSs are all outdoor and are IAB-nodes) 2. Drop micro nodes in a circle with center at 40m and radius of 20m Victim network 1. Macro layer: Hex grid 3 sector coordinated layout (0% grid shift) – Rel.15 legacy network 2. Same as aggressor Orientation: Highest gain towards donor
Inter-BS distance | Macro layer: 200m FR2, 500m FR1
Minimum distance between Micro BS | 40m
Minimum distance between Macro BS and UE | 10m
Minimum distance between Micro BS and UE | 10m

## Slide 4: Layout 2
Layout for nodes | IAB network: Micro layer: Hex tri-sectorial Number of IAB-donors (Ndonor): 1 Number of IAB-nodes is 19 – Ndonor Victim network 1. Micro layer: Hex tri-sectorial – grid shift derived from minimum distance (20meters and 40 meters) 2. same as aggressor IAB-node and Micro BS are assumed to have 3 panels with 120 degree shift relative to each other.
Inter-BS distance | Micro layer: 200m

## Slide 5: Further agreements on Layout 1/2
Layout 1: All micro IAB nodes are IAB-MTs and study will investigate at least interference on UL to the macro gNB receivers.
Layout 2: IAB nodes transmitting BH in UL slots or DL slots

## Slide 6: Victim system
Legacy Rel.15 NR (no IAB nodes) : All micro IAB nodes are IAB-MTs and study will investigate at least interference on UL to the macro gNB receivers
Same layout as aggressor with IAB nodes deployed: study will investigate at least IAB-MTs DL reception

## Slide 7: Scenarios
Scenario 1:
  In case of TDM operation the following mapping of IAB node transmission/reception to a TDD pattern (DL/UL/F resources) is assumed:
    IAB DU transmission / IAB MT reception: DL time slots
    IAB MT transmission / IAB DU reception: UL time slots
Scenario 2: only Layout 2
  In case of TDM operation the following mapping of IAB node transmission/reception to a TDD pattern (DL/UL/F resources) is assumed:
    IAB DU transmission / IAB MT reception: DL time slots
    IAB MT transmission / IAB DU reception: DL time slots

## Slide 8: Half duplex constraints
The following half duplex constraints will apply to all the IAB nodes of the network:
MT and DU operations (resource usage) are TDM-ed at each site
Each site is only Tx-ing or Rx-ing on different interfaces – Layout 2 and Scenario 2
DU is able to support multiple cells (and therefore multiple sectors) only if the cells are synchronized, i.e. different sectors of the same site cannot be simultaneously transmitting and receiving.

## Slide 9: IAB operation mode (1)
The same TDD pattern is assumed between two adjacent channel operators
Aggressor: IAB Network, Victim: NR Network
Layout | Scenario | Aggressor system | Victim system
1 | 1 | UL: (IAB-MT) -> (IAB-Donor) | UL: UE -> gNB
2 | 1 | UL: (IAB-MT) & UE ->(IAB-DU/IAB-Donor) | UL: UE -> gNB
 |  | DL: (IAB-DU/IAB-Donor)->(IAB-MT) & UE | DL: gNB->UE
 | 2 | DL: (IAB-MT) ->(IAB-DU/IAB-Donor) & DL: (IAB-DU/IAB-Donor)->(IAB-MT & UE) | DL: gNB->UE
Assumption for all scenarios: |  | 1 MT and 3 DUs per site (1 DU per sector) | 

## Slide 10: IAB operation mode (2)
The same TDD pattern is assumed between two adjacent channel operators
Aggressor: NR Network, Victim: IAB Network
Layout | Scenario | Aggressor system | Victim system
1 | 1 | UL: UE -> gNB | UL: (IAB-MT) -> (IAB-Donor)
 |  | DL: gNB->UE | DL: (IAB-Donor)->(IAB-MT)
2 | 1 | UL: UE -> gNB | UL: (IAB-MT) & UE ->(IAB-DU/IAB-Donor)
 |  | DL: gNB->UE | DL: (IAB-DU/IAB-Donor)->(IAB-MT) & UE
 | 2 | DL: gNB->UE | DL: (IAB-MT) ->(IAB-DU/IAB-Donor) & DL: (IAB-DU/IAB-Donor)->(IAB-MT & UE)
Assumption for all scenarios: |  | 1 MT and 3 DUs per site (1 DU per sector) | 

## Slide 11: IAB operation mode (3)
The same TDD pattern is assumed between two adjacent channel operators
Aggressor: IAB Network , Victim: IAB Network
Layout | Scenario | Aggressor system | Victim system
1 | 1 | UL: (IAB-MT) -> (IAB-Donor) | UL: (IAB-MT) -> (IAB-Donor)
2 | 1 | UL: (IAB-MT) & UE ->(IAB-DU/IAB-Donor) | UL: (IAB-MT) & UE ->(IAB-DU/IAB-Donor)
 |  | DL: (IAB-DU/IAB-Donor)->(IAB-MT) & UE | DL: (IAB-DU/IAB-Donor)->(IAB-MT) & UE
 | 2 | DL: (IAB-MT) ->(IAB-DU/IAB-Donor) & DL: (IAB-DU/IAB-Donor)->(IAB-MT & UE) | DL: (IAB-MT) ->(IAB-DU/IAB-Donor) & DL: (IAB-DU/IAB-Donor)->(IAB-MT & UE)
Assumption for all scenarios: |  | 1 MT and 3 DUs per site (1 DU per sector) | 

## Slide 12: Link level assumptions
Target SNR
  IAB node-MT:
    SNR target: 22dB [upper limit of shannon curve]
    γ = 1
  Legacy NR UE:
    SNR target: 15 dB
    γ = 1
Power control
  MT for UL transmissions: Yes
  DU for DL transmission: No
Map SINR into throughput with the shannon equation

## Slide 13: Pathloss model
Proposal 1: Re-use the pathloss model between parent/donor IAB node DU and child IAB node MT agreed in RAN1 in TR 38.874
The path loss for links between the IAB-node and candidate serving IAB-nodes/donors is determined based on N independent large-scale channel realizations (taking into account LOS/NLOS probability and shadow fading). The realization that results in the minimum pathloss between the IAB-node and the associated serving IAB-node/donor is selected.
  N=3 intra-operator serving cell
  N=1 for all others

## Slide 14: System level parameters
Parameters | 
Duplex mode | TDD
Frequency range | FR1: 4.9GHz – FR2: 30GHz
Beamforming | FR1: Yes – FR2: Yes
Simulation bandwidth | 100MHz for FR1 200MHz for FR2
Number of UEs in the network | FR2: 1 active UE/sector FR1: 3 active UEs/sector
gNB Tx power | 33 dBm for FR2 macro and micro 46 dBm for FR1
IAB node Tx power | 33 dBm for FR2, PC is TBD for Scenario 2 for MT link 38dBm for FR1 (medium range power limit)
gNB antenna height | 25m for macro cells and 10m for micro cells
IAB node antenna height | 25m for macro cells and 10m for micro cells
gNB receiver noise figure | 10dB for FR2 5dB for FR1
IAB node receiver noise figure | 10dB for FR2 5dB for FR1
UE Tx power (dBm) | FR2: 22.4dBm EIRP (13.4dBm conducted) FR1: 23dBm (conducted)
UE noise figure (dB) | 10

## Slide 15: BS antenna configuration (FR1)
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 5 dBi (assuming 1.8dB loss)
BS antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 8, 8, 1) Note 1,2
(dv, dh) | (0.8λ, 0.5λ)
Mechanical down tilt | 10°
Note 1: Mg = number of antenna panels in elevation, Ng – number of antenna panels in azimuth, M = number of antenna elements/subarrays in elevation, N= number of antenna elements/subarrays in azimuth, P = number of polarizations. Note 2: single polarization simulated under the assumption of polarization match. | 
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 5 dBi (assuming 1.8dB loss)
BS antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 8, 8, 1) Note 1,2
(dv, dh) | (0.8λ, 0.5λ)
Mechanical down tilt | 10°
Note 1: Mg = number of antenna panels in elevation, Ng – number of antenna panels in azimuth, M = number of antenna elements/subarrays in elevation, N= number of antenna elements/subarrays in azimuth, P = number of polarizations. Note 2: single polarization simulated under the assumption of polarization match. | 
FR1 BS antenna modelling for macro scenario

## Slide 16: BS antenna configuration (FR1)
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 3 dBi (assuming 1.8dB loss)
BS antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 8, 8, 1) Note 1,2
(dv, dh) | (0.5λ, 0.5λ)
Mechanical down tilt | 0°
Note 1: Mg = number of antenna panels in elevation, Ng – number of antenna panels in azimuth, M = number of antenna elements/subarrays in elevation, N= number of antenna elements/subarrays in azimuth, P = number of polarizations. Note 2: single polarization simulated under the assumption of polarization match. | 
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 3 dBi (assuming 1.8dB loss)
BS antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 8, 8, 1) Note 1,2
(dv, dh) | (0.5λ, 0.5λ)
Mechanical down tilt | 0°
Note 1: Mg = number of antenna panels in elevation, Ng – number of antenna panels in azimuth, M = number of antenna elements/subarrays in elevation, N= number of antenna elements/subarrays in azimuth, P = number of polarizations. Note 2: single polarization simulated under the assumption of polarization match. | 
FR1 BS antenna modelling for micro scenario

## Slide 17: BS antenna configuration (FR2)
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 3 dBi (assuming 1.8dB loss)
BS antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 8, 16, 1) Note 1,2
(dv, dh) | (0.5λ, 0.5λ)
Mechanical down tilt | 10°
Note 1: Mg = number of antenna panels in elevation, Ng – number of antenna panels in azimuth, M = number of antenna elements/subarrays in elevation, N= number of antenna elements/subarrays in azimuth, P = number of polarizations. Note 2: single polarization simulated under the assumption of polarization match. | 
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 3 dBi (assuming 1.8dB loss)
BS antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 8, 16, 1) Note 1,2
(dv, dh) | (0.5λ, 0.5λ)
Mechanical down tilt | 10°
Note 1: Mg = number of antenna panels in elevation, Ng – number of antenna panels in azimuth, M = number of antenna elements/subarrays in elevation, N= number of antenna elements/subarrays in azimuth, P = number of polarizations. Note 2: single polarization simulated under the assumption of polarization match. | 
FR2 BS antenna modelling for macro scenario

## Slide 18: BS antenna configuration (FR2)
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 3 dBi (assuming 1.8dB loss)
BS antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 8, 16, 1) Note 1,2
(dv, dh) | (0.5λ, 0.5λ)
Mechanical down tilt | 0°
Note 1: Mg = number of antenna panels in elevation, Ng – number of antenna panels in azimuth, M = number of antenna elements/subarrays in elevation, N= number of antenna elements/subarrays in azimuth, P = number of polarizations. Note 2: single polarization simulated under the assumption of polarization match. | 
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 3 dBi (assuming 1.8dB loss)
BS antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 8, 16, 1) Note 1,2
(dv, dh) | (0.5λ, 0.5λ)
Mechanical down tilt | 0°
Note 1: Mg = number of antenna panels in elevation, Ng – number of antenna panels in azimuth, M = number of antenna elements/subarrays in elevation, N= number of antenna elements/subarrays in azimuth, P = number of polarizations. Note 2: single polarization simulated under the assumption of polarization match. | 
FR2 BS antenna modelling for micro scenario

## Slide 19: UE antenna configuration (FR2)
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 3 dBi (assuming 1.8dB loss)
UE antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 2, 2, 1)
(dv, dh) | (0.5λ, 0.5λ)
UE orientation | Random orientation in the azimuth domain: uniformly distributed between -90 and 90 degrees* Fixed elevation: 90 degrees
NOTE: This is done to emulate two panels: the configuration is equivalent to 2 panels with 180 shift in horizontal orientation and UE orientation uniformly distributed in the azimuth domain between -180 and 180 degrees. | 
Parameter | Values
Antenna element vertical radiation pattern (dB) | 
Antenna element horizontal radiation pattern (dB) | 
Combining method for 3D antenna element pattern (dB) | 
Maximum directional gain of an antenna element GE,max | 3 dBi (assuming 1.8dB loss)
UE antenna configuration | (Mg, Ng, M, N, P) = (1, 1, 2, 2, 1)
(dv, dh) | (0.5λ, 0.5λ)
UE orientation | Random orientation in the azimuth domain: uniformly distributed between -90 and 90 degrees* Fixed elevation: 90 degrees
NOTE: This is done to emulate two panels: the configuration is equivalent to 2 panels with 180 shift in horizontal orientation and UE orientation uniformly distributed in the azimuth domain between -180 and 180 degrees. | 
FR2 UE antenna modelling for micro scenario

## Slide 20: UE antenna configuration (FR2)
Isotropic antenna with 0dBi gain

## Slide 21: Simulation methodology
Layout 1: Optimum orientation between parent and child
Layout 2: Antenna orientation based on planned macro layout
Topology is based on RSRP (based on pathloss and element antenna gain)
FFS activity factor