## Slide 1: Way Forward on CLI RRM
3GPP TSG-RAN WG4 Meeting #92 Ljubljana, Slovenia, 26 - 30 August 2019
Agenda Item: 9.2.3
R4-1909991
LG Electronics

## Slide 2: CLI measurement requirement
Definition for DL timing error (TCLI)
  DL timing error is the time difference between downlink reference timing in the serving cell and SRS arrival time.
    RAN4 will define the timing error as the side condition for SRS-RSRP.
      E.g., TCLI = NTA_offset + Tother
        NTA_offset 20usec for EN-DC(TDD), 13usec for FR1, 7usec for FR2
      FFS on whether the cell phase synchronization error (3usec) is added for TCLI
        Decide whether side condition is needed or not in next meeting
    FFS on whether the same side condition (TCLI) for sub-band RSSI
      Decide whether side condition is needed or not in next meeting

## Slide 3: SRS-RSRP measurement requirement
Reference SNR for SRS signal
  Option 1 : SNR with zero timing error
  Option 2 : SNR with timing error (TCLI)
  Decide one of the option in next meeting
The number of RB for SRS resource
  48 RBs
The number of sample for measurement accuracy
  3 samples

## Slide 4: SRS-RSRP measurement requirement
Other condition for SRS-RSRP measurement accuracy
  Define minimum distance between cyclic shifts of two SRS as half the maximum number of cyclic shifts for the side condition, which applies the case where the two SRS resources are on the same symbol.
  Measurement accuracy could be worse due to cross-correlation from interfering root sequence when two SRS resource are on the same symbol and same comb
  Companies are encouraged to provide how to capture these condition in the specification in next meeting
FFS for the measurement performance for single port measurement when multiple port SRS are transmitted

## Slide 5: UE behavior for CLI measurement
Scheduling restriction for CLI measurement
  SRS-RSRP measurement
    Depending on the UE capability, UE is not expected to receive PDCCH/PDSCH on SRS-RSRP measured OFDM symbols, and on Y data symbol before SRS-RSRP measured symbol in intra-band CA.
  CLI-RSSI measurement
    Depending on the UE capability, UE is not expected to receive PDCCH/PDSCH on CLI-RSSI measured OFDM symbols in intra-band CA.
      FFS for scheduling restriction on X data symbol before CLI-RSSI measured symbol
  Y and X values depends on TCLI.

## Slide 6: CLI measurement reporting range
SRS-RSRP reporting range
  Option 1: 1dB step size
CLI-RSSI reporting range
Reported value | Measured quantity value | Unit
SRS_RSRP_0 | SRS-RSRP<-140 | dBm
SRS_RSRP_1 | -140≤ SRS-RSRP<-139 | dBm
SRS_RSRP_2 | -139≤ SRS-RSRP<-138 | dBm
SRS_RSRP_3 | -138≤ SRS-RSRP<-137 | dBm
SRS_RSRP_4 | -137≤ SRS-RSRP<-136 | dBm
… | … | …
SRS_RSRP_95 | -46≤ SRS-RSRP<-45 | dBm
SRS_RSRP_96 | -45≤ SRS-RSRP<-44 | dBm
SRS_RSRP_97 | -44≤ SRS-RSRP | dBm
SRS_RSRP_98Note1 | Infinity | 
Note1 : ‘Infinity’ means that UE cannot detect SRS due to too strong signal to measure. |  | 
Reported value | Measured quantity value | Unit
CLI_RSSI_00 | CLI-RSSI  -100 | dBm
CLI_RSSI_01 | -100  CLI-RSSI < -99 | dBm
CLI_RSSI_02 | -99  CLI-RSSI < -98 | dBm
… | … | …
CLI_RSSI_74 | -27  CLI-RSSI < -26 | dBm
CLI_RSSI_75 | -26  CLI-RSSI < -25 | dBm
CLI_RSSI_76 | -25 CLI-RSSI | dBm
  Option 2: 2dB step size
Reported value | Measured quantity value | Unit
SRS_RSRP_0 | SRS-RSRP<-140 | dBm
SRS_RSRP_1 | -140≤ SRS-RSRP<-138 | dBm
SRS_RSRP_2 | -138≤ SRS-RSRP<-136 | dBm
SRS_RSRP_3 | -136≤ SRS-RSRP<-134 | dBm
SRS_RSRP_4 | -134≤ SRS-RSRP<-132 | dBm
… | … | …
SRS_RSRP_47 | -48≤ SRS-RSRP<-46 | dBm
SRS_RSRP_48 | -46≤ SRS-RSRP<-44 | dBm
SRS_RSRP_49 | -44≤ SRS-RSRP | dBm
SRS_RSRP_50Note1 | Infinity | 
Note1 : ‘Infinity’ means that UE cannot detect SRS due to too strong signal to measure. |  |