## Slide 1: Way forward on PDSCH CA normal demodulation requirements
Intel Corporation, …
3GPP TSG-RAN WG4 Meeting #92
Ljubljana, Slovenia, 26 – 30 August 2019 Agenda Item: 9.17.1
R4-1910046

## Slide 2: General issues
      General approach for developing CA normal demodulation requirement:
  Develop NR CA normal demodulation requirement based on per CC performance requirement, which is identical to single carrier performance without extra margin.
      Test design:
  Develop the methodology in a forward compatible way.
  For the exact CA capability and single CC channel bandwidth, FFS based on the Rel-15/16 core spec.
      EN-DC, NE-DC:
  All NR CA normal demodulation requirements are applicable to EN-DC and NE-DC with CA. In case of EN-DC and NE-DC, EUTRA performance will not be verified.
      NR-DC:
  All NR CA normal demodulation requirements are applicable to NR-DC with CA. No specific requirements for NR-DC will be specified.

## Slide 3: Scenarios
      Duplex mode:
  FR1: FDD+FDD CA, TDD+TDD CA, FDD+TDD CA
  FR2: TDD+TDD CA
      Channel bandwidth and SCS for requirements:
  Option 1: All configurable channel bandwidths for all the configurable SCSs
    Note: not consider FR1 60kHz SCS
  Option 2: Down-select considering the CA configurations in the core spec
    Option 2a: Down-select to ensure each CA configuration can be tested.
    Option 2b: Down-select to ensure the maximum aggregated channel bandwidth combination for each CA configuration can be tested.
  For option 2a/2b
    Till March 2020, focus on the CA configuration in Rel-16 June 2019 version
    From March 2020, cover the CA configurations in Rel-16 Mar 2020 version
      FFS scenarios with different SCS on different CCs

## Slide 4: Simulation assumptions
      Rank:
  For 2Rx
    Option 1: rank 1, 2
    Option 2: rank 1
    Option 3: rank 2
  For 4Rx
    Option 1: rank 1 or rank 2
    Option 2: rank 1, 2
    Option 3: rank 1, 2, 3, and 4
      MCS:
  Option 1: MCS 13 (16QAM, CR 1/2)
  Option 2: cover QPSK, 16QAM, 64QAM and 256QAM in different tests
  Other options are not precluded
      Receiver type:
  MMSE-IRC, FFS for R-ML

## Slide 5: Simulation assumptions
      TDD UL-DL pattern:
  FR1 30kHz: 7DS2U with S=6:4:4
  FR2 120kHz: DDDSU with S=10:2:2
      HARQ process number:
  Baseline
    FR1 FDD: 4
    FR1 TDD with 30 kHz SCS: 8
    FR2 TDD with 120 kHz SCS: 8
  FFS: 16 HARQ process for limited CA configuration(s)/band combination(s)
      Antenna correlation for MMSE-IRC: ULA Low
      Propagation condition:
  FR1: TDLA30-10
  FR2: TDLA30-75
      Throughput test point: 70% of max TP

## Slide 6: Simulation assumptions
      SSB configuration: Periodicity 20 ms, Allocated in first slot within 20ms
      PDSCH configuration
  FR1 FDD and TDD (full DL slots): Type A, Start symbol 2, Duration 12
  FR1 TDD (special slots) : Type A, Start symbol 2, Duration depends on configuration
  FR2 (full DL slots): Type A, Start symbol 1, Duration 13
  FR2 (special slots): Type A, Start symbol 1, Duration depends on configuration
      DMRS configuration for FR1 and FR2
  Type 1, 1 additional DMRS, Single symbol
      PTRS configuration for FR2
  Frequency density 2, Time density 1
      TRS configuration for FR1 and FR2
  20 ms periodicity, 2 slots, Offset 10 ms

## Slide 7: Test applicability rule
      FFS categorizing of CA capabilities
      FFS on test of different CA capabilities
      FFS on test applicability for different CA duplex mode
      FFS on selection of CA configuration(s) for test among supported CA configurations
      FFS on selection CBW combination for test for selected CA configuration

## Slide 8: Work prioritization
      Discuss the prioritization of the work regarding different test configurations

## Slide 9: NR CA testing in FR2
      For FR2 test, encourage TE vendors to provide analysis on the achievable SNR for larger aggregated bandwidths.
  Provide information for 29GHz and 39GHz carrier frequencies.