## Slide 1: WF on EN-DC HPUE FDD+TDD China Unicom, CHTTL, China Telecom
3GPP TSG-RAN WG4 Meeting #92 R4-1910277
Ljubljana, SI, 26th– 30th Aug, 2019

## Slide 2: Backgrounds (1/2)
The scope of PC2 FDD-TDD including the following two cases:
  Study starts from case 1, but case 2 is not precluded.
  Example band combination for this study is DC_3_n78
 | EN-DC maximum power | LTE maximum power | NR maximum power
Case 1 | 26dBm | 23dBm | 23dBm
Case 2 | 26dBm | 23dBm | 26dBm

## Slide 3: Backgrounds (2/2)
WF R4-1907488 was approved during RAN4#91
For case 1 PC2 FDD-TDD HPUE
  Further discuss
    The relationship between the duty cycle for LTE and NR, max LTE and NR power, and the maximum UL duty cycle for PC2 FDD-TDD EN-DC in the next meeting, starting from the following equation:
    PLTE, PNR, P26 represent the maximum linear power (mW) of LTE, NR, and EN-DC power class 2 respectively; DutyLTE, DutyNR represent the normalized uplink duty cycle of LTE and NR respectively.
    Duty threshold is the maximum UL duty cycle used to maintain the PC2 power class for FDD+TDD ENDC HPUE.
    The SAR effect differences for FDD and TDD bands will be considered.
    How to reflect the SAR difference for different bands in the above equation will be further studied.
    P-MPR can always be used by UE for SAR when necessary.
  Other solutions are not precluded
DutyLTE*(PLTE/ P26) + DutyNR*(PNR/ P26) ≤ Duty threshold….(1)

## Slide 4: WayForward on NSA FDD+TDD HPUE (1/3)
General
  The following options will be discussed for both case1 and case2.
Target on down selection on UE reporting capability solutions based on the following Options, and any new solution will not be discussed in RAN4#92bis.
  Option1 report EN-DC total Duty cycle(Duty threshold) based on DutyLTE*(PLTE/ P26) + DutyNR*(PNR/ P26) ≤ Duty threshold[2][6]
  Option2 report DutyLTE based on NR TDD sub-frame configuration[5]
  Option3 report DutyNR based on LTE fixed dutycycle with LTE maximum transmit power 23dBm[4]
  Option4 report SARratio based on DutyLTE*(PLTE/ P26) + SARratio*DutyNR*(PNR/ P26) ≤ 50%[5]
  Option5 report SARratio and EN-DC total Duty cycle(Duty threshold) based on DutyLTE*(PLTE/ P26) + SARratio*DutyNR*(PNR/ P26) ≤ Duty threshold[1]
  Option6 configure Plte lower than 23dBm based on LTE 100% dutycycle[3]
  Target on finishing this SI in RAN#86

## Slide 5: WayForward on NSA FDD+TDD HPUE (2/3)
Proponents of each option shall provide minimum and maximum values for case1 and case2 based on the following table of their option.
Case1（LTE 23dBm+NR 23dBm） | option1 | option2 | option3 | option4 | option5 | 
Report capability signaling | Duty threshold | DutyLTE | DutyNR | SARratio | SARratio | Duty threshold
Minimum value |  |  |  |  |  | 
Maximum value |  |  |  |  |  | 
Case2（LTE 23dBm+NR 26dBm） | option1 | option2 | option3 | option4 | option5 | 
Report capability signaling | Duty threshold | DutyLTE | DutyNR | SARratio | SARratio | Duty threshold
Minimum value |  |  |  |  |  | 
Maximum value |  |  |  |  |  | 

## Slide 6: WayForward on NSA FDD+TDD HPUE (3/3)
In next meeting, proponent of each option shall provide analysis at least from following aspects.
Comparison principle | option1 | option2 | option3 | option4 | option5 | option6
Performance i.e. Minimum performance based on the values of report capability |  |  |  |  |  | 
Specification impacts i.e. potential impacts to relevant specifications |  |  |  |  |  | 
Flexibility i.e. how to provide reasonable performance for different network configuration |  |  |  |  |  | 
Complexity i.e. complexity regarding BS scheduling, UE implementation, signaling design etc. |  |  |  |  |  | 
Consideration of the SAR effect differences for FDD and TDD bands i.e. whether the difference has been considered? And How? |  |  |  |  |  | 
Testability i.e. how the proposal can be tested for SAR regulatory compliance test. How much test effort is envisioned? |  |  |  |  |  | 

## Slide 7: reference
R4-1909060 Effective use of power of PC2 UE with two different UL bands NTT DOCOMO, INC.
R4-1908591 Further discussion on solutions for EN-DC FDD-TDD High Power UE CHTTL, China Unicom
R4-1908721 Increasing EN-DC power for FDD-TDD PC2 and PC3 Ericsson
R4-1908862 Discussion on different schemes for PC2 EN-DC (FDD+TDD) vivo
R4-1909080 About NSA FDD-TDD HPUE SAR OPPO
R4-1909908 Further consideration on SAR solutions for FDD+TDD HPUE Huawei, HiSilicon