## Slide 1
3GPP TSG-RAN WG4 Meeting #92Bis R4-1910931
Chongqing, China, 14th – 18th Oct, 2019
Agenda Item: 8.17.2.3
WF on BS demodulation for NR HST
CMCC

## Slide 2: Agreements
Maximum Doppler
    for 30KHz SCS, it is proposed to consider Doppler shift of 3334 Hz for UL with 500km/h
    for 15KHz SCS, it is proposed to consider Doppler shift of 1500 Hz for UL with 500km/h
Channel model
    for open space scenario, Ds is proposed to be 700 meters and Dmin is proposed to be 150 meters
CBW
    it is proposed to specify the BS demodulation requirements for the bandwidth of 5/10/20 MHz with 15 KHz SCS and the bandwidth of 10/20/40/100 MHz with 30KHz SCS. And applicability rule specified in Rel-15 NR can be reused

## Slide 3: Agreements
PUSCH
    Reference signal
      the reference signal of PUSCH is proposed to be DMRS, and the DMRS configuration is proposed to be 1+1+1 (type 1, single-symbol DMRS)
    Antenna configuration
      it is proposed to consider 2 TX, 8 RX

## Slide 4: Agreements
PRACH
    for 350km/h with PRACH format 0, the frequency offset for restricted set type A is proposed to be 1340Hz and the frequency offset for restricted set type B is proposed to be 2334Hz
    for 500km/h, it is proposed to consider PRACH format A2/A3/B4/C2. And the frequency offset is proposed to be 3334Hz