## Slide 1: WF on CSI-RS based RRM measurements requirements
CATT
3GPP TSG-RAN WG4 Meeting #92bis R4-1910956
Chongqing, China, 14-18 Oct 2019

## Slide 2: CSI-RS configuration for measurement requirements
CSI-RS configurations
  Requirements shall be defined for N sets of CSI-RS configurations (bandwidth of CSI-RS and density of CSI-RS resource)
    Option 1: N =1
    Option 2: N = 2
    Further decide N based on simulation results for different CSI-RS configurations
  Define requirements at least for 48 PRBs CSI-RS BW configuration. CSI-RS density is FFS.
  Encourage companies to submit simulation results based on agreed simulation assumption [1] in RAN4#93 meeting
Do not define requirements for CSI-RS with 24 PRBs BW and D = 1

## Slide 3: WF on CSI-RS based intra-frequency and inter-frequency measurement definition
The following condition is agreed to define CSI-RS based intra-frequency measurement
  the SCS of CSI-RS on serving cell and target cell is the same
  Additional conditions are FFS
The candidate options listed in slide 4-8 are considered to define CSI-RS based intra-frequency and inter-frequency measurement in RAN4#93 meeting
  Other options are not precluded
  The definition of intra-frequency and inter-frequency measurement should take UE measurement capability, MO configuration feasibility etc. into consideration.
Notes: CMCC: no impact on MO definition
Nokia: same view as CMCC
HW: prefer Option3
MTK: no intention to change MO definition, need to check the definition across MO. No impact the exsiting signalling in RAN2
Apple: option 2
Companies views:
Option1: (Nokia, HW, CMCC, ZTE)
Option2: (Apple, CATT,CMCC)
Option3: (HW, CATT)
Option4: (QC)

## Slide 4
Option 1:
the centre frequency of CSI-RS resources on the target cell configured for measurement is the same as centre frequency of CSI-RS resources on the serving cell configured for measurement, and,
    the SCS of CSI-RS on serving cell and target cell is the same

## Slide 5
Option 2:
    the bandwidth of CSI-RS resources of target cell configured for measurement is within the active BWP of serving cell, and,
    the SCS of CSI-RS on serving cell and target cell is the same

## Slide 6
Option 3:
the centre frequency of CSI-RS resources on the target cell configured for measurement is the same as centre frequency of CSI-RS resources on the serving cell configured for measurement, and,
    the bandwidth of CSI-RS resources of target cell configured for measurement is within the active BWP of serving cell, and,
    the SCS of CSI-RS on serving cell and target cell is the same

## Slide 7
Option 4:
the centre frequency of CSI-RS resources on the target cell configured for measurement is the same as centre frequency of CSI-RS resources on the serving cell configured for measurement, and,
the bandwidth of CSI-RS resources on the target cell configured for measurement is the same as bandwidth of CSI-RS resources on the serving cell configured for measurement, and,
    the bandwidth of CSI-RS resources of target cell configured for measurement is within the active BWP of serving cell, and,
    the SCS of CSI-RS on serving cell and target cell is the same

## Slide 8
Option 5:
the centre frequency of CSI-RS resources on the target cell configured for measurement is the same as centre frequency of CSI-RS resources on the serving cell configured for measurement, and,
the bandwidth of CSI-RS resources on the target cell configured for measurement is the same as bandwidth of CSI-RS resources on the serving cell configured for measurement, and,
    the bandwidth of CSI-RS resources of target cell configured for measurement is within the active BWP of serving cell, and,
    the SCS of CSI-RS on serving cell and target cell is the same, and,
    the CSI-RS is configured within the MO indicated as servingCellMO in ServingCellConfig, and,
    the CSI-RS is configured within the MO with intra-frequency SSB-based measurement, if SSB-based measurement is configured.

## Slide 9: Reference
1. R4-1910949 Link-level simulation assumptions for CSI-RS based measurements CATT