## Slide 1: WF on RRM Requirement Scope for Rel-16 NR eMIMO WI
Samsung
R4-1911389
3GPP TSG-RAN WG4#92Bis Meeting
Chongqing, China, 14-18 Oct, 2019
Agenda: 8.11.2

## Slide 2
Background
Rel-16 NR eMIMO WI (i.e., Enhancements on MIMO for NR) is a RAN1 leading WI with below major enhancement in RAN1 area:
  Enhancements on MU-MIMO support
  Enhancements on multi-TRP/panel
  Enhancements on multi-beam operation
    DL/UL beam indication with reduced latency and overhead
    Beam failure recovery for SCell
    L1-SINR measurement
  Enhancement on low PAPR RS
  Enhancement on full Tx power uplink transmission
Some of enhancements in Rel-16 NR eMIMO WI need introducing corresponding RAN4 RRM core requirement.
  Based on discussion in RAN4#92Bis, RRM requirement impacts by introducing Rel-16 MIMO enhancement features are identified.

## Slide 3
Way Forward for BFR on SCell
Identified RRM requirement impact for beam failure recovery on SCell:
  Link recovery procedure general (Section 8.5):
    Introduction part: Scenarios for SCell BFR needs to be added;
    Detailed scenarios (SCell with both UL and DL, SCell with DL only) needs clarification;
    Further clarification on that only CSI-RS based BFD is applied for SCell BFD.
  Beam failure detection:
    Rel-15 core requirement shall be followed and no impact identified.
  Candidate beam detection:
    Rel-15 core requirement shall be followed and no impact identified.
  New SCell BFRQ mechanism:
    Introduce Rel-16 RRM requirement for UE capability for maximum number of SCell for which UE performs BFR.
    No need to specify additional core requirement for SCell BFRQ mechanism.

## Slide 4
Way Forward for L1-SINR Measurement
Identified RRM requirement impact for L1-SINR Measurement and reporting:
  L1-SINR measurement for reporting:
    L1-SINR related UE capability.
    Measurement reporting requirement
    Requirement on measurement restriction of UE during L1-SINR measurement
    Requirement on scheduling availability of UE during L1-SINR measurement

## Slide 5
Way Forward for DL/UL beam indication with reduced latency and overhead
Identified RRM requirement impact for DL/UL beam indication with reduced latency and overhead:
  Spatial Relation Updates for AP-SRS via MAC-CE:
    Mechanism shall be introduced in Rel-16 RRM requirement enhancement work item for SRS-related requirement;
  Updating Pathloss RS for PUSCH/SRS via MAC-CE:
    No impact on RRM core requirement;
  Simultaneous Spatial Relation Update for Multiple PUCCH Resources:
    No impact on RRM core requirement;
  Simultaneous TCI States Activation/Selection across Multiple CCs/BWPs:
    Define RRM requirement for simultaneous TCI states activation/selection across multiple CCs/BWPs.