## Slide 1: 3GPP TSG-RAN WG4 Meeting #92bis Chongqing, China, 14th – 18th October, 2019
Ericsson
Way forward on Rel-16 MTC RRM enhancement
R4-1912147

## Slide 2: MPDCCH performance improvement for RLM
RAN4 assumes the downlink radio link quality measurement is based on CRS only even if MPDCCH uses DMRS+CRS for demodulation reference signals.
RAN4 sets the same evaluation period as Rel-13 eMTC, e.g., TEvaluate_Qout_CatM1 = 400 ms and TEvaluate_Qin_CatM1 = 200 ms for CE Mode A UE without DRX and TEvaluate_Qout_CatM1 = 4000 ms and TEvaluate_Qin_CatM1 = 2000 m for CE Mode B UE without DRX.
RAN4 will use the MPDDCH parameters in Table 3 to evaluate MPDCCH BLER for RLM with improved MPDCCH.

## Slide 3: Preconfigured UL resource
The value of M and N in the agreed measurement conditions for first measurement (RSRP1) and second measurement (RSRP2) are defined as follows:
  M/N=DRX cycle length when DRX cycle length < 1.28 seconds and M/N=DRX_cycle_length/2 ≥1.28 seconds.
The value of M and N in the agreed measurement conditions for first measurement (RSRP1) and second measurement (RSRP2) are as defined above when measurements are performed within PTW. But when outside PTW, M/N=DRX_cycle_length/4.
If the first- and second measurement conditions are not met, UE shall perform new measurement, or delay the PUR transmission until next PUR transmission opportunity or it may drop PUR and fall back to RACH.
The range is defined as [-2, …., 4] dB excluding 0 dB value with a 1 dB resolution when K=2. The range is defined as [2, ….,5 ] dB with a resolution of 1 dB when K=1.

## Slide 4: DL quality reporting
RAN4 specifies the RRM core requirements for MSG3-based channel quality reporting as shown in section 3 of R4-1911772.
For DL quality reporting in CONNECTED mode, RAN4 waits for RAN1/RAN2 decision.

## Slide 5: Mobility enhancement
Improved measurement accuracy requirements for RSRP based on RSS is defined based on L1 period of 320 ms.
RSS based absolute RSRP measurement accuracy requirements are defined as follows:
 | 1Rx | 2Rx
CE mode A, Es/Iot >= -6 dB | +/-4dB (for L1 measurement period of 320ms/640ms) | +/-4dB
CE mode B, Es/Iot >= -12 dB | +/-5dB (for L1 measurement period of 320ms), +/-4dB (for L1 measurement period of 640ms) | +/-4dB
CE mode B, -15 <= Es/Iot <= -12 dB | +/-6dB (for L1 measurement period of 320ms), +/-5dB (for L1 measurement period of 640ms) | +/-5dB

## Slide 6: Mobility enhancement
RSS based RSRP measurements for serving and neighbour cells in RRC_CONNECTED state are discussed based on RAN1/RAN2 agreements about the RSS configurations.
Signalling support is introduced to enable the eNodeB to configure the UE with RSS based RSRP measurement.