## Slide 1: WF on the addition of new bandwidths
Qualcomm Incorporated
R4-1912541

## Slide 2: Problem statement
Absence of specific signaling means that all bandwidths are supported [1]. However, as new bandwidths are added, legacy UE’s not signaling specific bandwidths are no longer compliant and can be misunderstood to support the new bandwidth when they don’t.
New bandwidths added are optional, so there needs to be a way to signal whether they are supported or not.
New bandwidths originally optional may become mandatory after some time, so there needs to be a way to identify which ones and when they are mandatory.

## Slide 3: Way forward
Define 3 different categories of bandwidths per band
  Legacy: These are defined at the time the band is introduced. This list never changes.
  Optional: Indicates a new bandwidth that is optional in the present version of the spec. In future versions of the spec, this bandwidth may migrate over to the “Mandatory” category.
  Mandatory: Indicates a new bandwidth that is mandatory in the present version of the spec
Possible signaling approach
  If not individually signaled, if no specific bandwidth signaled, all Legacy bandwidths are interpreted as supported
  New bandwidths (optional and mandatory category) are signaled via a bitmap. If not signaled, they are interpreted as NOT supported
  New bandwidths that are mandatory shall have supported bit set to ‘1’ in the bitmap
Send LS to RAN2

## Slide 4: Example

## Slide 5: Reference
[1] R4-1912438, “Signaling concerns for adding legacy channel bandwidth to an existing band,” Sprint