## Slide 1: 3GPP TSG-RAN WG4 Meeting #92Bis Chongqing, China, 14 - 18 October, 2019
Huawei, HiSilicon, Ericsson, Samsung
Way forward on LTE-NR coexistence for TDD
R4-1912711

## Slide 2: Test Configurations (1/2)
Number of tests
  Test 1: Mapping Type A, Start symbol 3, Duration 9
  Test 2: Mapping Type A, Start symbol 3, Duration 11
Test applicability rule:
  The test with duration 11 is applied only when UE supports additionalDMRS-DL-Alt
  If UE supports alternative DMRS configuration then it can pass requirements only for scenario with PDSCH duration 11 and skip testing for scenario with PDSCH duration 9
SCS for NR carrier: 15 kHz
TDD UL/DL configuration
  LTE: LTE UL-DL configuration 2, Special subframe configuration 7
  NR: DDDSU with S=10:2:2
PDSCH scheduling
  Skipped slots with NR SSB, LTE PBCH/PSS/SSS and special slots
  PDSCH is scheduled in NR slots {1, 5, 6, 10, 11, 15, 16} every 20ms

## Slide 3: Simulation assumption summary
Parameter |  | Unit | Value
Duplex mode |  |  | TDD
CHB/SCS |  |  | CBW:10MHz; SCS: 15kHz
Channel Model |  |  | TDLA30-10
TDD configuration |  |  | LTE: LTE UL-DL configuration 2, Special subframe configuration 7 NR with 15kHz SCS: DDDSU with S=10:2:2
SSB configuration |  |  | Periodicity 20 ms, allocated in first slot within 20 ms
TRS configuration for NR TDD configuration Option 1 |  |  | 2 slots, offset 10 ms, periodicity 20 ms
MCS |  |  | MCS 4 (QPSK, CR 0.30)
Antenna configuration and Rank |  |  | 4x2 and 4x4 ULA Low Rank 1
PDSCH configuration | Mapping type |  | Type A
 | Starting symbol (S) |  | 3
 | Length (L) |  | 9 and 11
 | PDSCH aggregation factor |  | 1
 | PRB bundling size |  | 2
 | PDSCH scheduling |  | Skipped slots with NR SSB, LTE PBCH/PSS/SSS and special slots: NR slots {1, 5, 6, 10, 11, 15, 16} every 20ms
PDSCH DMRS configuration | DMRS Type |  | Type 1
 | Number of additional DMRS |  | 1
 | Position of the first DM-RS for downlink |  | 3
 | Maximum number of OFDM symbols for DL front loaded DMRS |  | 1
CRS for rate matching (Note 1) | LTE carrier centre subcarrier location |  | Same as NR carrier centre subcarrier location
 | LTE carrier BW | MHz | 10
 | Number of antenna ports |  | 4
 | v-shift |  | 0
Number of HARQ Processes |  |  | 8
Note 1: No MBSFN is configured on LTE carrier |  |  | 

## Slide 4: FRC
Parameter | Unit | Values | 
Reference channel |  | Test 1 | Test 2
Channel bandwidth | MHz | 10 | 10
Subcarrier spacing | kHz | 15 | 15
Number of allocated resource blocks | PRBs | 52 | 52
Number of consecutive PDSCH symbols |  |  | 
For Slot i, if mod(i, 5) = 3 for i from {0,…,19} |  | N/A | N/A
For Slot i, if mod(i, 5) = {0,1} for i from {0,…,19} |  | 9 | 11
Allocated slots per 2 frames | Slots | 7 | 7
MCS table |  | 64QAM | 64QAM
MCS index |  | 4 | 4
Modulation |  | QPSK | QPSK
Target Coding Rate |  | 0.30 | 0.30
Number of MIMO layers |  | 1 | 1
Number of DMRS REs |  | 12 | 12
Overhead for TBS determination |  | 18 | 18
Information Bit Payload per Slot |  |  | 
For Slots i = 0 | Bits | N/A | N/A
For Slots i, if mod(i, 5) = {2,3,4} for i from {1,…,19} | Bits | N/A | N/A
For Slots i, if mod(i, 5) = {0,1} for i from {1,…,19} | Bits | 2472 | 3240
Transport block CRC per Slot |  |  | 
For Slots i = 0 | Bits | N/A | N/A
For Slots i, if mod(i, 5) = {2,3,4} for i from {1,…,19} | Bits | N/A | N/A
For Slots i, if mod(i, 5) = {0,1} for i from {0,…,19} | Bits | 16 | 16
Number of Code Blocks per Slot |  |  | 
For Slots i=0 | CBs | N/A | N/A
For Slots i, if mod(i, 5) = {2,3,4} for i from {1,…,19} | CBs | N/A | N/A
For Slots i, if mod(i, 5) = {0,1} for i from {1,…,19} | CBs | 1 | 1
Binary Channel Bits Per Slot |  |  | 
For Slots i=0 | Bits | N/A | N/A
For Slots i, if mod(i, 5) = {2,3,4} for i from {1,…,19} | Bits | N/A | N/A
For Slots i = 10, 11 | Bits | 7760 | 10256
For Slots i, if mod(i, 5) = {0,1} for i from {1,…,9,12,…,19} | Bits | 8384 | 10880
Max. Throughput averaged over 2 frames | Mbps | 0.865 | 1.134
Note 1: SS/PBCH block is transmitted in slot #0 with periodicity 20 ms Note 2: Slot i is slot index per 2 frames Note 3: No user data is scheduled on slots with LTE PBCH/PSS/SSS |  |  | 

## Slide 5: Way forward
Interesting companies are encouraged to provide alignment results in the next RAN4#93 meeting.