## Slide 1: Updated WF on IAB RRM Requirements
Qualcomm
3GPP TSG-RAN WG4 Meeting #92 Chongqing, China, Oct 14th - 18th, 2019
R4-1912829

## Slide 2: Background - I
RAN4 already agreed to the following during this meeting.
Requirements | Comments | Is requirement needed?
Cell reselection | Intra-frequency Inter-frequency | No
Handover |  | FFS Yes No
RRC Connection Mobility Control | RRC re-establishment Random access RRC release with redirection | Yes
SCell activation/deactivation delays |  | No
Interruptions related to SCells addition, release, activation, deactivation | Interruptions on serving cells due to any of the addition, release, activation, or deactivation procedures | No
PSCell addition/release delays |  | No
Active BWP switching | Interruptions at active BWP switching Active BWP switching delay | No
TCI switching | TCI switching delay | FFS

## Slide 3: Background - II
RAN4 already agreed to the following during this meeting.
Requirements | Comments | Is requirement needed?
RLM | Requirements for RLM, e.g., based on SSB, CSI-RS or both | FFS for PCell and/or PSCell
Link recovery procedures | Requirements for SSB-based and CSI-RS based beam failure detection and candidate beam detection | FFS for PCell and PSCell
Measurements requirements (time duration, number of cells, etc.) |  | FFS for L1-RSRP evaluation period. Needs further discussion for L3-RSRP evaluation period.
Measurement accuracy requirements |  | FFS for L1-RSRP Needs further discussion for L3-RSRP
MT timing related requirements | MT maximum receive timing difference MT transmit timing MT maximum transmit timing difference Timing Advance | MT transmit timing (Te and Tq) Timing Advance FFS: MT maximum receive timing difference MT maximum transmit timing difference
Switching time between MT and DU | --- | FFS
DU timing related requirements | 3 us requirement T_delta command | Yes (3 us requirement / cell phase synch) FFS for Tdelta command

## Slide 4: Way Forward - I
RAN4 agrees to define IAB RRM requirements based on the following table.
Requirements | Comments | Is requirement needed?
Cell reselection | Intra-frequency Inter-frequency | No
Handover |  | FFS
RRC Connection Mobility Control | RRC re-establishment Random access RRC release with redirection | Yes
SCell activation/deactivation delays |  | No
Interruptions related to SCells addition, release, activation, deactivation | Interruptions on serving cells due to any of the addition, release, activation, or deactivation procedures | No
PSCell addition/release delays |  | No
Active BWP switching | Interruptions at active BWP switching Active BWP switching delay | No
TCI switching | TCI switching delay | FFS

## Slide 5: Way Forward - II
RAN4 agrees to define IAB RRM requirements based on the following table.
Requirements | Comments | Is requirement needed?
RLM | Requirements for RLM, e.g., based on SSB, CSI-RS or both | FFS
Link recovery procedures | Requirements for SSB-based and CSI-RS based BFD and CBD | FFS
Measurements requirements (time duration, number of cells, etc.) |  | FFS
Measurement accuracy requirements |  | FFS
MT timing related requirements | MT transmit timing (Te and Tq) Timing Advance | Yes
 | MRTD MTTD | FFS
Switching time between MT and DU | --- | TBD in RAN4 RF session
DU timing related requirements | 3 us requirement | Yes
 |  | FFS
 | T_delta command |