## Slide 1: Way forward on SRS carrier switching RRM requirements
ZTE, Huawei, HiSilicon, MediaTek, Apple, Intel
3GPP TSG-RAN WG4 Meeting #92bis
Chongqing, China, 14 - 18 October, 2019
R4-1912838

## Slide 2: Background
Per WID RP-191601 “NR RRM enhancement in R16”, following requirements is to be specified
  RRM requirement of SRS carrier switching requirements for NR SA, NR-DC, EN-DC and NE-DC including
    Delay and interruption requirements of the following cases
      LTE SRS carrier switching impacting NR CC
      NR SRS carrier switching impacting LTE CC
      NR SRS carrier switching impacting NR CC

## Slide 3: Agreements during the meeting
Do not specify delay requirements of NR SRS carrier switching
Interruption time length (slots) shall depend on the SCS of aggressor and victim serving cells

## Slide 4: Open issues
Interruption requirements
  Option 1: define requirements for 900us NR SRS carrier switching time
  Option 2: define requirements for 900us and [TBD] NR SRS carrier switching time respectively
  Option 3: define requirements for any NR SRS carrier switching time if it is justified
  Option 4: Other option is not precluded.
  Note: Further check on SRS carrier switching time definition
    Whether the interruption depends on SRS switching time or pure RF tuning time
FFS Interruption duration and location for scenarios
  Interruptions on NR serving cells during NR SRS carrier switching in EN-DC, NE-DC, NR-DC and SA operation
  Interruptions on NR serving cells during LTE SRS carrier switching in EN-DC and NE-DC operation
  Interruptions on LTE serving cells during NR SRS carrier switching in EN-DC and NE-DC operation

## Slide 5: Open issues
Impact to E-UTRA measurement requirements, e.g intra/inter frequency measurement, RLM etc, due to NR SRS carrier switching
  Option 1 : In EN-DC and NE-DC operation, requirements relevant to E-UTRA measurements are impacted due to NR SRS carrier switching.
  Other options are not precluded
Impact on NR measurement requirements based on SSB/PBCH/CSI-RS, , e.g intra/inter frequency measurement, RLM etc, due to LTE SRS carrier switching
  Option 1: In EN-DC and NE-DC operation, requirements relevant to measurements on SSB/PBCH/CSI-RS are impacted due to LTE SRS carrier switching
  Other options are not precluded
Impact on NR measurement requirements based on SSB/PBCH/CSI-RS, e.g intra/inter frequency measurement, RLM etc, due to NR SRS carrier switching
  Option 1: In EN-DC, NE-DC, NR-DC and NR SA operation, requirements relevant to measurements on SSB/PBCH/CSI-RS are NOT impacted due to NR SRS carrier switching
  Other options are not precluded

## Slide 6: Open issues
Whether to differentiate sync and async case
  Option 1: define unified requirements for sync and async case
  Option 2: define separated requirements for synch and async case
FFS the additional impact on RRM requirements when LTE SRS switching and NR SRS switching are both configured for a UE in EN-DC and NE-DC operation is to be further investigated
  (e.g., can such requirements be based on combining the LTE SRS switching requirements and NR SRS switching requirements)

## Slide 7: WF on specification structure
Specification impact
    LTE SRS carrier switching impacting NR CC (in 38.133)
      EN-DC: NR PSCC and NR SCCs
      NE-DC: NR PCC and NR SCCs
    NR SRS carrier switching impacting LTE CC (in 36.133)
      EN-DC: LTE PCC and LTE SCCs
      NE-DC: LTE PSCC and LTE SCCs
    NR SRS carrier switching impacting NR CC (in 38.133)
      SA NR: NR PCC and NR SCCs
      NR-DC: NR PCC, NR PSCC, and NR SCCs

## Slide 8: WF
Companies are encouraged to bring further analysis on the open issues and other potential issues in the RAN4#93 meeting