## Slide 1: Draft WF on punctured channel
Charter Communications.
R4-1912868
3GPP TSG-RAN Working Group 4 (Radio) meeting #92bis
Chongqing, China, 14th– 18th Oct, 2019

## Slide 2: Background
In previous meetings, we have discussed various alternatives for emission mask considerations for NR-U with the goal and objective to generate a mask that provides fair co-existence with current incumbents in 5 GHz
  The results of our discussions was the approval of WF [1]. In this WF, there were several alternatives to address basic general spectrum emission mask for NR-U and Spectral Emission Mask with punctured channels
  In this WF, we will outline several scenarios for considerations with regards to NR-U Spectral Emission Mask with punctured channels and provide guidance in identifying the punctured channel limits to insure co-existence with incumbents in 5GHz

## Slide 3: WF on punctured channel – Option 1
As discussed in [R4-1911850], there are two mask proposals to captured emission limits at the punctured mask. These masks are shown below:
Figure 1a
Figure 2
Figure 1b

## Slide 4: WF on punctured channel – Option 1
RAN4 to agree in addressing NR-U punctured channel masks for co-existence with 5 GHz incumbents
RAN4 to agree to preliminary values for NR-U in the punctured area. These values can be revisit based on future simulation analysis.
  One punctured, limit at -25 dbr referenced to figure 1a
  Multiple punctures, limit -28dbr referenced to figure 1b and figure 2
  At the edge of the wide band mask, the floor limit drops t o -37 dbr and the out of band floor drops to -40 dbr referenced to figure 2
Companies are encouraged to provide simulations to provide limits in the punctured area for single punctured and multiple punctures

## Slide 5: WF on punctured channel – Option 2
Discuss the value of A – H and if point C and F are needed.

## Slide 6: WF on punctured channel – Option 2
Nokia proposal for values of A – H:

## Slide 7: WF on punctured channel – Option 3
Same as punctured spectrum mask in IEEE 802.11ax.

## Slide 8: Comparisons between Option 1 and 2
Options | 1 MHz | 5 MHz | 10 MHz | 20 MHz | 40 MHz
Opt 1 1 punctured mask | LE+1 mhz | LE + 5 MHz | LE + 5 MHz | LE + 20 MHz | LE + 40 MHz
 | -20dBr | - | -25 dBr | - | -
Opt 1 2-3 punctured mask | LE+1 MHz | LE + 5 MHz | LE + 5 MHz | LE + 20 MHz | LE + 40 MHz
 | -20 dBr | -25 dBr | - 28 dBr | - 28dBr | -28 dBr
Opt 2 | LE+ 1 MHz | LE + 5 MHz | LE + 5 MHz | LE + 20 MHz | LE + 40 MHz
 | - 20 dBr | - | -23dBr | -25 dBr | -28dBr
Option 3 | LE+ 1 MHz | LE + 5 MHz | LE + 5 MHz | LE + 20 MHz | LE + 40 MHz
 | - 20 dBr | - 20 dBr | - 20 dBr | - 20 dBr | - 20 dBr

## Slide 9: WF on punctured channel – UE and BS aspects
To accommodate carrier leakage, exception to the mask is needed (1 exception in 1MHz BW)
To accommodate the combination of image and ACLR a -25dBr floor can be considered for PC5 UEs in punctured channels

## Slide 10: References:
1- R4-1910535 WF on Emission Requirements for NR-U, Nokia