## Slide 1: WF on NR-U RX FRC
ZTE, Nokia
R4-1912872
3GPP TSG-RAN WG4 #92Bis
Chongqing, China, 10th Oct. - 18th Oct. 2019

## Slide 2: Background
  Some NR-U BS Rx requirements require new FRC(s) to be defined. FRC(s) parameters are critical to define Rx wanted signal and interfering signal configurations. NR BS Rx requirements are essential to finished Rel-16 NR-U WI.
  During RAN4#92 meeting, following proposals from Nokia [R4-1912338] and ZTE [R4-1911732] were submitted:
  Proposal: It is proposed to introduce new FRCs using PRB interleave approach for NR-U. [Nokia]
  Proposal 1: the PRB level interleave should also be adopted for NR-U which is similar as LAA. [ZTE]

## Slide 3
  Agreement:
    PRB level interleave should also be adopted for NR-U;
    use MCS index 4 and target coding rate = 308/1024 specified for NR BS RX REFSENS/ICS to NR-U BS RX REFSENS/ICS;
    use MCS index 16 and target coding rate = 658/1024 specified for NR BS RX Dynamic range to NR-U BS RX Dynamic range;
    Agreement for principle for FRC PRB index design:
    interleaved PRB should be equally spaced within BS transmission bandwidth configuration;
    interleave PRB frequency spanning should be over 80% of nominal channel bandwidth to meet ETSI regulatory requirement except for 10MHz.
 | SCS | FRC PRB index | PRB number
10MHz | 15KHz | N,N+5,N+10,..N+45, N={0,1,2,3,4,5,6} | 10
 | 30KHz | N,N+2, N+18 where N={0,1,2,3,4,5} | 10
 | 60KHz | N, N+1,N+2, N+4,N+10 where N={0} | 11
20MHz | 15KHz | N,N+10,N+20,..N+90 where N={0,1,2,3,...,15} | 10
 | 30KHz | N,N+5,N+10,..N+45 where N={0,1,2,3,4,5} | 10
 | 60KHz | N,N+2, N+18 where N={0,1,2,..,6} | 10
40MHz | 15KHz | N,N+10,N+20,...N+200 where N={0,1,2,3,4,...,15} | 20
 | 30KHz | N, N+10,...,N+90 where N={0,1,2,3,4,...,15} | 10
 | 60KHz | N,N+5,N+10,..N+45 where N={0,1,2,3,4,5} | 10
60MHz | 30KHz | N,N+8,N+16,...,N+152,N={0,1,2,...,9} | 20
 | 60KHz | N,N+8,N+16....,N+72,N={0,1,2,...,6} | 10
80MHz | 30KHz | N,N+10,N+20,...N+200 where N={0,1,2,3,4,...,16} | 20
 | 60KHz | N,N+10,N+20,..N+90 where N={0,1,2,3,...,15} | 10

## Slide 4: Work plan
    Target to:
    Finalize the NR-U RX REFSNES/ICS/Dynamic range requirement at the RAN4#93 meeting.

## Slide 5: References:
  [1]R4-1912338 Discussion on NR-U BS Rx requirements, Nokia
  [2]R4-1911732 Further discussion on NR-U BS RX RF requirement,ZTE