## Slide 1: WF on Transient period capability
Qualcomm Inc
3GPP TSG-RAN WG4 Meeting #93 R4-1912921
Chongqing, China, 14th – 18th Oct, 2019

## Slide 2: Background
In RAN4-92bis meeting, companies has presented
  test procedures and test parameters for testing the transient period capability [1,2]
  Location of the transient period when then capability is signaled [1,3]
  Proposals for the potential values for the capability [4]. These options are to be discussed further
Common understanding is that we can use an exclusion period equal to transient period capability for testing RMS EVM for DFT-spread waveform.
Some companies have concern on the testability for CP-OFDM waveforms.
Test parameters for the feature will be discussed and the open items will be listed in this WF.

## Slide 3: WF-1
Location of the transient period when a UE declares capability <10 usec:
  Currently if a transient period is symmetrically shared, it will still be symmetrically shared
  Currently if a transient period is on one side of a symbol boundary, it will still on that side of the symbol boundary
  The value of the transient period in the above Proposals will now be the transient period value that the UE supports according to its UE capability

## Slide 4: WF-2
Test parameters (Proposal for test parameters to be used for RMS EVM evaluation with power change):
  20 MHz BW to be used
  SCS of 15 kHz to be used
  Any modulation can be used
  An average EVM over 10 subframes to be used (FFS)
  Periodic power step to be used with 50% duty cycle and a power change every 14 symbols
  Power step to be achieved by changing number of RB allocation
  Long and long sub slots each with 14 symbols to be used

## Slide 5: WF-3
Window for EVM evaluation:
  EVM FFT window shall exclude all exclusion periods from the symbol duration to determine the FFT window for DFT-spread
  No extra margin to be added to the reported transient period for exclusion
  It is a common understanding that RMS EVM for DFT-spread waveform can be measured if the signaled capability is less or more than or equal to CP duration
  Companies are encouraged to define EVM FFT window location for each symbol for DFT-Spread and CP-OFDM waveforms.

## Slide 6: WF-4
Given the assumptions in the WF-1:3 slides:
  DFT-Spread can be used for the evaluation
  CP-OFDM to be included in the evaluation. Test procedure for CP-OFDM to be studied as well.
    For 10 usec transient period, if the FFT window only excludes CP the impact to RMS EVM to be studied.
Agreement: The benefit of the feature shall not be discussed further.

## Slide 7: Reference
[1] R4-1912460, Input to WF on Transient Period Capability, Skyworks Solutions Inc.
[2] R4-1912461, Test procedure for measuring the effect of transient period duration on EVM outside of transient for FR1, Qualcomm Incorporated, Keysight Technologies
[3] R4-1912458, Location of transient period with capability, Qualcomm Incorporated, Nokia, Ericsson, Nokia Shanghai Bell
[4] R4-1912462, Values for Transient Period Capability , Qualcomm Incorporated, Ericsson, Nokia, Nokia Shanghai Bell