## Slide 1: 3GPP TSG-RAN WG4 Meeting #92bis Chongqing , China, 26th – 30th Aug, 2019
ZTE...
WF on exclusion bands
R4-1912941

## Slide 2: Background
TX Exclusion band
The definition of TX exclusion band are defined in TS 25.113,TS 36.113,TS37.113,TS 37.114,TS 38.113. With minor difference, the definition is as below:
  Transmitter exclusion band: band of frequencies over which no tests of radiated immunity of a transmitter are made and is expressed relative to the carrier frequencies used (the carrier frequencies of the base stations activated transmitter(s)).
The requirements are captured below:
TS 25.113
  For UTRA FDD: Lower carrier frequency used - 12,5 MHz. to upper carrier frequency used + 12,5 MHz.
  For UTRA 3,84 Mcps TDD option: Lower carrier frequency used - 12,5 MHz. to upper carrier frequency used + 12,5 MHz.
  For UTRA 1,28 Mcps TDD option: Lower carrier frequency used - 4 MHz to upper carrier frequency used + 4 MHz.
  For UTRA 7,68 Mcps TDD option: Lower carrier frequency used - 25 MHz. to upper carrier frequency used + 25 MHz.
TS 36.113
  Lower carrier frequency used - 2.5 x BWChannel MHz to upper carrier frequency used + 2.5 x BWChannel MHz, where BWChannel is the channel bandwidth as defined in TS 36.104
TS 37.113
  No transmitter exclusion bands
TS 37.114
  No transmitter exclusion bands
TS 38.113
  No transmitter exclusion bands

## Slide 3: WF Agreement
Companies are encouraged to provide further analysis of TX exclusion bands:
  Verify if current EMC specs (MSR, AAS, NR) needs to be updated with the descriptions of Tx exclusion bands
  Clarify the relation among the Tx/Rx exclusion bands and their applicability to the Emission and RI requirements
    Clarify the the relationship between TX exclusion band used for RI tests and the deltaFOBUE used for the Emission test
  How to define the TX exclusion band for NR.

## Slide 4: References
[1] R4-1911065 Further discussion on protection for UE simulator receiver during RI test to OTA NR BS, ZTE
[2] 25.113
[3] 36.113
[4] 37.113
[5] 38.113