## Slide 1: WF on EIRP and EIS for n259
Huawei, HiSilicon
R4-1912977
3GPP TSG-RAN WG4 #92bis
Oct 14th – 18th, 2019
Chongqing, China

## Slide 2: Inputs for Peak EIRP
Peak EIRP: derivation of nominal, tolerance, and minimum values |  |  |  |  |  |  |  |  |  |  |  | 
Parameters | unit | Huawei (R4-1912512) |  | Qualcomm (R4-1911238) | Samsung (R4-1911445) |  | Apple (R4-1911513) |  | MediaTek (R4-1911597) | Sony, Ericsson (R4-1912330) |  | Average
 |  | Nominal | tolerance |  |  |  |  |  |  |  |  | 
Pout per element | dBm | 11.5 |  | 10 | 10.5 |  | 13 |  | 10.5 | 11 |  | 
# of antennas in an array |  | 4 |  | 4 | 4 |  | 4 |  | 4 | 4 |  | 
Total conducted power per polarization | dBm | 17.5 | -1 |  | 16.5 |  | 19 | -1 | 16.5 | 17 |  | 
Avg antenna element gain | dBi | 4 | 0 | 3.5 | 4.5 |  | 4 |  | 3.3 | 5.5 |  | 
Antenna rolloff loss versus frequency | dB | -1.5 | 0 |  | -1.5 |  | -3 |  | -1.6 | 1.5 |  | 
Realized antenna array gain | dBi | 8.5 |  |  | 9 |  | 7 | 0 | 7.7 | 9.5 |  | 
# of chains |  |  |  | 2 |  |  |  |  |  |  |  | 
Polarization gain | dB | 2 | -1 |  | 2.8 |  | 2.8 |  | 2.5 | 2.5 |  | 
Mismatch and transmission line loss including load pull | dB | -2 | -0.7 |  | -2 |  | -2.3 |  | -1.5 | 1 |  | 
Beam forming loss (phase shifter and amplitude error) | dB | -0.5 | -0.25 |  | -0.25 |  | -1 |  | -1.4 | 1 |  | 
Finite beam table | dB | -0.1 | 0 |  | -0.25 |  |  |  | 0 | 0 |  | 
Beam forming loss (one beam table fits all) | dB | -0.25 | 0 |  | -0.25 |  |  |  | -0.5 | 0 |  | 
Form factor integration losses | dB | -2.5 | -1 |  | -3 |  | -4 |  | -5 | 2.5 | 1 | 
Total implementation loss (nominal) | dB | -5.35 |  | 4.3 | 5.75 |  | 7.3 | 3.3 |  | 4.5 |  | 
Total implementation loss (worst case) | dB |  | -8.3 |  |  | -8.2 |  |  |  | 5.5 |  | 
Packaging Loss |  |  |  | 6.7 |  |  |  |  |  |  |  | 
Peak EIRP (Nominal) | dBm | 22.65 |  |  |  |  | 21.5 |  |  | 24.5 |  | 
Tolerance (+/-) | dB |  | 3.95 |  |  | 3.45 |  |  |  | 4 |  | 
Peak EIRP (Minimum) | dBm | 18.7 |  | 17.5 | 19.1 |  | 17.2 |  | 18.3 | 20.5 |  | 18.7

## Slide 3: Inputs for Peak EIS
Peak EIS: derivation of minimum values |  |  |  |  |  |  |  | 
Parameter | Unit | Huawei (R4-1912512) | Qualcomm (R4-1911238) | Samsung (R4-1911445) | Apple (R4-1911513) | MediaTek (R4-1911597) | Sony, Ericsson (R4-1912330) | Average
Band number |  | n259 |  |  |  |  |  | 
Frequency range | GHz | 39.5 – 43.5GHz |  |  |  |  |  | 
SNR requirement | dB | -1 |  |  |  |  | -1 | 
Implementation margin |  |  |  |  |  |  | 2 | 
Bandwidth | MHz | 50 | 50 | 50 | 50 | 50 | 50 | 
Thermal noise | dBm/Hz | -174 |  | -174 | -174 | -174 | -174 | 
Noise Figure | dB | 12 | 12 | 11.6 | 12 | 11.5 | 11 | 
Number of antenna in an array |  | 4 | 4 | 4 |  | 4 | 4 | 
Array gain | dB | 6 |  | 4.5 |  | 6 | 5.5 | 
Element gain | dBi | 4 | 3.5 | 4.5 |  | 3.3 | 4.5 | 
realized array gain |  |  |  |  | 7 |  |  | 
# of chains |  |  | 2 |  |  |  |  | 
Diversity gain | dB | 0 |  | 0 |  | 0 | 0 | 
Antenna gain roll-off over frequency | dB | -1.5 |  | -1.5 |  | -1.6 | -1.5 | 
Mismatch and transmission line loss |  |  | -3 |  | -3 |  |  | 
Beamforming loss | dB | -0.25 |  | -0.25 | -1.6 | -1.5 | -1.5 | 
Total insertion loss | dB | -9.5 |  | -8.2 | -10.6 | -8 | 3 | 
Form factor integratation losses |  |  | -3 |  | -6 |  | 3.5 | 
REFSENS | dBm | -84.8 | -85.6 | -84.5 | -82.4 | -84.7 | -85.5 | -84.7

## Slide 4: Way forward
Based on inputs from [1]-[6], averaging method is proposed to define the PC3 minimum peak EIRP, EIS requirements for n259:
  Minimum peak EIRP: 18.7dBm
  Minimum peak EIS: -84.7dBm/50MHz

## Slide 5: Reference
[1] R4-1912512, UE RF requirements for n259, Huawei, HiSilicon, RAN4 #92bis
[2] R4-1911238, n259 peak EIRP and REFSENS Budget, Qualcomm, RAN4 #92bis
[3] R4-1911445, Link budget analysis for n259, Samsung, RAN4 #92bis
[4] R4-1911513, Derivation of peak EIRP and REFSENS for band n259, Apple, RAN4 #92bis
[5] R4-1911597, n259 PC3 minimum peak EIRP and REFSENS link budgets, MediaTek, RAN4 #92bis
[6] R4-1912330, Link budget for n259, Sony, Ericsson, RAN4 #92bis