## Slide 1: WF on n39 AMPR Values
Qualcomm Inc, Intel
3GPP TSG-RAN WG4 NR #92-Bis
Chongqing, China, 14th - 18th Oct 2019
R4-1913038

## Slide 2: Background
n39 band has supporting BWs greater than 20MHz, but no AMPR or RB restriction requirement
Companies were encouraged to provide simulations and measurements for B39 coexistence for channel BWs 25Mhz, 30MHz, and 40MHz so requirements could be completed by RAN4#92-Bis [1].
2 companies have provided results [2], [3].
It was agreed through offline discussions to use the results of [2] for 25MHz and 30MHz channel BWs and results of [3] for 40MHz channel BWs.

## Slide 3: Plan
Bring CR to add n39 AMPR next meeting
Introduce new NS flag for n39 AMPR in Table 6.2.3.1-1
Use Agreed AMPR values in subclause 6.2.3.X
Update coexistence table to reflect no RB restriction requirement and coexistence limit for 25MHz, 30MHz, and 40MHz BWs because of AMPR
Specify additional spurious emission requirements in subclause 6.5.3.3.X

## Slide 4: Emission Requirements
Band 39 is not wide enough for a 5MHz protection region and 40MHz channel BW.
AMPR for 40MHz is defined without the 5MHz guard band.
Protected band | Frequency range (MHz) |  |  | Maximum Level (dBm) | MBW (MHz) | NOTE
Frequency range | 1805 | - | 1855 | -40 | 1 | 1
Frequency range | 1855 | - | 1880 | -15.5 | 5 | 1, 2, 3
NOTE 1: This requirement is applicable for carriers with aggregated channel bandwidths confined in 1885-1920 MHz for 25MHz and 30MHz channel BWs, and 1880-1920 MHz for 40MHz channel BW. NOTE 2: The requirement also applies for the frequency ranges that are less than FOOB (MHz) in Table 6.6.3.1-1 and Table 6.6.3.1A-1 from the edge of the channel bandwidth. NOTE 3: For these adjacent bands, the emission limit could imply risk of harmful interference to UE(s) operating in the protected operating band. |  |  |  |  |  | 

## Slide 5: Proposal for 25MHz and 30MHz channel BWs
AMPR values with 5MHz guard band.
Qualcomm would like to increase BPSK, QPSK AMPR values to 4dB as highlighted.
BW | Region 1 |  | Region 2 |  | 
 | RBstart | A-MPR | RBstart | LCRB | A-MPR
25MHz | ≤LCRB - 5MHz/12/SCS | A1 | ≤20MHz/3/12/SCS | ≤1.44 MHz/12/SCS | A2
 |  |  |  | ≤3.6 MHz/12/SCS | A3
30MHz | ≤LCRB - 5MHz/12/SCS | A4 | ≤25MHz/3/12/SCS | ≤1.44 MHz/12/SCS | A5
 |  |  |  | ≤3.6 MHz/12/SCS | A6
 |  | A-MPR (dB) |  |  |  |  | 
 |  | A1 | A2 | A3 | A4 | A5 | A6
DFT-s-OFDM | BPSK | ≤ 2.5 4 | ≤ 2 | N/A | ≤ 3.5 4 | ≤ 2 | N/A
 | QPSK | ≤ 3.5 5 | ≤ 2 | N/A | ≤ 4 5 | ≤ 2 | N/A
 | 16QAM | ≤ 4 5 | ≤ 2.5 | N/A | ≤ 4.5 5 | ≤ 2.5 | N/A
 | 64QAM | ≤ 4 5 | ≤ 2.5 | N/A | ≤ 4.5 5 | ≤ 2.5 | N/A
 | 256QAM | ≤ 4 5 | ≤ 2.5 | N/A | ≤ 4.5 5 | ≤ 2.5 | N/A
CP-OFDM | QPSK | ≤ 5.5 6.5 | N/A | ≤ 3 | ≤ 6 6.5 | N/A | ≤ 3
 | 16QAM | ≤ 5.5 6.5 | N/A | ≤ 3 | ≤ 6 6.5 | N/A | ≤ 3
 | 64QAM | ≤ 5.5 6.5 | N/A | ≤ 3 | ≤ 6 6.5 | N/A | ≤ 3
 | 256QAM | ≤ 5.5 6.5 | N/A | ≤ 3 | ≤ 6 6.5 | N/A | ≤ 3
NOTE 1: The backoff applied is max (MPR, A-MPR) where MPR is defined in Table 6.2.2-1. |  |  |  |  |  |  | 

## Slide 6: Proposal for 40MHz channel BWs
AMPR values without 5MHz guard band
Intel would like to add the missing A-MPR values in A3 and A6 and change the condition of RBstart of A2 as highlighted.
Modulation/Waveform | A1 | A2 | A3 | A5 | A6
 | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner | Outer/Inner
DFT-s-OFDM PI/2 BPSK | ≤ 11 | ≤ 7 | ≤ 3 | ≤ 5 | ≤ 2
DFT-s-OFDM QPSK | ≤ 11 | ≤ 7 | ≤ 3 | ≤ 5 | ≤ 2
DFT-s-OFDM 16 QAM | ≤ 11 | ≤ 7 | ≤ 3 | ≤ 5 | ≤ 2
DFT-s-OFDM 64 QAM | ≤ 11 | ≤ 7 | ≤ 3 | ≤ 5 | ≤ 2
DFT-s-OFDM 256 QAM | ≤ 11 | ≤ 7 | ≤ 3 | ≤ 5 | ≤ 2
CP-OFDM QPSK | ≤ 12 | ≤ 8 | ≤ 4.5 | ≤ 5 | ≤ 3.5
CP-OFDM 16 QAM | ≤ 12 | ≤ 8 | ≤ 4.5 | ≤ 5 | ≤ 3.5
CP-OFDM 64 QAM | ≤ 12 | ≤ 8 | ≤ 4.5 | ≤ 5 | ≤ 3.5
CP-OFDM 256 QAM | ≤ 12 | ≤ 8 | ≤ 4.5 | ≤ 5 | ≤ 3.5
NOTE 1: The backoff applied is max(MPR, A-MPR) where MPR is defined in Table 6.2.2-1 NOTE 2: Outer and inner allocations are defined in clause 6.2.2 |  |  |  |  | 
Channel BW | RBStart*12*SCS (MHz) | LCRB*12*SCS (MHz) | A-MPR
40MHz | ≤ 4.32 | > 0 | ≤ A1
 | >4.32, ≤10.44 | ≤ 10.8 | ≤ A3
 | >10.44 4.32, ≤18 | > 10.8 | ≤ A2
 | >18, ≤31.68 | > max(31.68 – Rbstart*12*SCS , 0) | ≤ A6
 | >31.68 | > 0 | ≤ A5

## Slide 7: References
R4-1909960, “n39 Coexistence Issue and Missing AMPR”, Qualcomm Inc., RAN4#92, Ljubljana, Slovenia, August 2019
RAN4-1911028 “A-MPR for n39”, Intel, Chongqing, China, October 2019
RAN4- 1912557 “n39 AMPR”, Qualcomm Inc., Chongqing, China, October 2019

## Slide 8: Example Plots showing regions
40MHz, 25MHz, 30MHz plot examples from contributed papers