## Slide 1: Way forward on NR mobility enhancement
Intel
3GPP TSG-RAN4 Meeting #92bis
Chongqing, China, 14– 18 October, 2019
R4-1911041
Document for: Approval

## Slide 2: Handover delay and interruption of handover with simultaneous Rx/Tx with source and target cells
Definition of HO delay will be split into two parts:
Delay (1): from HO command to PRACH preamble transmission
D1 = TRRC_procedure + Tsearch + TIU + TUE_process + T∆
Definitions of each term is same as that in the existing handover RRM requirements. Corresponding interruption in delay (1):
For intra-frequency:
  Case 1 (BWsource ≠ BWtarget): FFS and reuse existing [DCI based BWP switching delay] requirement as starting point. Companies are encouraged to provide analysis on interruption time associated with different UE Rx/Tx architecture.
  Case 2 (BWsource = BWtarget): FFS
For inter-frequency: reuse existing NR PSCell/SCell addition interruption requirement, i.e. follow Table 8.2.4.2.1-1 for inter-band synchronous and Table 8.2.4.2.1-2 for intra-band synchronous (1 additional slot is allowed for asynchronous case in inter-band asynchronous ).
Delay (2) on source release: Start point is FFS. Pending RAN2, existing PSCell release requirement can be reused if this is triggered by RRC
UE is not required to perform mobility purpose measurement after receiving HO command and before the source release is complete

## Slide 3: Agreements on conditional handover
The starting point of the CHO procedure is from the end of the last TTI containing the RRC command carrying the CHO command. Handover delay is split into the following phases
Phase 0: CHO command RRC processing
Phase 1: Measurement
Phase 2: HO execution
From test case perspective, RAN4 shall follow RAN2 agreement that CHO execution does not trigger measurement report.
Handover delay is defined as:
DCHO = TRRC_1 + Tmeasure + TIU + TRRC_2 + Tprocessing + T∆
Where:
TRRC_1: First segment of RRC processing time to process CHO command.
TRRC_2: Second segment of RRC processing time, starts after UE realizes the condition is met and identity of target cell is determined
Tmeasure: from the end of CHO RRC command is successfully decoded (no later than TRRC_1) until [UE realizes a handover condition for CHO is met].
Tprocessing: is time for UE processing (same as existing requirement).
T∆: is time for fine time tracking and acquiring full timing information of the target cell (same as existing requirement).

## Slide 4: Agreements on conditional PSCell addition/change
Conditional handover requirements are needed for at least conditional handover and PSCell addition/change for standalone NR and standalone LTE. Depending on discussion in RAN2, requirements for interRAT PSCell addition in 36.133 or other requirements may be needed