## Slide 1: 3GPP TSG-RAN WG4 Meeting #92bis Chong Qing, China, 14th - 18th Oct., 2019
Huawei, HiSilicon
WF on Rel-16 feMobility RRM
R4-1911902

## Slide 2: Conditional handover
The handover delay DCHO in CHO is defined from the time when handover condition is met from UE perspective to the time when the first PRACH preamble is transmitted.
Handover delay and interruption are specified as
  DCHO= Tinterrupt_CHO
  Where,
  -Tinterrupt_CHO =Tprocess_time+ Tiu+ 20
  -Tprocess_time: UE processing time, including delay for RF retuning, derive target eNB specific keys, configure security algorithm to be used in target cell.
  -TIU is the interruption uncertainty in acquiring the first available PRACH occasion in the new cell. TIU can be up to 30 ms.

## Slide 3: non-split dual active protocol stack solution
The handover delay is defined as when the UE receives a RRC message from source cell implying handover the UE shall be ready to start the transmission of the new uplink PUSCH channel on the target cell within Dhandover seconds from the end of the last TTI containing the RRC command.
Dhandover= RRC procedure delay+ Tsearch+Tiu+20ms
The following interruption is allowed during the time between end of the last TTI containing the RRC command on the old PDSCH and the UE shall be ready to start the transmission of the new uplink PUSCH channel on the target cell
  no interruption is allowed for both intra-frequency synchronous and asynchronous deployment when the bandwidth of target and serving cell is the same.
  5ms interruption is allowed for both intra-frequency synchronous and asynchronous deployment when the bandwidth of target and serving is different.
  1ms interruption is allowed for both synchronous and asynchronous inter-frequency deployment.