## Slide 1: WF on channel raster and sync raster for unlicensed band n47 and licensed bands
vivo, CATT, LGE
3GPP TSG-RAN WG4#92bis Meeting R4-1912880
Chongqing, China, 14-18 Oct, 2019

## Slide 2: Background (1)
Different companies have different channel raster and sync raster designs for NR-V2X with below contributions:
  R4-1911166, “Further discussion on system parameters for NR V2X band n47” (vivo)
  R4-1911167, “Discussion on system parameters for NR-V2X licensed bands” (vivo)
  R4-1911459, “Discussion on channel arrangement of NR V2X” (LG Electronics France)
  R4-1910973, “Discuss on the channel arrangement design for 5G V2X UE” (CATT)
  R4-1910974, “TP for channel arrangement design for 5G V2X UE” (CATT)

## Slide 3: Background(2)
Channel raster for LTE V2X
Channel raster for DSRC
Other regulation related to 5.9GHz[1]
Figure2: DSRC channel allocation(cited from the internet)
47 | 5855 | 54540 | 54540 - 55239 | 5855 | 54540 | 54540 – 55239
E-UTRA Operating Band | Downlink |  |  | Uplink |  | 
 | FDL_low (MHz) | NOffs-DL | Range of NDL | FUL_low (MHz) | NOffs-UL | Range of NUL
Table1: E-UTRA channel numbers

## Slide 4: Background(3)
According to RAN1’s agreements in RAN1 AH1901[2]:
  The frequency location for S-SSB is (pre-) configured
    o Note: it implies that there is no intended hypotheses detection in frequency location of S-SSB performed by the UE for a carrier in a given band
    o Note: the potential frequency locations for the (pre-)configured frequency location may be restricted, up to RAN4

## Slide 5: Channel raster for band n47
Channel raster for n47 should be based on general channel raster definition in NR which is SCS based channel raster.
  The co-existence of LTE V2X when the channel is shared should be considered and frequency shift is FFS.

## Slide 6: Sync raster for band n47
Do not define sync raster for NR V2X band n47.
Send LS to RAN1 and RAN2 to inform:
  RAN4 does not define sync raster for NR V2X unlicensed bands.

## Slide 7: Channel raster for licensed bands
Reuse NR Uu channel raster for sidelink in the NR V2X licensed bands.
  The co-existence of LTE Uu when the channel is shared should be considered and frequency shift is FFS.

## Slide 8: Sync raster for licensed bands
Do not define sync raster for SL interface in NR V2X licensed bands.
Send LS to RAN1 and RAN2 to inform:
  RAN4 does not define sync raster for NR V2X licensed bands.

## Slide 9: References
[1] Frequency bands for V2X, ACEA (https://www.acea.be/uploads/publications/ACEA_position_paper-Frequency_bands_for_V2X.pdf)
[2] R1-1901448, Offline discussion summary of AI 7.2.4.1.3 V2X SL Synchronization, CATT, RAN1-AH1901