## Slide 1: WF on NR V2X RRM requirement
LG Electronics
3GPP TSG-RAN WG4 #93 Meeting
Reno, US, 18th – 22nd Nov., 2019
R4-1913516

## Slide 2
Do not consider EN-DC and NE-DC for NR V2X RRM requirements in Rel-16.
Apply same NR V2X RRM requirements for both FR1 ITS band and a dedicated licensed band
Scenario for RRM requirements

## Slide 3
UE Tx Timing
Do not consider gNB in FR2 as synchronization reference source in Rel-16 NR V2X

## Slide 4
Define SyncRef UE identification time with 2 SLSS periods in FR1
RAN4 does not specify how to solve in following scenarios timing misalignment may exist between UEs communicating on SL
  UE1 and UE2 synced to two different gNBs, but the 2 gNBs are with different timing
  UE1 and UE2 synced to two different eNBs, but the 2 eNBs are with different timing
  UE1 synced to eNB, UE2 synced to gNB, eNB and gNB are with different timing
Synchronization(1/3)

## Slide 5
Dropping Rate for selection/reselection of NR V2X synchronization reference source
  When GNSS synchronization reference source is configured as the highest priority
    UE is synchronized to GNSS directly,
      UE shall not drop any V2X SLSS and data transmission
    UE is synchronized to a SyncRef UE that is synchronized to GNSS directly or in-directly
      UE shall not drop any V2X data transmission
      UE is allowed to drop a maximum of 20% of its SLSS transmissions during Tdetect,SyncRef UE_V2X of 1.6 seconds at SCH Es/Iot ≥0 dB
    In other case
      Same as case that serving cell/PCell synchronization reference source is configured as the highest priority
  When serving cell/PCell synchronization reference source is configured as the highest priority
    UE is allowed to drop a maximum of 4% of its V2X data and SLSS transmissions during Tdetect,SyncRef UE_V2X of 8 seconds at SCH Es/Iot ≥ 0 dB
    UE is allowed to drop up to 2 slots of its V2X data reception per PSBCH monitoring occasion and overall drop rate shall not exceed 0.2% of its V2X data reception during Tdetect,SyncRef UE_V2X
Synchronization(2/3)

## Slide 6
Evaluation time for initiation/cease SLSS Tx
  gNB as synchronization source
  GNSS as synchronization source
    Reuse the evaluation time of gNB when gNB is serving cell and UE is in-coverage of gNB
    Reuse the evaluation time of eNB when eNB is serving cell and UE is in-coverage of eNB
  SyncRef UE as synchronization source
    320ms(2 times of S-RSRP measurement period)
Synchronization(3/3)
DRX cycle | Tevaluate,NR SLSS [s] (number of DRX cycles
No DRX | max(2x200ms, ceil( (5+4) x Kp) x SMTC period)Note 1 x CSSFintra
DRX cycle≤ 320ms | max(2x200ms, ceil(1.5x (5+1) x Kp) x max(SMTC period,DRX cycle)) x CSSFintra
DRX cycle>320ms | ceil( (5+1) x Kp ) x DRX cycle x CSSFintra
NOTE 1: If different SMTC periodicities are configured for different cells, the SMTC period in the requirement is the one used by the cell being identified | 

## Slide 7
SSB RSRP measurement
  Measurement accuracy
    Reuse the same accuracy from NR Uu
    Side condition is SINR ≥ 0dB
  Measurement period
    160ms for SCS of 15kHz, 30kHz and 60kHz if SLSS periodicity is smaller than or equal to 160ms
Autonomous Resource Reselection measurement
  Make agreeable simulation assumption of L1 SL-RSRP measurement before RAN4#94 meeting through e-mail discussion and encourage interesting companies to provide simulation results in RAN4#94 to define measurement accuracy and side condition
Congestion Control measurement
  Reuse LTE-V2X S-RSSI measurement accuracy for NR V2X congestion control measurement
Measurement

## Slide 8
When NR Uu BWP switching, and NR V2X SL BWP configuration/ reconfiguration (if supported) are performed simultaneously
  Not define the interruption requirement and NR Uu BWP switching delay is not impacted
Interruption

## Slide 9
Work Split for draft CR/CR
Section | Company
12.1 Introduction | LG Electronics
12.2 UE Transmit Timing | Huawei
12.3 Initiation/Cease of SLSS Transmissions | MediaTek
12.4 Selection/Reselction of V2X Synchronization Reference Source | Qualcomm
12.5 [Autonomous Resource Selection/Reselection measurements] | Qualcomm
12.6 [Congestion Control measurements] | Qualcomm
12.7 Interruption | CATT
12.8 [Reliability of GNSS signal] | LG Electronics
10.3 V2X measurements | MediaTek