## Slide 1
3GPP TSG-RAN WG4 Meeting #93 R4-1913870
Reno, USA, 18th – 22nd Nov, 2019
Agenda Item: 9.17.2.2
WF on UE demodulation for NR HST
CMCC

## Slide 2: Agreements
Maximum Doppler
    for HST-SFN with 30KHz SCS, the DL maximum Doppler frequency is 1500Hz
    for HST-SFN with 15KHz SCS, the DL maximum Doppler frequency is 712 Hz
    for HST single tap with 15 KHz SCS, the DL maximum Doppler frequency 1250 Hz

## Slide 3: Agreements
MCS
    For Rank = 2, MCS 13 is considered
    For Rank = 1, MCS 17 is considered
Antenna connection
    both 2x2 and 2x4 are considered
    applicability rule can be considered

## Slide 4: Agreements
Signaling
    For HST-SFN, the NW assistance signalling is introduced in a similar way as that of LTE HST, which is a per-cell signalling and could be broadcast in system information and also provided in the handover command.
    For HST single tap, it is not necessary to introduce the network assistance signalling