## Slide 1: WF on NR-U RRM Requirements (all agreements in RAN4#93)
Ericsson, Qualcomm Inc.
3GPP TSG-RAN WG4 Meeting #93 R4-1915777
Reno, Nevada, USA, 18th – 22nd November, 2019
Agenda Item: 9.1.4

## Slide 2
Agreements from
Main Session and Ad Hoc Session

## Slide 3: Cell Reselection
Mm,max is
  [16] for 0.32 sec DRX cycle,
  [4] for 2.56 sec DRX cycle.
FFS: At least one cell which is checked by the UE for cell re-selection on each frequency is such that it is not more than X dB weaker than the strongest cell on that frequency, and it also fulfills the reselection margins, where value of X is TBD

## Slide 4: RRC Release with Redirection
FFS UE behavior upon exceeding L1,max
FFS UE behavior upon exceeding L2,max

## Slide 5: RRC Re-establishment
FFS UE behavior upon exceeding K1,max and K2,i,max
FFS UE behavior upon exceeding K3,max

## Slide 6: SIB Reading in RRC Re-establishment, RRC Release with Redirection, and Paging Interruption Requirements
SIB reading in RRC re-establishment, RRC release with redirection, and paging interruption requirements
  Further study SIB reading time including MIB and SIB1 decoding time
    Option 1: SIB reading time 1280 ms
    Other options are not precluded
  FFS whether soft combining or single shot detection without soft combining shall be applied
The above also addresses extending the time needed to acquire the MIB and SIB1 due to LBT failure in paging interruption requirements, based on the simulation study (simulation assumptions are to be further discussed off-line)

## Slide 7: HO Requirements
L1,max and L´1,max
  Do not define
L2,max
  Do not define
L3,max
  Do not define
Clarify UE behavior (refer to RAN2 spec and T304 timer) when UE cannot transmit in UL

## Slide 8: Active BWP Switching
Active BWP switching delay
  Rel-15 requirements are reused
  No changes to Rel-15 requirements wording (i.e. UE shall be able to receive PDSCH and shall be able to transmit PUSCH in the first available DL or UL slot respectively after BWP switching)
UL BWP switching triggered by consistent UL LBT failure
  FFS whether to introduce RRM requirements for UL BWP switching triggered by consistent UL LBT failure

## Slide 9: Timing Reference Cell
Scenario B and C: if the current reference cell (i.e. PCell in Scenairo C or PSCell in Scenario B) is unavailable to UE after certain number of DL SSB detection attempts, then the UE can take any activated SCell with SSB available at the UE within this CG as the new reference cell
FFS: The UE applies one shot timing adjustment

## Slide 10: SCell Activation: Interruption Window
Confirm RAN4#92-bis agreement on extending THARQ compared to Rel-15
  The exact wording is TBD
  FFS whether the extension depends on UE capability

## Slide 11: RLM: in-sync
FFS whether and how to take into account COT and LBT failures in the RLM requirements
Lin,max
  Option 1:
    Lin,max = [7] for Max(TDRX,TSSB)≤40 where TDRX=0 for non-DRX
    Lin,max = [5] for 40<Max(TDRX,TSSB)≤320
    Lin,max = [3] for TDRX>320
FFS whether for longer DRX cycles > 640, an additional criterion applies, to limit the acceptable period of consecutive LBT failures to [X] seconds

## Slide 12: RLM: out-of-sync
Extend the out-of-sync evaluation period
  Option 1: Out-of-sync evaluation period is scaled by a fixed factor of N (N > 1)
  Option 2: Same as for other measurements (out-of-sync evaluation is based on Lout, where Lout ≤Lout,max is the number of SSBs not available at the UE during TEvaluate_out_SSB)
    FFS if UE can distinguish whether signal is available for RLM out-of-sync

## Slide 13: RLM: QCL-ed SSBs
Option 1:
  UE is required to monitor at least one SSB from the set of SSBs that are QCLed with each other
Option 2:
  UE is required to monitor all SSBs from the set of SSBs that are QCLed with each other
Option 3:
  UE is required to monitor all SSBs regardless of QCL assumptions

## Slide 14: Independent Measurement Gap
Observation1:
  Independent gap patterns allow:
    Shorter measurement delays for both licensed and unlicensed bands,
    Fewer gap interruptions on both licensed or unlicensed serving cells, particularly if only one type of carrier needs gap based measurements
    Independent parameterization of gaps for NR and NR-U which can be matched to different deployment configurations (e.g. large versus small cells)
Observation 2:
  Bottlenecks for defining independent gap patterns in Rel-16:
    UE capabilities need to be carefully considered to ensure that as many as possible UE can support independent gap patterns
    UE capabilities may become more complicated
    time shortage for the NR-U WI core part
Do not consider an independent gap pattern for unlicensed bands in Rel-16

## Slide 15: Condition for NR-U Undetectable Cell to Remain Known in RRC_CONNECTED
Confirmed agreement:
  For NR-U extend the duration of the condition of the cell to remain known in RRC_CONNECTED state from 5 seconds to X seconds
    X = 8 sec

## Slide 16: PBCH Reading at SSB Index Detection
FFS whether PBCH reading is required for SSB index identification in FR1 for NR-U

## Slide 17: Inter-Frequency Measurements
Procedure | Rel-15 samples | Maximum number of DL LBT failures |  | 
 |  | Parameter name | Parameter value | Condition
PSS/SSS detection, with gaps | 8 | LPSS/SSS,gaps,max | FFS | Max(TDRX,TSMTC, MGRP)≤40
 |  |  | FFS | 40<Max(TDRX,TSMTC, MGRP)≤320
 |  |  | FFS | TDRX>320
Time index detection, with gaps | 3 | Lind,gaps,max | 5 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 3 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 2 | TDRX>320
Measurement, with gaps | 8 | Lmeas,gaps,max | 12 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 8 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 5 | TDRX>320
FFS: how to address the consecutively missing SSBs

## Slide 18: EN-DC SFTD
NLBT-fail,max
specify that time difference between frame timing acquisition for PCell and PSCell, respectively, shall fulfill |t1-t2| < max(200 ms, 5*TSMTC), where TSMTC is the PSCell SMTC period
  RAN4 will not define test case for this requirement in Rel-16
Condition | NLBT-fail,max
max(TDRX,TSMTC)≤40 | [7]
40<max(TDRX,TSMTC)≤320 | [5]
TDRX > 320 | [3]

## Slide 19: Inter-RAT SFTD
UE behavior upon exceeding Tmeasure_SFTD_LBT_max: UE shall stop the search
  FFS whether UE abandons the measurement
  Tmeasure_SFTD_LBT_max = k× Tmeasure_SFTD1, k=TBD≤10
Reporting delay: based on that the UE shall be capable of reporting SFTD at earliest upon having received the SFTD measurement configuration, and at latest X ms after the start of a period with Y consecutively available SSBs. Values of X and Y depend on the configuration in use and are FFS.
  Rel-15 side conditions apply

## Slide 20: RSSI and Channel Occupancy: Requirements Scope
RAN4 to define:
  intra-frequency (on PCC, PSCC, and SCC), inter-frequency, and inter-RAT measurement requirements for RSSI and channel occupancy
    FFS the exact definition of intra-/inter-frequency
  intra-frequency, inter-frequency, and inter-RAT measurement accuracy requirements for RSSI and channel occupancy
  measurement reporting mapping for RSSI
    FFS whether measurement report mapping is needed for channel occupancy, depending on its definition to be decided by other groups
  clarify measurement gap patterns applicability for RSSI and channel occupancy measurements:
    All Rel-15 measurement gap patterns applicable for FR1 measurements are also applicable for RSSI and channel occupancy measurements on carrier frequencies with CCA
    FFS: for gap-based measurements if RAN1 defines the measurement duration longer than 5 ms

## Slide 21: Measurement Accuracy for RSRP/RSRQ/SINR/L1-RSRP
Rel-15 measurement accuracy requirements apply
  How to address the applicability in the specification should consider the outcome of the email discussion

## Slide 22
Further Agreements

## Slide 23: RRC Re-establishment
UE behavior:
  Option 1:
    UE behavior is based on K1,max, K2,i,max, and KSI,max (FFS K3,max)
      KSI,max is the maximum time for SI reading
  Option 2:
    Use the existing RAN2 procedure upon the expiring of the T311 timer
  Option 3:
    UE behavior is based on K1,max, K2,i,max, and KSI,max (FFS K3,max) and timer T311, whichever comes first

## Slide 24: SI Reading in RRC Release with Redirection, RRC Re-establishment, and Paging Interruption Requirements
Option 2: SI reading time is derived based on the necessary number of samples and the LBT impact
  Number of PBCH samples for MIB is 5
  Number of PDSCH samples for SIB1 is based on simulation results with 95% of decoding success rate, assuming:
Parameters | Unit | Value
Channel bandwidth | MHz | 20
SCS | kHz | 15
Number of transmitter antennas |  | 1
Number of receive antennas |  | 2
Allocated resource blocks for PDSCH |  | 24 (allocated in the lower edge of the carrier)
MCS index |  | 4
Modulation |  | QPSK
Target Coding Rate |  | 0.33
Number of control symbols |  | 2
PDSCH mapping type |  | Type A
Information Bit Payload |  | 
For slots with RMSI | Bits | 1864
Number of Code Blocks per slot |  | 1
Binary Channel Bits Per slot |  | 
For slots with RMSI | Bits | 6048
Side condition (PDSCH SNR) | dB | -6
Propagation channel model |  | AWGN, TDLA30-10, TDLB100-400, TDLC300-100
Receiver assumption |  | Single shot detection Soft-combining (2, 4 and 8 samples)
SIB1 transmission period | ms | 20
Metric |  | 95% of SIB1 acquisition success rate
Derived based on the PDSCH DMRS assumption: dmrs-TypeA-Position=2, dmrs-Type=1, dmrs-AdditonalPositions=2, maxLength=1, Antenna port index: 1000, and Number of PDSCH DMRS CDM group(s) without data: 1. |  | 

## Slide 25: RLM
RLM requirements based on periodic CSI-RS (TCSI-RS) are to be defined in Rel-16
  Background: RAN1 agreed that CSI-RS-based RLM-RS both within and outside the SSB-based RLM measurement window (i.e., DRS transmission window) can be used for in-sync and out-of-sync evaluations (resolves FFS from previous agreement)

## Slide 26: Intra-Frequency Measurements
Procedure | Rel-15 samples | Maximum number of DL LBT failures |  | 
 |  | Parameter name | Parameter value | Condition
PSS/SSS detection, no gaps | 5 | LPSS/SSS,max | FFS | Max(TDRX,TSMTC)≤40
 |  |  | FFS | 40<Max(TDRX,TSMTC)≤320
 |  |  | FFS | TDRX>320
PSS/SSS detection for deactivated SCell, no gaps | 5 | LPSS/SSS,deact,max | FFS | Max(TDRX, measCycleSCell)≤40
 |  |  | FFS | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | FFS | TDRX>320
Time index detection, no gaps | 3 | Lind,max | 5 | Max(TDRX, TSMTC)≤40
 |  |  | 3 | 40< Max(TDRX, TSMTC)≤320
 |  |  | 2 | TDRX>320
Time index detection for deactivated SCell, no gaps | 3 | Lind,deact,max | 5 | Max(TDRX, measCycleSCell)≤40
 |  |  | 3 | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | 2 | TDRX>320
Measurement, no gaps | 5 | Lmeas,max | 7 | Max(TDRX, TSMTC)≤40
 |  |  | 5 | 40< Max(TDRX, TSMTC)≤320
 |  |  | 3 | TDRX>320
Measurement on deactivated SCell, no gaps | 5 | Lmeas,deact,max | 7 | Max(TDRX, measCycleSCell)≤40
 |  |  | 5 | 40< Max(TDRX, measCycleSCell)≤320
 |  |  | 3 | TDRX>320
PSS/SSS detection, with gaps | 5 | LPSS/SSS,gaps,max | FFS | Max(TDRX,TSMTC, MGRP)≤40
 |  |  | FFS | 40<Max(TDRX,TSMTC, MGRP)≤320
 |  |  | FFS | TDRX>320
Time index detection, with gaps | 3 | Lind,gaps,max | 5 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 3 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 2 | TDRX>320
Measurement, with gaps | 5 | Lmeas,gaps,max | 7 | Max(TDRX, TSMTC, MGRP)≤40
 |  |  | 5 | 40< Max(TDRX, TSMTC, MGRP)≤320
 |  |  | 3 | TDRX>320
FFS: whether and how to address the consecutively missing SSBs

## Slide 27: L1-RSRP
L1,max:
  L1,max=7 for Max(TDRX,TSSB) ≤ 40 where TDRX=0 for non-DRX
  L1,max=5 for 40 < Max(TDRX, TSSB) ≤ 320
  L1,max=3 for TDRX > 320
For periodic and aperiodic L1-RSRP reporting, the L1-RSRP reporting delay reuses the Rel-15 reporting delay
  Option 1: reuses the Rel-15 reporting delay
  Option 2: is extended to account UL LBT failure (e.g., similar to semi-persistent)
For semi-persistent CSI reporting, L1-RSRP reporting delay for the last CSI is extended to account for UL LBT failures resulting in UE being not being able to transmit
  FFS how to extend the delay, where the maximum extension is
    Option 1: determined by RAN1/RAN2 specifications
    Option 2: is pre-defined
FFS: For semi-persistent CSI reporting with PUCCH,
  if UE cannot transmit HARQ-ACK on the MAC CE activation due to UL LBT failures, UE should not start the L1-RSRP measurement and reporting
  if UE cannot transmit HARQ-ACK on the MAC CE deactivation due to UL LBT failures, UE continues the L1-RSRP measurement and delay the L1-RSRP reporting. If UE does not receive deactivation command during the delay period, UE restart to transmit L1-RSRP. FFS how to extend the delay

## Slide 28: SCell Activation: Known SCell Definition
Extend the time before the reception of the SCell activation command from Rel-15 time TNR to time TNR-U
  Option 1: TNR-U = max([5+k] measCycleSCell, [5+k] DRX cycles), k=TBD>0 and k is a fixed number
  Option 2: do not extend

## Slide 29: SCell Activation Delay
THARQ
  Confirm RAN4#92-bis agreement on extending THARQ compared to Rel-15
    The exact wording is TBD
    FFS whether the extension depends on UE capability
TCSI_reporting
  Confirm RAN4#92-bis agreement on extending TCSI_reporting compared to Rel-15 (TCSI_reporting,ref) and also add the DL impact:
    TCSI_reporting = TCSI_reporting,ref +L4*TCSI-RS +CSI
      UE behavior upon exceeding L4,max (L4,max=TBD) is to abandon the SCell activation procedure
      CSI ≤ CSI,max
      FFS CSI,max
        Option 1: CSI,max is determined by RAN1/RAN2 specifications
        Option 2: CSI,max is a pre-defined value

## Slide 30: SCell Activation Delay (cont.)
Tactivation_time
  Tactivation_time is extended to compensate for signal occasions not available at the UE
  Known cell
    TFirstSSB+ Trs *L1+ X ms, if the SCell measurement cycle is ≤160ms
      FFS: “and HARQ≤TBD”
    TSMTC_MAX*(1+L2,1) + Trs*(1+L2,2)+ Y ms, if the SCell measurement cycle is >160ms
      FFS: “or HARQ>TBD”
  Unknown cell
    TSMTC_MAX*(2+L3,1) + Trs*(2+L3,2)+ Z ms, provided the SCell can be successfully detected in one attempt
  UE behavior upon exceeding L1,max, L2,1,max, L2,2,max, L3,1,max, and L3,2,max: abandon SCell activation procedure
  L1≤L1,max, L2,1≤L2,1,max, L2,2≤ L2,2,max, L3,1≤ L3,1,max, and L3,2≤ L3,2,max
    The exact definition of L1, L2,1, L2,2, L3,1, L3,2 is FFS

## Slide 31: SCell Deactivation
Confirm RAN4#92-bis agreement on extending THARQ compared to Rel-15
  The exact wording is TBD
  FFS whether the extension depends on UE capability

## Slide 32: Active TCI State Switching: Known State Requirements
RRC-based:
  LRRC,known,max =[2] for TSSB≤40 ms, LRRC,known,max =[1] for TSSB>40 ms
    Upon exceeding LRRC,known,max the UE may stop the active TCI state switching procedure and FFS: declare beam failure
MAC-CE based:
  LMAC,known,max =[2] for TSSB≤40 ms, LMAC,known,max =[1] for TSSB>40 ms
    Upon exceeding LMAC,known,max the UE may stop the active TCI state switching procedure and FFS: stay in the old state
  Confirm RAN4#92-bis agreement on extending THARQ for MAC-CE based switching
    The exact wording is TBD

## Slide 33: Active TCI State Switching: Unknown State Requirements
RRC-based:
  L1RRC,unknown,max =[2] for TCSI-RS/SSB ≤40 ms, L1MAC,unknown,max = [1] for TCSI-RS/SSB>40 ms
  L2RRC,unknown,max =[2] for TSSB ≤40 ms, L2MAC,unknown,max = [1] for TSSB>40 ms
  Upon exceeding L1RRC,unknown,max or L2RRC,unknown,max the UE may abandon the active TCI state switching procedure and FFS: declare beam failure
MAC-CE based switching:
  L1MAC,unknown,max = [2] for TCSI-RS/SSB≤40 ms, L1MAC,unknown,max = [1] for TCSI-RS/SSB>40 ms
  L2MAC,unknown,max =[2] for TSSB≤40 ms, L2MAC,unknown,max = [1] for TSSB>40 ms
  Upon exceeding L1MAC,known,max or L2MAC,known,max the UE may stop the active TCI state switching procedure and FFS: stay in the old state
  Confirm RAN4#92-bis agreement on extending THARQ for MAC-CE based switching
    The exact wording is TBD

## Slide 34: PSCell Addition: Known Cell Definition
The time between the reception of the PSCell configuration command and measurement/report is
  Option 1: extended from 5 seconds to [8] seconds
  Option 2: not extended

## Slide 35: PSCell Addition Delay
L1max=3 for SMTC periodicity >40 ms, L1max=5 for SMTC periodicity ≤40 ms
L2max=2 for SMTC periodicity >40 ms, L2max=3 for SMTC periodicity ≤40 ms
Upon exceeding L1max or L2max or upon T304 timer, whichever comes first, the UE shall stop the PSCell addition procedure

## Slide 36: UL LBT and Measurement Reporting
Background: Agreed in RAN4#92-bis:
  Event-triggered reporting:
    UE measurement reporting delay is extended to account for UL LBT failures resulting in UE being not being able to transmit, provided the UL resources are configured
    This applies for all UL channel access categories other than the channel access category 1
      Existing reporting requirements apply for the reporting based on the UL channel access category 1
Event triggered reporting:
  FFS: UE shall abandon the measurement report when the extension UL, i.e., the time period from the time of the first reporting attempt failed due to UL CCA failure until the time of the successful reporting attempt, exceeds UL,max
  The extension is
    Option 1: determined by RAN1/RAN2 specifications
    Option 2: a pre-defined value
  measurement reporting delay can be further extended to account for DL LBT failures, in the same way as in the measurement period requirements
Periodic measurement reporting:
  FFS: UE measurement reporting delay is extended by  UL ≤  UL,max where  UL,max is limited by Treport (Treport is the length of one measurement report period), or until the new measurement is available
    Option 1: UL,max is determined by RAN1/RAN2 specifications
    Option 2: UL,max is a pre-defined value
  No extension for UL channel access category 1
Event-triggered periodic reporting:
  UL impact is accounted for based on the same principle as for periodic reporting
  For the first report, the measurement reporting delay is further extended to account for DL LBT failures, in the same way as for event-triggered reporting

## Slide 37: UL LBT and Measurement Reporting: Specification Impact
The measurement reporting requirements are to be captured in:
  TS 38.133
    DL and UL impact: sections 9.2A.4 (intra-frequency), 9.3A.5 (inter-frequency)
    UL impact only: sections 9.4.2.4 (inter-RAT NR-E-UTRA FDD), 9.4.3.4 (inter-RAT NR-E-UTRA TDD)
  TS 36.133
    DL impact only: section 8.1.2.4.21 (E-UTRA FDD -NR)
    DL and UL (for reporting on NR PSCell only) impact: 8.17.4A.1.3 (NR measurements in EN-DC, for reporting on NR PSCell only)

## Slide 38: Measurement Reporting Criteria
FFS: for UE capable of and configured (if such capability exists) with wideband operation with CCA, 1 report for RSSI and channel occupancy measurements is capable of minimum 1 RSSI measurement and 1 channel occupancy measurement per subband
for UE not capable of or not configured (if such capability exists) with wideband operation with CCA, 1 report for RSSI and channel occupancy measurements is capable of minimum 1 RSSI measurement and 1 channel occupancy measurement per carrier frequency with CCA

## Slide 39: UE Measurement Capability
FFS: impact of multiple candidate SSB index positions on UE measurement capability related to number of cells and SSBs