## Slide 1: Way forward on one shot timing adjustment NR RRM requirements
ZTE, Ericsson
3GPP TSG-RAN WG4 Meeting #93
Reno, US, 18 - 22 November, 2019
R4-1915790

## Slide 2: Background
When the magnitude of the DL reference time differece deltaT exceeds threshold H, the UE shall adjust its transmission timing in one adjustment
  deltaT = |T1-T2|
    T1 is the DL reception reference time of the former beam at the UE just before UE Rx beam switch
    T2 is the DL reception reference time of the new beam at the UE just after the UE Rx beam switch
  One shot UE transmit timing adjustment step is 2*(T1-T2)

## Slide 3: Consideration at gNB (for information)
Available tolerance of uplink transmission timing error at gNB reception
  The total uplink timing error at gNB reception will furhter increase (compared to the values in the table) due to timing drift as DL reference timing estimation may be conducted long time ago
SCS of SSB signals (KHz) | SCS of uplink signals (KHz) | Timing errors at BS reception (Tc) | UL CP length(Tc) | Existing timing error in percentage of UL CP length at BS reception(%)
15 | 15 | 1536 | 9216 | 17
 | 30 | 1152 | 4608 | 25
 | 60 | 896 | 2304 | 39
30 | 15 | 1280 | 9216 | 14
 | 30 | 1024 | 4608 | 22
 | 60 | 704 | 2304 | 31
120 | 60 | 480 | 2304 | 21
 | 120 | 320 | 1152 | 28
240 | 60 | 448 | 2304 | 19
 | 120 | 288 | 1152 | 25

## Slide 4: Consideration at gNB
Allowed uplink transmission timing error at gNB reception
  The assumption to develop one shot timing adjustments requirements is that the total uplink timing error at gNB reception shall not exceed X% of UL CP:
    Option 1 = X is 50
    Other value of X is not precluded.

## Slide 5: Consideration at UE
Accuracy of one shot timing adjustment (Te1)
  Option 1: The baseline is the same as initial timing transmission timing error Te.
    Additional margin for Te1 is TBD
      Potential source of timing errors
        DL reference timing estimation error
        Timing drift due to DL reference timing estimation may be conducted long time ago during Rx beam sweeping
  Option 2: No accuracy requirements for one shot timing adjustment.

## Slide 6: Consideration at UE
The threshold H for applying one-shot adjustment
  Candidate of threshold H
    Option 1: [5%] UL CP
    Option 2: [10%] UL CP
    Option 3: [15%] UL CP
    Option 4: [20%] UL CP
    Option 5: [25%] UL CP
    Other options are not precluded

## Slide 7: Way forward
Option 1: Finalize one shot timing adjustment requirements in Rel-15 under condition
    Threshold H: TBD% UL CP
    Accuracy after one shot timing adjustment: TBD
Option 2: Remove existing one shot timing adjustment requirements in Rel-15
    It may be further considered in Rel-16

## Slide 8: Interruption
Interruption requirement due to one shot timing adjustment
  Option 1: an interruption of up to one symbol is allowed due to one shot timing adjustment. (Huawei)
  Option 2: No interruption requirement due to one shot timing adjustment is specified. (Ericsson, ZTE, MediaTek)
  Agreements: Option 2