## Slide 1: Way forward on PMI reporting requirements for Tx ports larger than 8 and up to 32
Ericsson, Samsung
3GPP TSG-RAN4 Meeting #93
USA, Reno, November 18 - 22, 2019
Agenda item: 9.18.1.2
R4-1915858
Document for: Approval

## Slide 2: Timeline of previous agreements
#92
  WF: R4-1910017
#92bis
  WF: R4-1912834
  simulation assumptions: R4-1912811

## Slide 3: PMI tests for single panel type I requirements
Wideband PMI requirements
  32Tx ports
subband PMI requirements for 16 Tx ports
  If subband PMI test for 16 Tx ports will be introduced, only 32 Tx ports will be covered in wideband PMI test.
  If subband PMI test for 16 Tx ports will not be introduced, both 16 and 32 Tx ports will be covered in wideband PMI test.
  Decide whether to define subband requirements based on the simulation results.
  Companies are encouraged to run simulation for the following 4 cases. Consider the following priority if no time to run simulation for all 4 cases.
    Priority for simulation: Follow subband PMI, Random subband PMI > Follow wideband PMI, Random wideband PMI
    For subband/wideband gain comparison, run all tests with channel model TDLC300-5

## Slide 4: Initial Single panel type I subband PMI simulation assumptions:
Propagation condition: TDLC300-5
Correlation matrix: XP high
Number of Tx ports: 16
Duplex mode: FDD
Rx antennas: 2
Subband size: 8
See detailed simulation assumptions for other parameters

## Slide 5: Further Single panel type I agreements
Use rank 2 for all the PMI test
First subcarrier index and first symbol location for NZP CSI-RS
  Option 1
    (k0, k1, k2, k3) = (2, 4, 6, 8), l0 = 5 for 16 Tx ports, and (k0, k1, k2, k3) = (2, 4, 6, 8), (l0, l1) = (5, 7) for 32 Tx ports.
  Option 2
    (k0, k1, k2, k3) = (2, 4, 6, 8), l0 = 5 for 16 Tx ports, and (k0, k1, k2, k3) = (2, 4, 6, 8), (l0, l1) = (5, 12) for 32 Tx ports.
  Down-select to one option in the next meeting.

## Slide 6: Type II codebook requirements
Encourage companies to provide inputs on the following test parameters in the next meeting:
  Number of Tx ports:
    (N1, N2), (O1, O2)
  L (numberOfBeams)
  Npsk (phaseAlphabetSize)
  subbandAmplitude
  Beam steering model
  Test metric
  MCS and rank
  MIMO correlation
  Channel model

## Slide 7: Type II Codebook simulation parameters: For information
Codebook construction
  16 Tx ports (N1, N2) = (4, 2) and (O1, O2) = (4,4)
  32 Tx ports (N1, N2) = (4,4) and (O1, O2) = (4, 4)
    L (numberOfBeams): 2
    Npsk (phaseAlphabetSize) : beam combining coefficient (phase) set size, Npsk =4
    subbandAmplitude: 'true' or 'false’
Beam steering model
  beam steering model with dual-cluster beams as specified in B.2.3B.4A of TS 36.101
    Relative power ratio among two beams is fixed as 1 (p =1)

## Slide 8: Type II Codebook simulation parameters: For information cont’d
Test metric:
  Option 1: Relative throughput ratio between following PMI with Type II codebook and following PMI with Type I codebook
  Option 2: Relative throughput ratio between following PMI and random PMI
MCS and rank:
  Option 1: MCS 13, Rank 2
  Option 2: MCS 20, Rank 2
MIMO correlation:
  XP High
Channel model:
  TDLA30-5