## Slide 1
3GPP TSG-RAN WG4 Meeting #93 R4-1915869
Reno, USA, 18th – 22nd Nov, 2019
Agenda Item: 9.17.2.2
WF on UE demodulation for NR HST
CMCC

## Slide 2: Background
The following WFs were approved:
  R4-1910050 WF on demodulation for UE NR HST, RAN4#92
  R4-1912808 Way forward on NR HST UE demodulation, RAN4#92BIS

## Slide 3: HST-SFN
Maximum Doppler frequency
  For TDD 30 KHz SCS, 500km/h
    Option 1: 1500Hz
    Option 2: 1667Hz
  For FDD 15 KHz SCS, 500km/h
    Option 1: 712Hz
    Option 2: 875Hz
    Option 3: 851Hz
  FFS on whether +-0.1ppm UE DL frequency error or lower value should be used when determine the maximum Doppler frequency
  Further discuss on the estimation error methodology and other errors

## Slide 4: HST-SFN
MCS (for Rank 2)
  Option 1: MCS4
  Option 2: MCS13
  Option 3: MCS17
  MCS should be decided based on whether the maximum throughput can be achieved

## Slide 5: HST single tap
Maximum Doppler frequency
  For 15KHz SCS, 500km/h
    Option 1: 1250Hz
    Option 2: 875Hz
MCS ( for Rank 1)
  Option 1: MCS 17
  Option 2: MCS 13
  MCS should be decided based on whether the maximum throughput can be achieved

## Slide 6: HST single tap
Single tap requirements definition
  Option A: Define requirements based on worst case and UE performs multi-shot TRS-based time/freq tracking
  Option B: Define requirements under assumption UE is aware on HST single tap conditions and can adjust time/freq tracking algorithms
    Further study how UE can become aware on conditions
      Option 1: UE detects the conditions
      Option 2: Rely on agreed NR HST RRM enhancement network assistance signaling
      Option 3: Additional network assistance is provided
Further study UE demodulation performance under HST single tap conditions for the case of single-shot and multi-shot TRS-based tracking

## Slide 7: Multi-path fading channel
Maximum Doppler frequency
  FDD 15KHz SCS: 600 Hz
  TDD 30 KHz SCS: 1200 Hz
DMRS configuration
  DMRS 1+1+1
Channel model:
  TDL-C 300ns

## Slide 8: Multi-path fading channel
MCS
  Option 1: MCS4
  Option 2: MCS13
  Option 3: MCS17
  Note: MCS should be discussed together with rank assumption
Rank
  Option 1: Rank = 1
  Option 2: Rank = 2
  Note: rank1 is mandatory, rank2 is mandatory with capability signalling

## Slide 9: Transmission scheme
DPS transmission scheme 1a is feasible in HST scenario for both UE and BS. Whether to define new requirements and tests for DPS transmission scheme 1a are FFS.
DPS transmission scheme 1b is feasible in HST scenario for both UE and BS. Whether to define new requirements and tests for DPS transmission scheme 1b are FFS.
Further study feasibility and performance benefits of transmission scheme 2 when its details are finalized by RAN1
Transmission scheme 3
  Further check whether Rel-16 eMIMO WI can support transmission scheme 3
    If it is supported in Rel-16 eMIMO WI, further study feasibility and performance benefits of transmission scheme 3 in Rel-16 HST WI when its details are finalized by RAN1
    If it is not supported in Rel-16, no requirements are defined in Rel-16 HST WI. Companies can bring analysis on the performance benefits and feasibility
Note: Details of transmission scheme 1a, 1b, 2 and 3 can be found in Annex

## Slide 10: Signaling
UE capability signaling
  Introduce per-UE capability to support enhanced demodulation performance for HST-SFN joint transmission scheme with velocity up to 500km/h.
  No need to introduce UE capability for HST-SFN transmission scheme 1a and 1b.
NW assistance signaling
  Introduce per-cell network assistance signalling to inform UE on HST-SFN deployment with joint transmission (JT) scheme

## Slide 11: Target speed
For HST single tap, introduce requirements for target speed of 500km/h
For HST-SFN,
  Introduce requirements for target speed of 500km/h
  FFS on whether to introduce requirements for target speed of 350km/h.
    Further discuss on the maximum Doppler, MCS and other parameters for 350km/h

## Slide 12: Updated simulation assumption for HST-SFN
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 4; MCS 13; MCS 17 based on 64QAM table | 
Propagation condition | HST-SFN | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds=700m, Dmin=150m | 
Rank | Rank = 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | Option 1: 712Hz Option 2: 875Hz Option 3: 851Hz | Option 1: 1500Hz Option 2: 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 13: Updated simulation assumption for HST-single tap
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
MCS | MCS 13; MCS 17 based on 64QAM table | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
Propagation condition | HST-single tap | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Ds and Dmin | Ds= 300m, Dmin=2m | 
Rank | Rank = 1 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | Option 1: 1250Hz Option 2: 972Hz | 1667Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 14: Simulation assumption for multi-path fading channel
Parameter | Value | 
 | FDD 15KHz SCS | TDD 30KHz SCS
Antenna configuration | 2×2; 2×4 | 
DMRS type | type 1 | 
Number of DMRS symbols | DMRS 1+1+1 | 
TDD pattern | 7D1S2U, S: 6D 4G 4U | 
MCS | MCS 4; MCS 13; MCS 17 based on 64QAM table | 
Propagation condition | TDL-C 300ns | 
TRS periodicity | 10ms, 2slot pattern | 
PDSCH mapping | Type A, Start symbol 2, Duration 12 | 
Rank | Rank = 1 and 2 | 
BW | 10MHz | 40MHz
Maximum Doppler shift | 600Hz | 1200Hz
Testing metric | SNR @70% of maximum throughput | 
Note: The other parameters are same as Rel-15

## Slide 15: Annex
Candidate transmission scheme to be further studied
  Transmission scheme 1 - DPS: PDSCH is only transmitted from one TRP at one time
    Transmission scheme 1a: UE only needs to track 1 TCI state (detail can be found in R4-1911003)
    Transmission scheme 1b: UE needs to track more than 1 TCI states (detail can be found in R4-1911091)
  Transmission scheme 2 - PDSCH is jointly transmitted from two or more adjacent TRPs scheduled by multi-DCI(detail can be found in R4-1911091)
  Transmission scheme 3 - Joint transmission + Distributed reference signal (detail can be found in R4-1911003)
    joint transmission + Distributed TRS
    joint transmission + Distributed DMRS