## Slide 1
3GPP TSG-RAN WG4 Meeting #93 R4-1915887
Reno, USA, 18th – 22nd Nov, 2019
Agenda Item: 8.17.1
WF on RRM for NR HST
CMCC

## Slide 2: Cell re-selection requirements
Cell re-selection requirements specified in Rel-16 LTE HST WI can be reused for NR HST
  The details are as following table:
  No enhancement applied for 2.56s DRX length for NR HST
  Capture a note in the requirements table that 2.56s requirement has not been enhanced to support high speed operation.
DRX cycle length [s] | Tdetect,NR_Intra [s] (number of DRX cycles) | Tmeasure,NR_Intra [s] (number of DRX cycles) | Tevaluate,NR_Intra [s] (number of DRX cycles)
0.32 | [2.56 x M2 (8 x M2)] | [0.32 x M3 (1 x M3)] | [0.96 x M4 (3 x M4)]
0.64 | [5.12 (8)] | [0.64 (1)] | [1.92 (3)]
1.28 | [8.96 (7)] | [1.28 (1)] | [3.84 (3)]
2.56 | [58.88 (23)] | [2.56 (1)] | [7.68 (3)]
Note 1: FFS whether to keep M2, M3, M4 |  |  | 

## Slide 3: Cell identification delay requirements for non-DRX case
Rel-15 PSS/SSS detection delay requirements, measurement delay requirements for non-DRX case are applicable to the high speed scenario
Further study SSB index acquiring delay requirements

## Slide 4: Cell identification delay requirements for DRX case
For DRX cycle ≤ 320ms
  FFS whether 3 or 5 samples shall be used for measurement period
  [5] samples shall be used for cell detection
  FFS whether 1.5x relaxation factor shall be used
For DRX cycle > 320ms
  Option 1: measurement period is enhanced from 5 samples to 3 samples
  Option 2: no enhancement
  Other option is not precluded
  FFS if requirements for all SMTC periodicities shall be enhanced

## Slide 5: Signalling
Introduce network assistance signalling to inform UE the enhanced RRM requirements apply in the cell
Introduce a per-UE capability of enhanced RRM requirements to support on high speed conditions with velocity up to 500km/h

## Slide 6: RLM
Reuse Rel-15 RLM requirements for NR HST
  FFS whether 1.5x relaxation factor shall be used

## Slide 7: Beam management
CBD based on SSB/CSI-RS
  FFS on whether Rel-15 CBD requirements based on SSB/CSI-RS can be reused for NR HST
BFD based on SSB/CSI-RS
  Rel-15 BFD requirements based on SSB/CSI-RS can be reused for NR HST
    FFS whether 1.5x relaxation factor shall be used

## Slide 8: Beam management
L1-RSRP based SSB
  FFS on whether Rel-15 requirements (measurement delay, measurement accuracy) can be reused for NR HST
L1-RSRP based on CSI-RS
  FFS on whether Rel-15 requirements (measurement delay, measurement accuracy) can be reused for NR HST

## Slide 9: Inter-RAT measurement
EUTRA-NR Inter-RAT measurement (before EN-DC)
  Cell re-selection
    Option 1: reuse the R16 NR HST cell re-selection requirements, the details are:
    Other option is not precluded
  Cell identification without DRX in connected mode
    Option 1: reuse Rel-15 NR PSS/SSS detection delay requirements, measurement delay requirements and SSB index acquiring delay
    Other option is not precluded
DRX cycle length [s] | Tdetect,NR_Intra [s] (number of DRX cycles) | Tmeasure,NR_Intra [s] (number of DRX cycles) | Tevaluate,NR_Intra [s] (number of DRX cycles)
0.32 | [2.56 x M2 (8 x M2)] | [0.32 x M3 (1 x M3)] | [0.96 x M4 (3 x M4)]
0.64 | [5.12 (8)] | [0.64 (1)] | [1.92 (3)]
1.28 | [8.96 (7)] | [1.28 (1)] | [3.84 (3)]
2.56 | [58.88 (23)] | [2.56 (1)] | [7.68 (3)]
Note 1: FFS whether to keep M2, M3, M4 |  |  | 

## Slide 10: Inter-RAT measurement
EUTRA-NR Inter-RAT measurement (before EN-DC)
  Cell identification with DRX in connected mode
    Option 1: Reduce the number of measurement samples
    Option 2: Reuse the Rel-15 NR cell identification requirements and the feasible DRX cycles can be further discussed
    Other option is not precluded

## Slide 11: Inter-RAT measurement
NR-EUTRA Inter-RAT measurement (NR SA)
  Cell re-selection
    Option 1: reuse the R16 LTE HST cell re-selection requirements, and details are:
    Other option is not precluded
DRX cycle length [s] | Tdetect,EUTRAN_Intra [s] (number of DRX cycles) | Tmeasure,EUTRAN_Intra [s] (number of DRX cycles) | Tevaluate,E-UTRAN_intra [s] (number of DRX cycles)
0.32 | 2.56 (8) | 0.32(1) | 0.96(3)
0.64 | 5.12 (8) | 0.64 (1) | 1.92 (3)
1.28 | 8.96 (7) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)

## Slide 12: Inter-RAT measurement
NR-EUTRA Inter-RAT measurement (NR SA)
  Cell identification without DRX in connected mode
    Option 1:
      The Rel-15 requirements TIdentify,E-UTRAN with Tinter1 of 60ms can be reused for high speed scenario.
      FFS whether the current requirements TIdentify,E-UTRAN with Tinter1 of 30ms can be reused for high speed scenario
    Other options are not precluded

## Slide 13: Inter-RAT measurement
NR-EUTRA Inter-RAT measurement (NR SA)
  Cell identification with DRX in connected mode
    Option 1
    Option 2
    Other options are not precluded
DRX cycle length (s) | TIdentify, E-UTRAN (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.2.2 apply | Non-DRX requirements in clause 9.4.2.2 apply
0.16 < DRX-cycle<1.28 | Note1, 2 (10) | Note1, 2 (10)
1.28 | Note1, 2 (8) | Note1, 2 (8)
1.28< DRX-cycle ≤10.24 | Note1, 2 (20) | Note1, 2 (20)
NOTE 1: The time depends on the DRX cycle length. NOTE 2: Intra-frequency deployed is assumed for LTE HST and intra-frequency without gap is assumed for NR HST, So CSSFinterRAT = 1. |  | 
DRX cycle length (s) | TIdentify, E-UTRAN TDD (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.3.2 apply | Non-DRX requirements in clause 9.4.3.2 apply
0.256 | 3.84*CSSFinterRAT (15*CSSFinterRAT) | 3.84*CSSFinterRAT (15*CSSFinterRAT)
0.32 | 4.8*CSSFinterRAT (15*CSSFinterRAT) | 4.8*CSSFinterRAT (15*CSSFinterRAT)
0.32< DRX-cycle ≤10.24 | Note1 (20*CSSFinterRAT) | Note1 (20*CSSFinterRAT)
NOTE 1: The time depends on the DRX cycle length. |  | 

## Slide 14: Feasible configuration on SSB/CSI-RS periodicity for HST scenario
Feasible SSB periodicity for HST
  Option 1 : <= 40ms
  Option 2 : <= 160ms
  Other option is not precluded
Feasible CSI-RS periodicity for HST
  Option 1 : <= 40ms
  Option 2 : <= 160ms
  Other option is not precluded

## Slide 15: SS-SINR
Option 1: SINR accuracy requirement is not applicable to HST scenario
Option 2: SS-SINR measurement is not supported in HST scenario
Option 3: identify the SNR upper bound below which the Rel-15 SS-SINR measurement requirements are reused. For the SNR larger than the upper bound, FFS whether to introduce new requirements or do not specify requirements