## Slide 1: 3GPP TSG-RAN WG4 Meeting #93 Reno, USA, 18th – 22th November 2019
Huawei, HiSilicon
Way forward on RRM requirements of R16 enhancement for NB-IoT
R4-1915890

## Slide 2: Preconfigured UL resource
When TA is obtained in RRC_IDLE mode, the values of M and N are derived as follows:
    Normal coverage
      min(800, NxDRX cycle)
    Enhanced coverage
      min(1600, NxDRX cycle)
    Where N is the relaxation factor N given by Table 4.6.2.1A-1 and Table 4.6.2.1A-1 for normal and enhanced coverage respectively.
UE should make the first and second measurements available within this time range
When UE receives a TA update through PUR ACK DCI in RRC IDLE, then the first RSRP measurement that was performed in RRC CONNECTED to obtain reference RSRP measurement should be discarded and replaced with the most recent version of the second RSRP measurement (i.e. the measurement used for TA validation), i.e., RSRP1 := RSRP2.

## Slide 3: Multi carrier operation non-anchor RRM
UE is allowed to combine the non-anchor NRSRP samples with anchor NRSRP samples
  The anchor NRSRP can be obtained by applying the corresponding power offset signaled by the network to the non-anchor NRSRP.
  FFS for conditions when UE can combine the non-anchor and anchor NRSRP samples
Any filtered results, either from anchor or non-anchor carrier, can trigger neighbor cell measurement and/or relaxed monitoring abortion.

## Slide 4: NRSRP measurement in non-sparse PO case
FFS the feasibility of NRSRP measurements in non-sparse PO case (nB<T/2)
  Option 1: disallow RRM measurements in non-anchor carrier.
  Option 2: NRSRP measurements are allowed but with no requirements
  Option 3: NRSRP measurements are allowed under some cases/conditions which are FFS.
  Other options are not excluded.