## Slide 1: WF on Number of bands and CCs to be considered in Rel-16 NR-U WI
Ericsson
R4-1915977
3GPP TSG-RAN WG4 #93
Reno, USA, 18th Nov. – 22nd Nov. 2019

## Slide 2: Proposal: Number of bands and CCs
  RAN4 to focus on the following in Rel-16 work:
  Any future band combination consisting of more than two bands or more than 5 NR-U CCs can be introduced later but will be release independent from Rel-16.
  Maximum 400MHz aggregated BW is considered in DL for NR-U band
  Maximum 100MHz UL CBW is considered for NR-U band
Scenario A1 | PCell in NR + up to 5 DL SCells in NR-U PCell in NR + up to 5 DL SCells in NR-U + 1 UL SCell in NR-U
Scenario B | PCell in LTE + PSCell in NR-U + up to 4 DL SCells in NR-U PCell in LTE + PSCell in NR + up to 5 DL SCells in NR-U
Scenario C | PCell in NR-U + up to 4 DL Scells in NR-U
Note 1: PCell and PSCell have both DL and UL Note 2: Both contiguous and non-contiguous DL NR-U SCells are allowed | 

## Slide 3: How to handle band combinations related to NR-U?
Ericsson to collect band combination proposals prior to RAN plenary
  Interersted companies are requested to send band combination proposals on RAN4 reflector
  Deadline for providing band combination proposals by Friday, 29 November 2019 23.59 UTC
    RAN plenary tdoc deadline: Friday 29 November 2019
    RAN plenary submissiond deadline: Monday 2 December 2019
The band combinations proposed for Rel-16 NR-U WI will be included in NR-U WID and to be approved in December RAN plenary

## Slide 4: Conclusion of the Rel-16 WI
If requirements related to at least one band combination is completed, then Rel-16 WI can be considered completed.
All remianing combinations will be worked on after the completion of this WI, however will be considered release independent from Rel-16.
  How to handle the remaining band combinations after Rel-16 WI is FFS.