## Slide 1: WF on FR2 inter-band DL CA
Nokia, …
R4-1916024
3GPP TSG-RAN WG4 Meeting #93
Reno, NV, USA, 18-22 Nov 2019
Agenda: 9.14.7

## Slide 2: Background
In RAN4#93, the following aspects have been discussed:
The feasibility of existing 8 us time difference requirement (MRTD) of the received symbols and how to avoid simultaneous Tx & Rx in FR2 inter-band DL CA scenarios
whether UE is capable for forming beams towards the same directions and different directions for 28 GHz + 39 GHz simultaneously
whether UE is capable for forming beams towards the same directions and different directions for 28 GHz + 28 GHz simultaneously
Whether single AoA or two AoAs shall be adopted for UE RF test.
Whether power imbalance among bands shall be assumed in core requirement and/or conformance test requirement.
Whether co-located or non-co-located deployment should be assumed.
Relaxation framework and factors in EIS spherical coverage requirement.

## Slide 3: WF on beam management
UE is assumed to be feasible to have independent beam management for the bands that are part of supported band configuration in inter-band CA for 28 GHz + 39 GHz combinations.
  “28GHz” stands for a band group includes n257, n258, n261
  “39GHz” stands for a band group includes n259, n260
Beam management for the bands that are part of supported band configuration in inter-band CA for 28 GHz + 28 GHz or 39 GHz + 39 GHz combinations.
  Alt 1: UE is assumed to have common beam management
  Alt 2: UE is assumed to have independent beam management

## Slide 4: WF on EIS spherical coverage
Spherical coverage requirements for inter-band CA are tested from single AoA for Rel-16 if the following testability solution can be provided.
  Testability SI will study the TE capability of transmitting 28 GHz + 39 GHz, 28 GHz + 28 GHz, or 39 GHz + 39GHz from same direction simultaneously.
  PSD condition among bands.
    PSD difference up to TBD dB between 28GHz and 39GHz shall be considered in the conformance test configuration and [equal] PSD among 28+28 and 39+39 band groups
    Confirm PSD condition for each scenario in RAN4#94.
Defining EIS spherical coverage requirement for inter-band CA.
  The UE shall meet the EIS spherical coverage requirement simultaneously among bands, the common EIS spherical coverage range between the two bands shall be 50% for power class 3 UE.
  Rel-15 EIS spherical coverage requirement will be taken as baseline assuming that the relaxation for 50%-tile point for power class 3 UE is introduced. The relaxation framework and value are FFS. Relaxation value cannot be 0.

## Slide 5: WF on peak EIS
The UE shall meet the Peak EIS requirements per band for FR2 DL CA, and they are not required based on common coverage range between two bands; The relaxation framework and values are FFS

## Slide 6: WF on MRTD
There shall be no change in BS TAE requirement.
In RRM session in RAN4#94, discuss if MRTD can be reduced or not.
  Alt.1: Max propagation delay difference is 1 us, and MRTD can be revised to 4 us
  Alt.2: No change in MRTD, i.e., 8us.
  Alt.3: Other values not precluded.
For UE not supporting simultaneous Tx/Rx for inter-band CA, a solution to avoid simultaneous Tx & Rx in FR2 DL CA scenarios is needed; potential alternatives are:
  Alt. 1: Assume all CCs in FR2 inter-band CA combinations have the same UL/DL TDD configuration and reflect the worst case alignment as an interruption requirement; further specification details can be discussed as part of the Rel-16 RRM work
  Alt. 2: It is UE implementation issue to discard DL symbols that can not be processed before UL; the specification impact is FFS and can be discussed as part of the Rel-16 RRM work
  Alt. 3: Other solutions are not precluded