## Slide 1: WF on UE RF requirements for adding channel BW to band n1
Ericsson, Skyworks Solutions Inc., Qualcomm, Huawei
3GPP TSG-RAN WG4 Meeting #93 R4-1916056
Reno, USA, November 18-22 2019

## Slide 2: Background
Contributions and discussion on:
  REFSENS values [1], [2]
  A-MPR results [2], [3], [4], [5].

## Slide 3: REFSENS values: Agreement
Following values are agreed:
Operating band / SCS / Channel bandwidth / Duplex mode |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz | Duplex Mode
n1 | 15 |  |  |  |  |  |  | 1281 |  |  |  |  |  | FDD
 | 30 |  |  |  |  |  |  | 641 |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  | 301 |  |  |  |  |  | 
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode
n1 | 15 |  |  |  |  |  |  | -90.6 |  |  |  |  |  | FDD
 | 30 |  |  |  |  |  |  | -90.7 |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  | -90.9 |  |  |  |  |  | 

## Slide 4: A-MPR areas - B33-34 protection
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
25 MHz | 1932.5≤ FC ≤ 1967.5 | [ ≥0 ] | [ ≥9.72MHz ] | TBD
 |  | [ ≥18.72 ] | [ <1.08MHz ] | TBD
30 MHz | 1935 ≤ FC ≤ 1965 | ≥0 | ≥13.5MHz | A3
 |  | ≥21.6 | <1.08MHz | A5
40 MHz | 1940 ≤ FC ≤ 1960 | ≥0, <2.88 | >0 | A2
 |  | ≥2.88, <17.1 | ≥max (0, 12*SCS*RBend - 3.6) | A3
 |  | ≥17.1, <27.36 | ≥13.5 | A4
 |  | ≥27.36, <34.56 | ≥13.5 | A2
 |  | ≥27.36, <34.56 | <1.08 | A5
 |  | ≥34.56 | >0 | A1

## Slide 5: A-MPR areas - B39-34 protection
Channel Bandwidth, MHz | Carrier Center Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
25 MHz | 1932.5≤ FC ≤ 1967.5 | [ ≥0 ] | [ ≥9.72 ] | TBD
 |  | [ ≥18.72 ] | [ <1.08 ] | TBD
 |  | [ ≤3.96 ] | [ <1.08 ] | TBD
30 MHz | 1935 ≤ FC ≤ 1965 | ≥0, <2.7 | >0 | A1
 |  | ≥2.7, <6.48 | >0 | A5
 |  | ≥6.48, <14.4 | ≥max (0, 12*SCS*RBend – 3.6) | A3
 |  | ≥14.4, <21.6 | ≥10.8 | A4
 |  | ≥21.6 | ≥10.8 | A2
 |  | ≥21.6 | <1.08 | A5
40 MHz | 1940 ≤ FC ≤ 1960 | ≥0, <4.5 | >0 | A1
 |  | ≥4.5, <10.44 | <1.08 | A5
 |  | ≥4.5, <18 | ≥max (0, 12*SCS*RBend - 3.6) | A4
 |  | ≥18, <34.56 | ≥14.4 | A2
 |  | ≥27.36, <34.56 | <1.08 | A5
 |  | ≥34.56 | >0 | A1

## Slide 6: Reference
R4-1913153, n1 REFSENS, Qualcomm
R4-1915429,Experimental measurements for n1 40MHz REFSENS and n34 protection, Skyworks
R4-1913150, n1 Wide BW AMPR, Qualcomm
R4-1914393, Band n1 Wider CBW, UE A-MPR simulation results, Ericsson
R4-1914588, A-MPR simulation results for n1 30 MHz, Huawei