## Slide 1: WF on UE RF requirements for adding channel BW to band n38
Ericsson, Qualcomm
3GPP TSG-RAN WG4 Meeting #93 R4-1916070
Reno, USA, November 18-22 2019

## Slide 2: Background
Contributions and discussion on:
  REFSENS values [1]
  A-MPR simulation results [2], [3].

## Slide 3: REFSENS values: agreement
Following values were agreed (RAN4#92b)
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode
n38 | 15 | -100.0 | -96.8 | -95.0 | -93.8 | -92.7 | -91.9 |  |  |  |  |  |  | TDD
 | 30 |  | -97.1 | -95.1 | -94.0 | -92.8 | -92.0 |  |  |  |  |  |  | 
 | 60 |  | -97.5 | -95.4 | -94.2 | -93.0 | -92.1 |  |  |  |  |  |  | 
Operating band / SCS / Channel bandwidth / Duplex mode |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Operating Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 80 MHz | 90 MHz | 100 MHz | Duplex Mode
n38 | 15 | 25 | 50 | 75 | 100 | 128 | 160 |  |  |  |  |  |  | TDD
 | 30 |  | 24 | 36 | 50 | 64 | 75 |  |  |  |  |  |  | 
 | 60 |  | 10 | 18 | 24 | 30 | 36 |  |  |  |  |  |  | 

## Slide 4: A-MPR results
Channel Bandwidth, MHz | Carrier Frequency, Fc, MHz | Regions |  | A-MPR
 |  | RBend*12*SCS MHz | LCRB*12*SCS MHz | 
25 MHz | 2582.5≤ FC ≤ 2602.5 | <18.0 | ≥max (0, 12*SCS*RBend – 3.6) | A1
 |  | ≥18.0 | <7.2 | A1
 |  | ≥18.0 | ≥7.2 | A2
30 MHz | 2585 ≤ FC ≤ 2600 | <21.6 | ≥max (0, 12*SCS*RBend – 3.6) | A1
 |  | ≥21.6 | <12.6 | A1
 |  | ≥21.6 | ≥12.6 | A2
Modulation/Waveform | A1 | A2
 | Outer/Inner | Outer/Inner
DFT-s-OFDM PI/2 BPSK | [<3] | [<4]
DFT-s-OFDM QPSK | [<3] | [<4]
DFT-s-OFDM 16 QAM | [<3] | [<4]
DFT-s-OFDM 64 QAM | [<3] | [<4]
DFT-s-OFDM 256 QAM | [<3] | [<4]
CP-OFDM QPSK | [<5] | [<6]
CP-OFDM 16 QAM | [<5] | [<6]
CP-OFDM 64 QAM | [<5] | [<6]
CP-OFDM 256 QAM | [<5] | [<6]

## Slide 5: Reference
R4-1911820, Band n38 - wider CBW – UE RF requirements, Ericsson
R4-1913149, n38 wide BW AMPR, Qualcomm
R4-1914395, Band n38 – Adding wider CBW – UE RF requirements –A-MPR simulation, Ericsson