## Slide 1: WF on gNB requirements for NR Positioning
Intel, ….
R4-1913464
3GPP TSG-RAN WG4 Meeting #93 Reno, USA, 18th – 22nd Nov, 2019

## Slide 2: Background
In RAN4#92b, RAN4 agreed on gNB measurement requirements
  Further discuss whether and how to define gNB measurement requirements
  Open questions
    Necessity of requirements
    Applicability to different BS types
    Requirements types (e.g. UL RTOA, UL SRS-RSRP, gNB Rx-Tx time difference, AoA and ZoA).

## Slide 3: NW synchronization error for OTDOA
RAN4 can further discuss the feasibility of two alternatives to resolve the impacts due to the imperfect cell phase synchronization on the positioning performance (e.g. OTDOA).
  Alt.1: Introduce new requirements of cell-phase synchronization error for networks or
  Alt2: Rely on additional signaling of either transmission time difference error (i.e. offset in transmission time among cells) or transmission time synchronization accuracy

## Slide 4: gNB measurement reporting
UL RTOA reporting granularity is determined by equation where is the CBW in MHz selected from the set [5, 10, 20, 25, 40, 50, 80, 100, 200, 400] MHz and closest to the configured bandwidth of UL SRS/PRS transmission.
The following granularity is used for AoA reporting . Azimuth and Zenith AoAs are reported using 11 and 10 bits respectively
UL SRS (PRS) RSRP reporting granularity is set to 1dB. Range of values and mapping for UL SRS (PRS) RSRP reporting is TBD.