## Slide 1: MIMO layer adaptation
2019/11/05

## Slide 2: overview
Motivation
  For evaluation on power consumption of MIMO layer adaption with different transition time
Simulation methodology and assumption
  UE power modeling
  Traffic modeling and DRX configuration
  General assumption
Simulation results
  Observation: For FTP3 with different MIMO layer adaption time, from 5slots to 2slots, 2.86% and 0.95% could be got for deep sleep mode and light sleep mode respectively.

## Slide 3: Motivation
For evaluation on power consumption of MIMO layer adaption with different transition time
  Option1: with 5slot transition time
  Option2: with 2slot transition time
Observation: whether option2 with 2slots transition time could get performance gain comparing with 5slots transition time.

## Slide 4: Simulation methodology and assumptions(1/5)
UE power modeling
Traffic modeling and DRX configuration
General assumption
UE procedure for evaluation

## Slide 5: Simulation methodology and assumptions(2/5)
UE power modeling
Power State | Characteristics | Relative Power
Deep Sleep | Time interval for the sleep should be larger than the total transition time entering and leaving this state. Accurate timing may not be maintained. | 1 (Optional: 0.5)
Light Sleep | Time interval for the sleep should be larger than the total transition time entering and leaving this state. | 20
Micro sleep | Immediate transition is assumed for power saving study purpose from or to a non-sleep state | 45
PDCCH-only | No PDSCH and same-slot scheduling; this includes time for PDCCH decoding and any micro-sleep within the slot. | 100
SSB or CSI-RS proc. | SSB can be used for fine time-frequency sync. and RSRP measurement of the serving/camping cell. TRS is the considered CSI-RS for sync. FFS the power scaling for processing other configurations of CSI-RS. | 100
PDCCH + PDSCH | PDCCH + PDSCH. ACK/NACK in long PUCCH is modeled by UL power state. | 300

## Slide 6: Simulation methodology and assumptions(3/5)
UE power modeling
Sleep type | Additional transition energy: (Relative power x ms) | Total transition time
Deep sleep | 450 | 20 ms
Light sleep | 100 | 6 ms
Micro sleep | 0 | 0 ms*
* Immediate transition is assumed for power saving study purpose from or to a non-sleep state |  | 
Antenna scaling (DL) | 2Rx power is 0.7x 4Rx power for FR1 1Rx power is 0.7x 2Rx power for FR2 | Assume same number of antenna elements per Rx chain
BWP transition power consumption:
For evaluation, when BWP transition duration is one slot or longer, the slot-average power level is 50 power units

## Slide 7: Simulation methodology and assumptions(4/5)
Traffic modeling and DRX configuration
 | FTP traffic
Model | FTP model 3
Packet size | 0.5 Mbytes
Mean inter-arrival time | 200 ms
DRX setting | Period = 160 ms Inactivity timer = 100 ms
MAC-CE | Enable MAC-CE when data transmission is finished

## Slide 8: Simulation methodology and assumptions(5/5)
General assumption
Assumptions | 
Scenario | ITU UMi
Channel tracking time and CSI measurement | based on CRS-RS, CSI-RS period 10ms
TDD configuration | DSUUD, SCS=30KHz
Bandwidth | 100MHz
UL transmission | Disable, UL slot is assumed as micro-sleep and ideal feedback for ACK, CSI.
Transmission rate | Transmission rate is based on DU scenario SE with 256 transmission antenna, gNB: (M,N,P,Mg,Ng; Mp,Np) = (16,8,2,1,1;2,8).10UE is dropped within one TRP.
UE antenna configuration | 4 MIMO layer for PDSCH+PDCCH detection or PDSCH only transmission; 2 MIMO layer for PDCCH-only detection

## Slide 9: Simulation results
Sleep mode | FTP3(deep sleep) |  | FTP3(light sleep) | 
MIMO layer adaption time | 5slots | 2slots | 5slots | 2slots
Power consumption per slot(power unit/slot) | 17.702 | 17.1953 | 32.8099 | 32.4997
performance gain | 0.00% | 2.86% | 0.00% | 0.95%
Observation:
For FTP3 with different MIMO layer adaption time, from 5slots to 2slots, 2.86% and 0.95% could be got for deep sleep mode and light sleep mode respectively.