## Slide 1
3GPP TSG-RAN WG4 Meeting #93 R4-1913871
Reno, USA, 18th – 22nd Nov, 2019
Agenda Item: 9.17.1
WF on RRM for NR HST
CMCC

## Slide 2: Agreements
Cell re-selection
    the intra-frequency cell reselection requirements of NR high speed scenario are proposed to be as following:
DRX cycle length [s] | Tdetect,NR_Intra [s] (number of DRX cycles) | Tmeasure,NR_Intra [s] (number of DRX cycles) | Tevaluate,NR_Intra [s] (number of DRX cycles)
0.32 | 2.56 x M2 (8 x M2) | 0.32 x M2 (1 x M2) | 0.96 x M2 (3x M2)
0.64 | 5.12 (8) | 0.64 (1) | 1.92 (3)
1.28 | 8.96 (7) | 1.28 (1) | 3.84 (3)
2.56 | 58.88 (23) | 2.56 (1) | 7.68 (3)
Note: M2 = 1.5 if SMTC periodicity of measured intra-frequency cell > 20 ms; otherwise M2=1. |  |  | 

## Slide 3: Agreements
Cell identification delay in connected state
    For intra-frequency measurement, it is proposed to only consider the case of without measurement gap in Rel-16 NR HST WI
    For no DRX case, the current PSS/SSS detection delay requirements, measurement delay requirements and SSB index acquiring delay requirements are applicable to the high speed scenario, and all the candidate SMTC periods can be applied
    For the case of DRX cycle is configured, following two options of enhancement can be further discussed:
      Option 1: reduce the number of measurement samples
      Option 2: reuse the current cell identification requirements and the feasible DRX cycles can be further discussed, but configuration of DRX cycle is up to network.

## Slide 4: Agreements
NR inter-RAT measurement delay requirements before EN-DC
    the NR inter-RAT cell re-selection requirements before EN-DC are proposed as following:
    for NR inter-RAT measurement requirements in connected mode before EN-DC, for the case of no DRX, the current PSS/SSS detection delay requirements, measurement delay requirements and SSB index acquiring delay requirements are applicable to the high speed scenario, and all the candidate SMTC periods and all the candidate MGRP can be applied
    for NR inter-RAT measurement requirements in connected mode before EN-DC, for the case of DRX, following two options of enhancement can be further discussed:
      Option 1: reduce the number of measurement samples
      Option 2: reuse the current cell identification requirements and the feasible DRX cycles can be further discussed, but configuration of DRX cycle is up to network.
DRX cycle length [s] | Tdetect,EUTRAN_Intra [s] (number of DRX cycles) | Tmeasure,EUTRAN_Intra [s] (number of DRX cycles) | Tevaluate,E-UTRAN_intra [s] (number of DRX cycles)
0.32 | 2.56 x 1.5 (8 x 1.5) | 0.32 x 1.5 (1 x 1.5) | 0.96 x 1.5 (3 x 1.5)
0.64 | 5.12 (8) | 0.64 (1) | 1.92 (3)
1.28 | 8.96(7) | 1.28 (1) | 3.84 (3)
2.56 Note1 | 58.88 (23) | 2.56 (1) | 7.68 (3)

## Slide 5: Agreements
NR inter-RAT measurement delay requirements for SA
    the cell re-selection requirements on LTE inter-RAT measurement for SA are proposed as following:
    for LTE inter-RAT measurement requirements in SA connected mode with no DRX, the current requirements TIdentify,E-UTRAN with Tinter1 of 60ms can be reused for high speed scenario. The current requirements TIdentify,E-UTRAN with Tinter1 of 30ms need to be enhanced to support high speed scenario
    for LTE inter-RAT measurement requirements in SA connected mode with DRX, the TIdentify,E-UTRAN are proposed as following:
DRX cycle length [s] | Tdetect,EUTRAN_Intra [s] (number of DRX cycles) | Tmeasure,EUTRAN_Intra [s] (number of DRX cycles) | Tevaluate,E-UTRAN_intra [s] (number of DRX cycles)
0.32 | 2.56 (8) | 0.32(1) | 0.96(3)
0.64 | 5.12 (8) | 0.64 (1) | 1.92 (3)
1.28 | 8.96 (7) | 1.28 (1) | 3.84 (3)
2.56 Note1 | 58.88 (23) | 2.56 (1) | 7.68 (3)
DRX cycle length (s) | TIdentify, E-UTRAN (s) (DRX cycles) | 
 | Gap period = 40 ms, 20 ms | Gap period = 80 ms
≤0.16 | Non-DRX requirements in clause 9.4.2.2 apply | Non-DRX requirements in clause 9.4.2.2 apply
0.16 < DRX-cycle<1.28 | Note1 (10) | Note1 (10)
1.28 | Note1 (8) | Note1 (8)
1.28< DRX-cycle ≤10.24 | Note1 (20) | Note1 (20)
NOTE 1: The time depends on the DRX cycle length. |  | 

## Slide 6: Agreements
signaling
    RRM requirements are specified for the target velocity of 500km/h, and network assistance signaling and UE capability signaling are introduced for velocity of 500km/h