## Slide 1: Wayforward on dormancy behaviour
Mediatek inc.
3GPP TSG-RAN WG4 RAN#93
Reno, USA, 18th – 22th Nov., 2019
R4-1914120 Document for: Approval

## Slide 2: Background
  According to the RAN2 agreement, the 'dormancy' behavior implies that the UE stops monitoring PDCCH but continues other activities such as AGC and RRM measurement, CSI measurements, and beam management.
Agreement in RAN2 #106 meeting:
1 SCell dormant state like LTE euCA will not be introduced in NR.
2 ‘dormancy’ behaviour will be studied as a solution for fast return to SCell utilisation for data transfer. The 'dormancy' behaviour implies that the UE stops monitoring PDCCH but continues other activities such as CSI measurements, AGC and beam management. RAN1/4 input required on feasibility and benefit.

## Slide 3: Background
  RAN4 is requiredrequested to use the BWP framework to evaluate the switching delay of transitions between ‘dormancy’ and ‘non-dormancy’ behaviors
LS to RAN4 (R1-1909893):
ACTION: RAN1 kindly asks RAN2 to take the above information into account, and RAN4 to kindly provide information on whether the existing BWP switch delay requirements are adequate, or whether different delay requirement should be defined for the transition between ‘dormancy’ and ‘non-dormancy’ behaviour in the case BWP framework is used. RAN1 would also like to kindly remind RAN4 to provide response to R1-1905912 sent in RAN1 #96b.
Agreements in RAN1 #98Bis meeting:
For the L1 based Scell dormancy indication sent on primary cell within active time
  UE is configured with at least two BWPs for an Scell
    The explicit information field in DCI indicates switching to/from dormant BWP configured for the Scell
      FFS definition of dormant BWP
      FFS whether or not to the same BWP switching delay to the non-dormant to dormant transition delay
  Note: Rel15 behavior for case when 1BWP is configured for the Scell (i.e., no dormancy indication for that Scell)

## Slide 4: Background
  RAN4’s reply in #92Bis meeting
LS to RAN1 R4-1912830:
RAN4 only discussed change in PDCCH monitoring and CSI-RS reporting configuration when changing from dormancy behaviour to non-dormancy behaviour.
  RAN4 is still discussing if the existing latencies defined for DCI-based BWP switching are adequate for transition between ‘dormancy’ and ‘non-dormancy’ behaviour.
  The interruption time has not been discussed.

## Slide 5: Wayforward
RAN4 to discuss how to handle the delay and interruption requirements for transitions between ‘dormancy’ and ‘non-dormancy’ behaviors in different scenarios
  Whether to differentiate UE in “light sleep mode” and “deep sleep mode” during dormancy based on following factors
    Configured CSI-RS periodicity
    Other impact factors are not precluded
Figure 1: Options for power saving mode.

## Slide 6: Wayforward
The delay and interruption requirements as well as the corresponding UE capabilities of BWP framework related features, i.e., BWP switching, MIMO layer adaptation, and dormancy behavior, should be discussed as a package
  Whether same UE requirements can be applied when
    BWP, MIMO layer and SCell dormancy are changed individually in different time
    BWP, MIMO layer and SCell dormancy are changed in the same time